Colorado State Metal and Nonmetal

Mine Rescue, First Aid & Team Technician Contest

Idaho Springs, Colorado

July 12th, 13th, & 14th 2011

- MSHA requires Periodic Maintenance should be performed at least __________ on Mine Rescue Breathing Apparatus.

  - Daily

  - Weekly

  - Every 30 days

  - Quarterly

MSHA Miners Act,  BioPak 240 R Benchman manual Rev I, page 15

- In a properly working positive pressure NIOSH/MSHA approved Closed Circuit breathing apparatus the pressure inside the breathing loop/circuit is:

  - Lower than ambient

  - The same as ambient

  - The same as cylinder pressure

  - Slightly higher than ambient

BioPak 240 R Benchman Instruction Manual Rev I page 22, 25, USER Test Q # 9

- If a slight leak occurs in the breathing loop/circuit or facemask seal, the user generally will:

  - Hit the demand valve more often

  - Reduce duration

  - Increase oxygen consumption

  - All of the Above

  - None of the Above

BioPak Benchman Manual Rev I  page 22, USER test Q # 4

- Under extremely heavy work conditions, if the user inhales and collapses the diaphragm as far as it can travel, it activates the

  - By-Pass Valve

  - Demand Valve

  - Relief Valve

  - Check Valve

BioPak 240 R User Manual, Rev H, p. 17, Benchman Manual p. 15, 22

- What specifically controls the directional flow of the breathing gasses:

  - The hoses

  - The mask

  - The breathing bag or chamber

  - The CO2 scrubber/absorber

  - The check valves

BioPak 240 R USER Quiz Rev A, page 5, Q # 30, Benchman’s Quiz, Rev B, p. 5 Q # 34

- The function of the regulator is to:

  - Increase cylinder pressure in the apparatus

  - Moisture control

  - Decrease cylinder pressure in the apparatus plumbing and pneumatics

  - A & C

BioPak 240 R Benchman’s Quiz, Rev B, p. 2 Q # 14

- If you hear the Demand every time you inhale, and you are not working hard, you should:

  - Use the Emergency By-Pass Valve

  - Breathe slower

  - Turn off the oxygen cylinder

  - Check your facemask fit and adjust it for a better seal

BioPak 240 R User’s Quiz, Rev A, p. 1 Q # 4

- The approved NIOSH/MSHA and manufacturer rated duration of my Closed Circuit Breathing Apparatus is:

  - 1-Hour

  - 2-Hours

  - Variable

  - 3-Hours

  - 4-hours

BioPak 240 R User Manual Rev H, p. 18, 20 and Benchman’s Manual Rev I, p. 25

- Symptoms of breathing higher than normal levels of  CO2 may be:

  - Increased breathing rate

  - Headache, Dizziness, Light headed

  - Singing

  - Hunger

  - A & B	NO ONLY A

BioPak 240 R User’s Manual, Rev H, p. 10, 13, 18,  Benchman’s Manual Rev I, p. 9,

- If after removing my apparatus I leave the oxygen cylinder open, which valve will be wide open and  deplete the left over oxygen supplies:

  - Demand valve

  - Emergency Bypass valve

  - Relief valve

  - None of the Above

BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- When installing or filling CO2 absorption material into my apparatus  it is important to:

  - Follow the manufacturer’s instructions

  - Inspect the packaging for expiration date

  - Properly seal the apparatus from ambient air

  - Properly dry the material so it can be reused

  - All EXCEPT D

BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- When installing my pressurized oxygen cylinder in a ready to go apparatus, caution should be used to ensure:

  - Oils from my fingers and hands do not get on the valve

  - The cylinder and valve are clean

  - It is filled with the correct gas

  - It is pressurized to the correct amount

  - All the above

BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- A small leak in the breathing circuit/loop will cause the ____________ valve to open frequently.

  - Relief/Vent

  - Demand

  - Bypass

  - None of the Above

BioPak 240 R Benchman’s Manual, Rev I, p. 15, 22, BioPak 240 R User’s Quiz, Rev A, p. 1, Q # 4, BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- If Positive Pressure could be attributed to ONLY ONE component in the apparatus what would it be:

  - The spring(s)

  - The breathing chamber or breathing bag

  - Oxygen pressure

  - Bypass valve

BioPak 240 R Benchman’s Quiz, Rev B, p. 1, Q # 4, BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- Manual overuse of the __________ will significantly reduce the duration of the apparatus.

  - Relief/Vent valve

  - Purge valve

  - On/Off Valve

  - Emergency Bypass

BioPak 240 R Benchman’s Quiz, Rev B, p. 1, Q # 4, BioPak 240 R and S Users Training, BioPak 240 R and S User and Benchman’s Manuals

- The functional bump test is intended to be a measure of the accuracy of the instrument.

  - True

  - False

(page 23 iTX rev 6 manual and page 17 rev3 in the MX6 manual)

- The Industrial Scientific Corporation iTX and the iBrid gas instruments have an operating temperature range from 20 °F to 116 °F.

  - True

  - False

(page 30 in rev 6 iTX manual, and slide 26 in online features video for MX6)

- Industrial Scientific recommends that a full instrument calibration be performed using certified concentration(s) of Industrial Scientific branded calibration gas(es) _______ to ensure maximum accuracy.

  - Daily

  - Weekly

  - Monthly

  - None of the above

(page 23 iTX manual and page 17 in the MX6 manual)

- If there is an oxygen sensor installed in the instrument, it is calibrated during the zeroing operation.

  - True

  - False

(page 9 rev 6 in the iTX manual and page 18 rev 6 in the MX6 iBrid manual)

- The range for an Oxygen (O2) sensor is 0% to 25%.

  - True

  - False

(page 29 rev 6 in iTX manual and last chart in MX6 manual (range for an O2  sensor is 0% to 30%) )

- During calibration, what is the recommended flow rate for both the iTX and the iBrid?

  - 1.5 liter per minute (LPM)

  - 2.0 liter per minute (LPM)

  - 3.0 liter per minute (LPM)

  - None of the above

(page 24 in the iTX and page 19 rev 6 in the MX6 iBrid)

- Marginal calibration occurs if the (gas) sensor's full span value or span reserve is between 40% to 60% of the applied (calibration) gas value concentration.

  - True

  - False

(page 23 in iTX manual, slide 30 in the Cal training video iTX, and slide 14 in the cal training video MX6)

- Both the iTX and the iBrid gas instruments can accept zinc-ion battery types.

  - True

  - False

(page 29 in iTX, page 5 rev 3 in iBrid)

- All over-range conditions will clear automatically when the gas concentration has decreased to a level within the display range of the gas instrument in non-latching mode.

  - True

  - False

(slides 51 and 52 in the Operation training video iTX and slide 70 in the Operation training video MX6)

- Prior to entering the normal GAS READING mode during start-up, the gas instrument will display all installed sensor types.

  - True

  - False

(under 3rd paragraph on page 8 iTX (rev 6), and on slide 25 of the on-line Operations Training Video for the MX6-iBrid)

- The specific gravity of nitrogen dioxide is

  - 1.5894

  - 1.5291

  - 1.1054

  - 1.1906

Modules 2-17

- Although smoke may irritate your lungs when you inhale it, it is not normally considered to be an asphyxiant.

  - True

  - False

Modules 2-26

- Blackdamp is a mixture of carbon monoxide and air which results from a mine fire.

  - True

  - False		Whitedamp

Modules 2-26

- The smoke tube is used to show the direction and velocity of slow-moving air (below __________ feet per minute).

  - 100

  - 110

  - 120

  - 130

  - 210

Modules 3-18

- The pitot tube has a J-tube water gauge or some other differential pressure gauge for determining the velocity pressure inside the duct or tubing.

  - True

  - False		U

Modules 3-16

Bonus Question worth Zero points

A team is a unit made up of a group of individuals working towards a common goal.

- ___c____

- ___d____

- ___d____

- ___b____

- ___e____

- ___c____

- ___d____

- ___e____

- ___e____	Correction only A

- _a____

- _e____

- _e____

- _b____

- _a____

- _d____

- _b____

- _b____

- _c____

- _a____

- _b____

- _d____

- _b____

- _b____

- _b____

- _a____

- _a____

- _a____

- _b____

- _c____

- _b____