Judge’s Instructions

- Show the contestant the time clock and the check in/out board.

- Provide contestant with the blank map, written statement, and ventilation and roof control plans.  The contestant has 5 minutes to review the plans prior starting the clock and the underground portion of the contest.

- Show the contestant the Main Haulageway and which area he or she is to pre-shift.  Entries are labeled left to right facing inby.

For taking the air reading on the section, give the contestant the following information:

Width = 	20 feet

Height = 	8 feet				CORRECT LOCATIONS

Velocity =	166 fpm LOX

If the contestant travels through over knee deep water, (this endangers contestant).   The vent device must be extended in the #1 entry to vent the face.    To vent the #3 face with line curtain the check curtain must be installed.   To take a proper LOX and evaluate section air the check curtain must be installed in cross cut #2 to #3 entry at xc #3.  If contestant does not take an air reading in the proper location for the LOX; deduct for improper location.

Provide the contestant the following gas reading for the outby areas 0.0% CH4 and 20.9% O2.

Contestant must simulate taking the air reading for 60 seconds.

Contestant can correct following hazards; de-energize non-permissible pump  in #1 entry, no fire extinguisher at pump by de-energizing and stating locking and tagging out pump,  powder mag cleared by de-energizing pump within 25 feet of pump cable; three sticks of powder; move to powder mag., advance curtain in #1 face,  move AMS up #2 entry, move life line up #2 entry,  stop bolting process and install curtain for roof bolters #3 entry

Contestant will report rock dust pod in #2 entry, check curtain xc #2 entry 2 to 3, over knee deep water #1 entry, missing balls on life line for stopping with door.

The contestant will have 30 minutes to work the problem.  Notify the contestant when 1 minute remains.