Team Member Written Test

2012 Southeast/Central Kentucky Mine Rescue Contest

June 19, 2012

Maysville, Kentucky

Name __________________________  Company ____________________________

Team Name ____________________   Contest Position No. __________________

Team Member No. ______________

Circle the letter for your answer.  Circle only one answer.

- A mine rescue and recovery operation simply consists of a team going into the mine to rescue survivors or put out a fire.

  - true

  - false

- Federal officials have the following function(s) in a mine rescue event:

  - advise and observe

  - supervise and direct

  - consult

  - all of the above

  - none of the above

- The mine rescue team is under direct supervision of the team captain.

  - true

  - false

- All roads and paths leading to the mine should be secured and guarded by:

  - company personnel

  - police officers

  - either of the above

  - none of the above

- The mine manager or superintendent should establish the command center and oversee all aspects of the rescue and recovery operation.

  - true

  - false

- One of the surface operation duties of the mine clerk is to examine each person entering the mine for matches and smoking materials.

  - true

  - false

- Which one of the following is a false statement:

  - Portable gas detectors accurately detect oxygen deficiency, carbon monoxide, methane, and hydrogen sulfide.

  - Chemical analysis is a more accurate method for detection of other gases.

  - Air samples can be collected in evacuated bottles.

  - Before March 9, 1978, electrical circuit gas detectors did not have to be approved.

- Air samples taken from behind sealed areas of the mine are analyzed to determine when it’s safe to begin rescue work.

  - true

  - false

- Which one of the following best describes a gas:

  - has a definite shape and volume

  - has a definite volume but changes shape

  - has neither shape or volume

  - none of the above

- Which one of the following does not affect the rate of diffusion of a gas:

  - air currents in the mine

  - turbulence of the air

  - temperature

  - atmospheric pressure

  - flammability range

- Specific gravity and relative weight mean the same thing.

  - true

  - false

- One of the gases below is not soluble in water.  Which one?

  - sulfur dioxide

  - radon

  - acetylene

  - hydrogen

- The Threshold Limit Value (TLV) of a gas is typically expressed in:

  - percent

  - parts per million

  - parts per billion

  - ph (protons of hydrogen)

- Asphyxiating gases cause suffocation.  They do this by displacing nitrogen in the air.

  - true

  - false

- The gases present in a mine following a disaster will vary according to:

  - the type of mine

  - the disaster situation

  - the type of equipment

  - all of the above

  - a and b above

- Oxygen is an explosive gas.

  - true

  - false

- Downcast is an intake ventilation shaft and upcast is an exhaust ventilation shaft.

  - true

  - false

- When it comes time to fixing the ventilation, the command center will be counting on you to build controls where and how you are instructed.

  - true

  - false

- The natural ventilation pressure can only be supplied by an energy source.

  - true

  - false

- Which of the following describes a bulkhead:

  - concrete blocks or other incombustible material

  - sealed tightly against the back, floor, and sides

  - a stopping

  - all of the above

  - a and b above

- The smoke tube is used mainly to determine what direction very slow moving air is moving but not the velocity.

  - true

  - false

- Which of the following is an incorrect statement:

  - It is best to enter the mine by way of the safest intake airway

  - Check the cage to make sure it’s operating properly

  - Test an automatic elevator by running it down and up at least once.

  - All of the above are correct

- A fresh air base is usually established at the point where conditions no longer permit barefaced exploration.

  - true

  - false

- There should be a communication link between the team and the fresh air base.

  - true

  - false

- Logging the times that all personnel enter and leave the fresh air base is the responsibility of:

  - not required by anyone

  - fresh air base coordinator

  - mine clerk

  - mine superintendent

- Which of the following is an example of a class D combustible metal:

  - potassium

  - aluminum

  - zinc oxide

  - none of the above

- Choose the item below to best indicate why a mine fire would be sealed rather than fought directly.

  - insufficient materials to fight directly

  - buildup of explosive gases

  - location of the fire

  - all of the above

  - a and b above

- When survivors are located, the location, time, and date should be marked on the team’s map and marked on the side in the passageway where they were found.

  - true

  - false

- A second priority triage condition is:

  - inhalation of poisonous gas

  - moderate heat exhaustion

  - third degree burns involving less than 2% of the body

  - none of the above

- A consideration when re-ventilating after an explosion is the percent of oxygen present.

  - true

  - false