2012 Northern Mine Rescue Contest

Rochester, NY

Written Test – Field Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Circle the letter preceding the correct answer to each of the following questions.  Circle only one answer per question.

- The mine superintendent or other designated person, as part of the mine emergency command group (Command Center), will likely oversee numerous aspects of rescue and recovery operations.

  - True*

  - False

- The degree to which a toxic gas will affect you depends on three factors: (1) how concentrated the gas is; (2) how toxic the gas is; and (3) ________.

  - the Threshold Limit Value of the gas.

  - whether the gas has an IDLH limit.

  - how well the gas interacts with oxygen.

  - how long you are exposed to the gas. *

- Some toxic gases harm the skin or can be absorbed by the skin.  An SCBA will protect you from these gases.

  - True

  - False*

- It is much more difficult to remove a concentration of a light gas like hydrogen by ventilation than it is to remove the same concentration of a heavier gas like sulfur dioxide.

  - True

  - False*

- Atmospheric pressure is measured _________.

  - on the litmus scale

  - using an anemometer

  - on a barometer*

  - with a sling psychrometer

- Gases respond to cold temperatures by expanding and diffusing more readily.

  - True

  - False*

- ____________ determines where a gas will stratify in still air in the mine (whether it will rise or fall).

  - The atomic number

  - The chemical index

  - Poisson’s Ratio

  - Specific gravity*

  - None of the above

- The basic principle underlying mine ventilation is that air always moves __________.

  - when the fan is operating

  - wherever the permanent controls direct it to go

  - from high pressure regions to low pressure regions*

  - toward the working faces

  - None of the above

- With mechanical ventilation, mine fans are used to create the _________ by changing the air pressure at specified points in the mine.

  - pressure differential*

  - constant flow paths

  - volumetric airflow

  - inertial distribution

- Regulators are used to control and adjust the quality of airflow in the mine in order to ensure proper distribution.

  - True

  - False*

- Barefaced exploration should stop at any point __________.

  - when the team encounters smoke or damage

  - when gas tests indicate the presence carbon monoxide or other toxic gases

  - when there are elevated readings of explosive gases

  - when an oxygen deficiency is detected

  - All of the above*

- The fresh air base is the base of operations and starting point for rescue and recovery work into respirable atmospheres.

  - True

  - False*

- When conducting rescue work, it is a good idea to limit intake of stimulants such as coffee and colas, because _________.

  - they keep you awake

  - they increase your heart rate

  - they increase your respiration rate

  - Both b. and c. *

- Before your team proceeds to the fresh air base, it is the ________ responsibility to make sure the team, its equipment, and its apparatuses are ready to go.

  - fresh air base coordinator’s

  - captain’s*

  - team technician’s

  - safety director’s

  - mine emergency coordinator’s

- If the team loses voice contact with the fresh air base, three tugs or pulls on the communication line will signify ________.

  - Advance

  - Retreat*

  - Stop

  - Emergency or Distress

- Information the team relays to the fresh air base as it proceeds is known as the “_______.”

  - systematic update

  - debriefing information

  - exploratory data

  - progress report*

- Think of Class B fires as those that involve contents that will _______.

  - Burn

  - Blister

  - Boil*

  - Bake

- Water is an effective extinguishing agent on ________ fires.

  - Class A*

  - Class B

  - Class C

  - All of the above

- When a team goes into a mine to explore or fight a fire, it should be concerned with two main things -- ________.

  - how many people are missing and where they are located

  - where the fire is located and the conditions in the fire area

  - toxic chemicals and explosive gases

  - spreading of the fire and the possibility of an explosion*

  - None of the above

- The explosive range of hydrogen is 4.0 to 74.2 percent when there is at least 4.0 percent oxygen present.

  - True

  - False*

- The explosive range of methane is 5 to 15 percent when there is at least _______ percent oxygen present.

  - 14.3

  - 10.7

  - 12.1*

  - 20.9

- When several survivors suffering from physical and/or psychological trauma have been located, the accurate sorting of priority victims may mean the difference between life and death.  This sorting of victims is commonly referred to as the “______” system.

  - priority

  - moulage

  - first line

  - triage*

  - None of the above

- The best way to relieve psychological stress in survivors is to communicate with them _________.

  - as soon as possible*

  - only when necessary

  - enough to determine what has happened

  - for at least 15 minutes

- When a team locates a body, the usual procedure is to _______.

  - keep calm

  - cover the victim

  - place the victim in a body bag

  - report the location to the command center*

- Reestablishing ventilation and bringing fresh air to an area damaged by fire or explosion is the main task of mine rescue teams in a rescue operation.

  - True

  - False*

- Direct ventilation is the re-ventilation of a sealed area in successive blocks by means of airlocks.

  - True

  - False*

- The most hazardous aspect of hydrogen is the fact that it can replace oxygen in air and act as an asphyxiant.

  - True

  - False*

- Sulfur dioxide will not burn or explode but it is a very toxic and irritating gas.

  - True*

  - False

- Hydrogen sulfide is flammable and explosive in concentrations of 4.3 to 45.5 percent in normal air.  It is most explosive at _______ percent.

  - 12.1

  - 45.5

  - 4.3

  - 14.2*

- There are three reasons for the “team check,” these include: __________.

  - to make sure that the team is fit and ready to continue

  - give the team a chance to rest

  - break up the monotony of systematic exploration

  - team checks are required by the contest rules

  - to make sure that each team member’s apparatus is functioning properly

  - a., b., and e.*

  - a., d., and e.

  - only d.