Judge’s Instructions

- Show the contestant the time clock and the check in/out board.

- Provide contestant with the blank map, written statement, and ventilation and roof control plans.  The contestant has 5 minutes to review the plans prior starting the clock and the underground portion of the contest.

- Show the contestant the entries and which area he or she is to pre-shift.  Entries are labeled left to right facing inby.

Contestant needs to take air reading Last Open Cross-Cut to be able to insure compliance with vent plan.

For taking the air reading on the section, give the contestant the following information:

LOX 		Width = 	19 feet

Height = 	7 feet

Area = 	133			CORRECT LOCATION

Velocity =	210 fpm for LOX face fan off, 98 fpm face fan on  (See Below)

CFM =            27930 CFM

LOX Method of calculations = 210 FPM Area measurements minus the Vent tube equals area of 128 times the FPM and then add the air quantity for fan off.

LOX Method of calculations = 98 FPM Area measurements minus the Vent tube equals area of 128 times the FPM and then add the air quantity for fan on.

Number two entry air quantity fan on = 15386 CFM

Fan off = 1050 CFM

If contestant does not take an air reading in the proper location for the LOX; deduct for improper location

If contestant advances vent tube in #2 they will send over 1% ch4 through face fan, deduct for endanger them self and if greaser is still on section include them.

If contestant turns off all power in the section flip placard at the water hole to over knee deep, and deduct for an additional hazard that cannot be corrected and if not identified deduct or if not recorded.

Provide the contestant the following gas reading for the outby areas 0.0% CH4 and 20.9% O2.

Contestant must simulate taking the air reading for 60 seconds.

Contestant can correct following hazards:  Turn off face fan or shut off air to #2 in vent tube and hang line curtain in #2 face to replace vent tube that is back ; clear Methane #2 face; clear Methane #3 face, ventilate #3 face; Miner energized; Roof bolter energized; move warning sign #3 face; move CO sensor to outby tail piece, .

The contestant will have 30 minutes to work the problem.  Notify the contestant when 1 minute remains.