VENTILATION PLAN

- Ventilation devices shall be maintained to within 5 feet of the face and to the last row of supports.

- Permanent ventilation (stoppings) between intake to return shall be maintained up to and including the third connecting crosscut.

- Air Quantities Required

| Mining Face | 12,000 CFM |
| --- | --- |
| Idle Face | 5,000 CFM |
| Bolting Face | 5,000 CFM |
| Working place | 5,000 CFM |
| Last Open Crosscut | 22,000 CFM |

- No roof bolting activities can be conducted on the downwind side of the continuous miner.

Roof Control Plan

1.    The Roof Control Plan requires 5-foot fully grouted resin bolts to be 	installed on 5-foot by 5-foot centers, with a minimum of 4 bolts per row.

2.     Roof bolts are required to be installed to within 5 feet of the face.

3.	The depth of mining cuts shall not exceed 20 feet as measured from the 	last row of permanent supports.

4.	Faces shall be bolted within 24 hours of mining; except during equipment 	(roof bolter) breakdowns.   Upon completion of repairs, bolting of un-	supported faces shall immediately begin.

- Unsupported warning indicator to be hung on second to last row.

Emergency Response Plan

- Section SCSR shall be provided with enough SCSR’s for every person working on the mining section.

CONTESTANT STATEMENT

You have been assigned to do a pre-shift examination of the 001 section.  This is a down shift for the section, conducting some maintenance.   This includes all entries #1 - #3.   Entries are average 20-feet wide by 8-feet high.   The mine has a history of water and methane.  Energizing / de-energizing equipment is handled through switches.  All actions must be verbalized to the Judges.  Gas readings and air readings will be handled through the Judges.