Date of Examination	6/6/13		Time From:		AM/PM  To:			AM/PM

Section/Area	003		       Reported Outside?   Yes	 No	  Time:			AM/PM

Reported By:				  Received By:			  INITIAL (AUTHORIZED PERSON)

Preshift required within 3 hours prior to any 8-hour interval.

| Location | Hazardous Condition | CH4 | O2 | Action Taken |
| --- | --- | --- | --- | --- |
| Entry #1 , XC #1 | Not enough SCSR’s for crew |  |  | Dangered |
| Entry #1, XC #1 | Not enough air for Diesel |  |  | Turn off unit |
| Entry #1, XC #1 | Not enough air in face |  |  | Repair vent curtain corner |
| Entry #1 face |  | 0.0% | 20.9% |  |
| Entry #2 | Broken fire hydrant |  |  | Dangered |
| Entry #2 | Life line over belt |  |  | Re-route line |
| Entry #2 face |  | 0.0% | 20.9% |  |
| Entry #3 face |  | 0.0% | 20.9% |  |
| Entry #3 | Roof bolter bolting downwind of miner |  |  | Stop bolting |
| Entry #3 | Not enough air in face |  |  | Repair vent curtain corner |
| Power Center |  | 0.0% | 20.9% |  |
| Entry #3 | Gas reading | 0.0% | 20.9% |  |
| Entry #1 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |
| Entry #2 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |
| Entry #3 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |

Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOX | 23680 |  |  |
| Entry #1 | 4080* | *Not required |  |
| Entry #2 | 16640* |  |  |
| Entry #3 | 1824* |  |  |

Velocities

Longwall Headgate:  			  				Longwall Tailgate:

CH4:		  O2:

Remarks:

Signed by Preshift Certified Examiner		      Date					     Certification Number

Countersigned by Mine Foreman		      Date					     Certification Number

Countersigned by Operator/Agent		      Date					     Certification Number