PRICE, UTAH PRESHIFT CONTEST – 2013

CONTESTANT: _________________________ WORKING No.:_____

JUDGES INSTRUCTIONS

- Show contestant time clock and check in/out board.  Contestant only has to hang tag on board and does not have to sign and date board.

- Contestant must provide own distance measuring device, tool apron, blank index cards, pen/pencil, paper, clip board, anemometer, watch, roof testing device, and detector.

- When contestant is ready, provide him/her with the blank mine map, statement, and ventilation and roof control plans.  Contestant has 5 minutes to review these and cannot travel into the mine until the clock is started.  THE 5-MINUTE REVIEW IS DONE WITH THE CLOCK NOT YET STARTED.

- Contestants have 30 minutes after starting clock to complete the problem.  Judges will notify contestant when 1 minute is left.

- Don’t take contestant back on field after clock is stopped & don’t discuss discounts.

JUDGING INFORMATION

OUTSIDE							      CHECK IF DONE

START CLOCK....................................................................................    ________

CHECK IN............................................................................................    ________

CHECK SCSR......................................................................................    ________

CHECK GAS DETECTOR (Must be left on during problem)................   ________

CHECK IF CONTESTANT HAS REQUIRED EQUIPMENT

SAFETY CAP................................................................................    ________

SAFETY BOOTS (not shoes)........................................................    ________

MINING BELT w/ID TAG THAT MATCHES CHECK-IN TAG.......    ________

CHECK IN TAG ………………………………………………………     ________

MSHA APPROVED CAP LIGHT (must work but can be left off)....   ________

SCSR..............................................................................................   ________

ANEMOMETER ……………...........................................................   ________

WATCH ………………………………………………………………...    ________

MSHA APPROVED GAS DETECTOR (must be left on).................   ________

ROOF TESTING DEVICE...............................................................   ________

DISTANCE MEASURING DEVICE.................................................   ________

BLANK INDEX CARDS....................................................................  ________

JUDGING INFORMATION

GAS TESTS & DTI’s						TEST 		   DTI

MADE		 TEST

No. 1 Entry (anywhere in entry).............................................. ______	______

No. 2 Entry (anywhere in entry).............................................. ______	______

No. 3 Entry (anywhere in entry).............................................. ______	______

No. 1 Face ……………………………...................................... ______	______

No. 2 Face.............................................................................. ______	______

No. 3 Face ……………………................................................. ______	______

Section Power Center …………..…......................................... ______	______

ROOF TESTS (verbally state visual exam in each entry)		   TEST MADE

No. 1 Entry............................................................................................ __________

No. 2 Entry............................................................................................ __________

No. 3 Entry............................................................................................ __________

HAZARDOUS CONDITIONS (verbally identify)			      IDENTIFY

No. 1 Entry

Diesel operating not enough air( turn off diesel)….….……… ___________

Not enough air in idle face (fix corner of curtain)….……......... ___________

Not enough SCSR’s for crew on section (danger & DTI)….… ___________

No. 2 Entry

Life line ran over belt (re-install life line)…………… …….…... ___________                           		Damaged fire hydrant (warning & DTI)………………..………. ___________

Stopping not Check curtain in x-cut 2 (danger & DTI)………... ___________

No. 3 Entry

Roof bolter bolting downwind miner (stop and ventilate) ..___________

Not enough air for bolting (fix curtain)…………………………..  ___________

AIR READINGS (Entries & XCs are 20’ wide X 8’ high and the area behind curtains given on placards)   CORRECTLY  TAKEN

148 fpm - LOX between Nos. 2 & 3 Entries ......................................................... _________

NOTES:

- Must take air readings for 60 seconds.

- Not taking LOX air reading in proper location. Rule 9.

- Contestant may use either anemometer held in proper direction of air flow.

- Not taking a total LOX air reading noted above. Rule 7.

- If placard not present at required gas test location, 02 = 20.9%, CH4 = 0.0%.

- If contestant travel beyond roof bolt to fix move vent device in #3 face, contestant endangers self. Rule 16