Date of Examination	6/19/14		Time From:		AM/PM  To:			AM/PM

Section/Area	003		       Reported Outside?   Yes	 No	  Time:			AM/PM

Reported By:				  Received By:			  INITIAL (AUTHORIZED PERSON)

Preshift required within 3 hours prior to any 8-hour interval.

| Location | Hazardous Condition | CH4 | Action Taken |
| --- | --- | --- | --- |
| Entry #3, XC #2 | Pump labeled wrong |  | Dangered |
| Entry #3, | Life line backwards |  | Re-hang |
| Entry #3 face | Excessive Methane | 1.45% | Ventilate |
| Entry #2, XC 1 to 2 | Belt fabric slip hazard |  | dangered |
| Entry #2, XC#3 | Hot bottom belt roller |  | Turn off belt and Danger |
| Entry #2, XC 4 | Timbers missing toe of cave |  | Dangered |
| Entry #2 | Curtain missing |  | Install check curtain |
| Entry #2 face |  | 0.7% | None observed |
| Entry #1, XC 3 | Equipment doors not airlock |  | dangered |
| Entry #1, XC 3 to 4 | Roof bolter energized high methane in cave |  | De-energized bolter and dangered |
| Entry #1 face | High methane | 2.5% | Installed check curtain |
| Power Center |  | 0.0% |  |
| Entry #1 | Gas reading may be part of other entry above | 0.9% |  |
| Entry #2 | Gas reading may be part of other entry above | 0.0% |  |
| Entry #3 | Gas reading may be part of other entry above | 0.0% |  |

Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOX | 29,260 |  |  |

Velocities

Longwall Headgate:  			  				Longwall Tailgate:

CH4:		  O2:

Remarks:

Signed by Preshift Certified Examiner		      Date					     Certification Number

Countersigned by Mine Foreman		      Date					     Certification Number

Countersigned by Operator/Agent		      Date					     Certification Number