Colorado Mine Rescue Contest

Golden, CO

May 20-22, 2014

DRAEGER BG4 Technician Team Test

# Company Name_____________________________________________

Team Name________________________________________________

Name_____________________________________________________

1.  The volume of gas changes in response to any changes to atmospheric pressure or temperature. For example: An decrease in pressure causes a gas to contract.

- True

- False

2. The specific gravity of normal air is ____?

- 2.0

- 1.5

- 2.5

- 1.0

3.  Sulfur dioxide has a specific gravity of ______?

- 2.2639

- 2.2640

- 2.2638

- 2.2648

4.  Oxygen is the first largest component of normal air.

- True

- False

5.  Carbon Monoxide is explosive and flammable. It’s explosive range in normal air is ____ to ____ percent.

- 12.0 to 75.0

- 13.0 to 76.2

- 12.5 to 74.2

- 12.5 to 72.4

6.  For ventilation tubing can be either rigid (for exhausting systems) or collapsible (for forcing systems).

- True

- False

7.  Mine doors are always hung so that the ventilating air pressure will pull them closed if they are accidentally left open.

- True

- False

8.   A medium-velocity (or “regular”) anemometer for measuring velocities from ____ to _____ feet per minute

- 100 to 1,000

- 130 to 3,000

- 110 to 1,500

- 120 to 2,000

9. When using a smoke tube the more accurate method of determining the air velocity is to take readings at quarter points within the airway.

- True

- False

10. The speech diaphragm of the BG 4 is a very thin paper, which could easily

contribute to considerable leakage if it is damaged.

- True

- False

11. All parts of the BG 4 must be cleaned in lukewarm water with a

strong detergent.

- True

- False

12. When drying the Max temperature is ___ °C

- 65 °C

- 70 °C

- 60 °C

- None of the above

13. When charging the oxygen cylinder the maximum charging pressure is ______ psi/200 bar.

- 3035

- 3235

- 3535

- 3135

14. The oxygen must have a purity < 99.5% and must be

both tasteless and odorless.

- True

- False

15. Testing the PSS BG 4 with Inserted CO2 Absorber. During the shelf life of the apparatus the operating test can be run a total of _____ times, each

test lasting no more than 15 minutes.

- four

- five

- seven

- six

16. Checking the Response threshold of the Low

Pressure Warning.The low-pressure warning should be activated

when the pressure is lower than ____ mbar .

a) 1.5

b) 1.4

c) 1.7

d) 1.3

17. Checking the Inhalation Valve, Set “set positive pressure pumping”. Tightly pinch the exhalation hose with your hand. Start pumping slowly until ____  mbar is indicated on the pressure gauge.

a) 10

b) 15

c) 20

d) None of the above

18. Leak Test with Positive Pressure  Set “Leak test” Press the button to reduce the pressure to ___ mbar. Start the stopwatch. The pressure must not change by more than 1 mbar during one minute.

a)  6

b)  7

c)  8

d) None of the above

19. Check Relief Valve  Set “positive pressure pumping”, Continue pumping until the relief valve opens. Read off the opening pressure on the pressure

gauge: It should lie between____ and _____ mbar.

a) 3 and 4

b) 2 and 6

c) 2 and 5

d) 3 and 5

20. High-Pressure Leak Test   In the event of a fault:

The X icon appears on the display.

Alarm bleeps four times.

red LEDs flash.

a) True

b) False

21. Checking the Constant Dosage Valve  The constant metering quantity should

lie between____ an ____ L/min1).

- 1.5 an 1.9

- 1.4 an 1.8

- 1.5 an 2.0

22. Symbol “Battery warning 1”On power up a long beep (acoustic alarm) will sound and the display will show “Battery warning 1” icon. When this icon is first displayed, it is acceptable to safely use the PSS BG 4 for up to 6 hours (under

standard Sentinel operation).

- True

- False

23. BG 4 Pressure Reducer High pressure IN activates the Sentinel

Medium pressure output   4.2 bar ± .2bar (58 psi — 64 psi)

- True

- False

24. BG 4 Pressure Reducer High pressure IN activates the Sentinel

Relief valve activation ____ bar (87 psi)

- 5

- 7

- 6

- 4

25. BG 4 Pressure Reducer High pressure IN activates the Sentinel

Dosage output ___ to____ L/min.

- 1.5 to 1.8

- 1.8 to 2.0

- 1.5 to 1.9

- None of the above

26. BG 4 Pressure Reducer High pressure IN activates the Sentinel

Bypass output  > 60 L/min.

- True

- False

27. BG 4 High Pressure O2 Cylinders the Cylinder contains 500 liters of 99% O2

- True

- False

28. BG 4 High Pressure O2 Cylinders the Carbon cylinder pressure is full at ____ psi

- 2000

- 3000

- 2500

- 3500

29.  BG 4 High Pressure O2 Cylinders the Carbon cylinder has a 20 year lifespan.

- True

- False

30. Equipment Breathing apparatus approved for at least ____hours

shall be used in the Mine Rescue Contest problems.

- six

- five

- three

- four