Colorado Mine Rescue Contest

Golden, CO

May 20-22, 2014

MX4 Ventis Technician Team Test

# Company Name_____________________________________________

Team Name________________________________________________

Name_____________________________________________________

1.  The volume of gas changes in response to any changes to atmospheric pressure or temperature. For example: An decrease in pressure causes a gas to contract.

- True

- False

2. The specific gravity of normal air is ____?

- 2.0

- 1.5

- 2.5

- 1.0

3.  Sulfur dioxide has a specific gravity of ______?

- 2.2639

- 2.2640

- 2.2638

- 2.2648

4.  Oxygen is the first largest component of normal air.

- True

- False

5.  Carbon Monoxide is explosive and flammable. It’s explosive range in normal air is ____ to ____ percent.

- 12.0 to 75.0

- 13.0 to 76.2

- 12.5 to 74.2

- 12.5 to 72.4

6.  For ventilation tubing can be either rigid (for exhausting systems) or collapsible (for forcing systems).

- True

- False

7.  Mine doors are always hung so that the ventilating air pressure will pull them closed if they are accidentally left open.

- True

- False

8.   A medium-velocity (or “regular”) anemometer for measuring velocities from ____ to _____ feet per minute

- 100 to 1,000

- 130 to 3,000

- 110 to 1,500

- 120 to 2,000

9. When using a smoke tube the more accurate method of determining the air velocity is to take readings at quarter points within the airway.

- True

- False

10. For safety reasons, the Ventis MX4 must be operated and serviced by qualified personnel only.

- True

- False

11.  Servicing the unit, replacing or charging battery packs, or using the communication port can be done in any area.

- True

- False

12. _______ compound vapors or other known contaminants may affect the combustible gas sensor and cause readings of combustible gas to be lower than actual gas concentrations

- Methane

- Silicone

- Nitric Oxide

- None of the above

13. The use of plastic cases can produce inaccurate readings with diffusion (non-aspirated) gas detection instruments for specific monitoring applications.

- True

- False

14. Obstruction of the sensor openings or pump inlet and/or contamination of the water barriers may cause readings to be higher than actual gas concentrations.

- True

- False

15. CSA C22.2 No. 152 requires before each day’s usage, sensitivity must be tested on a known concentration of pentane or methane equivalent to ___% or ___% of full scale concentration.

- 35% or 55%

- 20% or 45%

- 25% or 50%

- 30% or 65%

16. Industrial Scientific recommends the “3 & 3 Sampling Rule” when sampling with a motorized pump and tubing, one should allow for 3 minutes plus 3 seconds per foot of tubing used, prior to noting the monitor readings.

a )True

b) False

17. The monitor performs continuous datalogging at ___ second intervals.

a) 10

b) 15

c) 20

d) 5

18. The Ventis MX4 has _____ alarm and warning levels.

a)  three

b)  four

c)  two

d) None of the above

19. The lowest level indicator is a warning with beep patterns to indicate service needs (e.g., low battery or calibration due).

a) True

b) False

20. A negative over-range condition occurs when the gas concentration value sensed is more than the sensor’s measuring range.

a) True

b) False

21. A STEL alarm occurs when the calculated time weighted average reaches the monitor’s hazardous value for the set time frame..

- True

- False

22. A “b” indicates which sensor(s) is overdue for bump testing. Two beeps sound every _____ seconds and the calendar and alarm icons display.

- 20

- 25

- 30

- 15

23.  The gas value flashes for each sensor overdue for calibration._____ beeps sound every 30 seconds and the calendar and alarm icons display. The gas cylinder icon flashes.

- Two

- Three

- Four

- None of the above

24.  The rechargeable Lithium-ion (Li-ion), batteries have recharge time of ____ hours.

- 2-5

- 4-6

- 3-7.5

- 3-5

25. To power-on the Ventis MX4, press ON/OFF/MODE and hold for ____ to ___ seconds

- two to four

- one to two

- three to four

- three to five

26. To enter configuration mode: simultaneously press ON/OFF/MODE and

ENTER, hold for five seconds, and release.

- True

- False

27. The standard calibration option sets the monitor to calibrate all four

sensors simultaneously.

- True

- False

28. On the Bump Test Percentage Requirement Screen the Value range is 50% to 99%

- True

- False

29. During calibration Aspirated monitor with Demand Flow Regulator, a Calibration tubing 2 feet in length with integrated “t” fitting must be used.

- True

- False

30. Equipment Breathing apparatus approved for at least ____hours

shall be used in the Mine Rescue Contest problems.

- six

- five

- three

- four