Missouri Mine Rescue Contest

Rolla, MO

September 23-25, 2014

BG4 Written Test

1. The panorama Nova mask is tested with negative pressure?

A. True

B. False

2. The high pressure o-ring should be replaced every 6 months?

A. True

B. False

3. The temperature for drying must not exceed 60 degrees C?

A. True

B. False

4. Weight of the Bg4 with 1.4 kg ice, mask and charged cylinder is ___lbs.

A. 31

B. 32

C. 33

D. 34

5. A carbon cylinder holds 2 quarts of compressed air?

A. True

B. False

6. Relief valve, on the reducer, activation is ___ psi?

A. 78

B. 85

C. 87

D. 80

7. Bypass output is 50 psi?

A.  True

B. False

8. Minimum valve output is 80 psi?

A. True

B. False

9. The minimum valve utilizes medium pressure from the reducer?

A. True

B. False

10. The inhalation flange side of the center connector is short?

A. True

B. False

11. Moisture trap opens at < 10 mbar?

A. True

B. False

12. The breathing temperature at 240 minutes with a breathing rate	30 l/min and ambient temperature at 75 degrees F is _____.

A. 93

B. 95

C. 98

D. 100

13. Operation with out ice pack is also permitted 0 degrees C.

A. True

B. False

14. At a pressure greater than 1.4 mbar the negative pressure warning must react?

A. True

B. False

15. Set “pump negative pressure” to check inhalation valve.

A. True

B. False

16. To check the relief valve, an opened cylinder and bypass can be used to inflate the bag?

A. True

B. False

17. The constant dosage must be between 1.5 and 1.9 L/sec.?

A. True

B. False

18. After minimum valve check the RZ remains at position “pump negative pressure”.

A. True

B. False

19 Minimum Valve test, observe pressure gauge; the admission of the minimum valve must activate before 1.2 mbar?

A. True

B. False

20 To check the bypass valve, set the RZ on negative pressure?

A. True

B. False

21. The smoke tube is used mainly to determine what direction very slow-moving oxygen is moving, and at what velocity.

A. True

B. False

22. __________ are devices used to control and adjust the quantity of airflow in the mine.

A. Anemometers

B. Auxiliary Fans

C. Regulators

D. None of the above

23. To obtain the “flow” of air through the mine there must be a difference in air quality

between the intake and exhaust airways.

A. True

B. False

24. If placards have not been changed after _______ seconds, teams must assume that

their actions were not successful.

A. 10

B. 20

C. 15

D. 30

25. No team member may advance more than (3) feet beyond the second (2nd)

intersection before tying across and/or behind into all unexplored areas that intersect.

A. True

B. False

26. The captain must verbally indicate to the judges each time initials and dates are

simulated.

A. True

B. False

27. Whether to use regulators to control the fire or to entirely seal the fire must be

decided by the __________.

A. Fresh Air Base Attendant

B. Mine Manager

C. Team

D. Command Center

28. The most dangerous aspect of methane is the fact that it is toxic.

A. True

B. False

29. Knowing the effects of air current, temperature, and pressure on a gas will help you

determine its rate of diffusion.

A. True

B. False

30. Your team will make frequent tests for gases as it advances beyond the portal.

A. True

B. False