2014 Southwestern Regional Mine Rescue Contest

Carlsbad, NM

Written Test – Field Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

- During a rescue and recovery operation, one of the duties of the outside Supervisor is to:

  - Arrange for guards and state and/or local police.

  - Notify all persons on the notification plan of the emergency.

  - Obtain gas samples from the main exhaust.

  - None of the above

- The explosive range of Ethane in normal air is?

  - 2.12 – 9.35%

  - 3.0 – 12.5%

  - 2.5 – 9.35%

  - None of the above

- Reestablishing ventilation and bringing fresh air to an area damaged by fire or explosion is the main task of mine rescue teams in a rescue operation.

  - True

  - False

- The law requires that gas detectors be able to measure concentrations of methane from 0.0 to 90% of volume, oxygen from 0.0 to 20% of volume, and carbon monoxide from 0.0 to 9,999 ppm.

  - True

  - False

- Air locking operations should never be undertaken until the oxygen content of the air behind the seals has been reduced to at least _________%.

  - 2.0%

  - .05%

  - 1%

  - 5.0%

- Urethane foam should never be applied greater than ______ inch thick because of spontaneous combustion.

  - ½ inch

  - 2 inch

  - 1 inch

  - 1 ½ inch

- You can allow a rescued miner to walk out of the mine alone if the miner appears to be in good shape?

  - True

  - False

- Usually, after temporary seals are erected, a waiting period of about 48 hours is recommended before beginning construction on permanent seals?

  - True

  - False

- When constructing a temporary bulkhead from a crosscut, the bulkhead should be ____ feet into the passageway?

  - 10 to 12

  - 1 to 2

  - 4 to 6

  - None of the above.

- The smoke tube is used to determine the direction and velocity of air moving above 120 feet per minute.

  - True

  - False

- If you are exposed to high concentrations of CO, you may experience very few symptoms before losing consciousness.

  - True

  - False

- Breathing air containing 5% Carbon Dioxide can increase respiration ___%.

  - 500

  - 300

  - 150

  - None of the above.

- ____________ is found after methane explosions in air having low oxygen content?

  - Butane

  - Ethane

  - Acetylene

  - Argon

- During the debriefing session the __________ will provide the information found during exploration?

  - Team Captain

  - Co-Captain

  - Fresh Air Base

  - Team

- Heavier gases such as carbon dioxide and sulfur dioxide do not diffuse rapidly, so they’re easier to disperse?

  - True

  - False

- The degree to which a toxic gas will affect you depends on three factors: 1) how concentrated the gas is 2) how explosive the gas is and 3) how long you’re exposed to the gas?

  - True

  - False

- The formula used to find the quantity of air moving through a drift is:

  - Quantity (ft3) = Area (ft2) x Velocity (ft/min.)

  - Quantity (ft3) = Area (ft2) x Velocity (ft/sec.)

  - Quantity (ft2) = Area (ft2) x Velocity (ft/min.)

- Oxides of nitrogen are highly toxic. Breathing even small amounts will cause irritable bowel syndrome.

  - True

  - False

- A line brattice is brattice cloth or plastic that is hung to channel intake air into a working area that otherwise would not have adequate ventilation.

  - True

  - False

- 3rd degree burns covering less than 10% of the body (not including hands, feet, or face) is considered low or third priority.

  - True

  - False

- The team briefing is normally conducted:

  - Only at a mine rescue contest

  - At the fresh air base

  - Command Center

  - None of the above

- Rock –Strata gases commonly called “rock gas” is assumed to contain what two types of gasses?

  - Hydrogen and Carbon Monoxide

  - Nitrogen and Sulfur Dioxide

  - Nitrogen and Carbon Dioxide

  - Hydrogen Sulfide and Hydrogen

- Normally gasses do not stratify when the ventilation system in a mine is working properly.

  - True

  - False

- In a multi-level mine, a tunnel driven perpendicular to the main vein system of the mine is considered a?

  - Drift

  - Stope

  - Crosscut

  - None of the above

- A main cause of oxygen deficiency in a mine is:

  - Insufficient ventilation

  - Displacement by other gases

  - A fire or explosion

  - Consumption by workers

  - All of the above.

- The three preconditions for opening a sealed fire area are: 1) O2 content is low enough to prevent an explosion 2) there is no CO and 3) the sealed area has cooled so the fire will not rekindle when re-ventilated?

  - True

  - False

- The advantage of progressive ventilation is it is a fast process.

  - True

  - False

- Ventilation controls affect the amount of air that travel and the direction of flow.

  - True

  - False

- A fresh air base is usually established at a point where conditions no longer permit barefaced exploration.

  - True

  - False

- The command center for rescue and recovery operations is generally only consisting of federal and state officials?

  - True

  - False