Missouri Mine Rescue Contest

Rolla, MO

October 3 – October 6, 2016

Written Team Trainer Test

- According to the 2016 M/NM Mine Rescue contest Rules, once a team is registered, no changes will be permitted without the permission of the local association.

  - True

  - False (Rule Book Pg. 2)

- Wireless communication or electronic devices will only be permitted in isolation if voted upon.

  - True

  - False (Rule Book Pg. 4)

- When a breathing apparatus is required to be used on a patient, the team must demonstrate proper donning procedures and unit activation.

  - True (Rule Book Pg. 5)

  - False

- While the team is in the mine, judges must not ask questions, answer questions, or interfere with the team.

  - True (Rule Book Pg. 17-18)

  - False

- When judging the field problem, in the event more than one discount applies, the lowest discount will be assessed for a violation.

  - True

  - False (Rule Book Pg. 18)

- Ventilation changes will be considered as starting, stopping, altering, or redirecting the air current.

  - True (Rule Book Pg. 19)

  - False

- On the mine maps, solid lines will denote actual workings.

  - True (Rule Book Pg. 23)

  - False

- If there are no harmful gas concentrations, entrances to all mine openings can be examined barefaced.

  - True

  - False (Rule Book Pg. 25)

- The team captain must orally warn the team each time loose ground conditions are encountered.

  - True (Rule Book Pg. 26)

  - False

- A team will be considered to have passed an opening or intersection when the number ___ member is passed the opening.

  - 3

  - 4

  - 5 (Rule Book Pg. 27)

  - None of the above

- The pulse is nothing more than a remote heartbeat.

  - True (Brady Ninth Edition Ch. 11 Pg. 224)

  - False

- ____ is the measurement of the pressure of blood against the walls of the arteries, both when the heart beats and when it is at rest.

  - Capillary Pressure

  - Palpation Pressure

  - Blood Pressure (Brady Ninth Edition Ch. 11 Pg. 227)

- Carotid pulse is the pulse felt on the thumb side of the wrist.

  - True

  - False (Brady Ninth Edition Ch. 12 Pg. 255)

- In SAMPLE history the S stands for significant and substantial.

  - True

  - False (Brady Ninth Edition Ch. 12 Pg. 262)

- Jugular Vein Distention is an indication of possible injury to the head.

  - True

  - False (Brady Ninth Edition Ch. 12 Pg. 227)

- The weight of air acts as a reference point from which we measure the relative weight of other gases.

  - True (Modules 2-6)

  - False

- Color, odor, and taste are physical properties that can help you identify a gas, especially when exploring under apparatus supplied oxygen.

  - True

  - False (Modules 2-8)

- Oxygen is not an explosive gas, but it does support combustion.

  - True (Modules 2-13)

  - False

- Oxygen is the largest component of normal air.

  - True

  - False (Modules 2-14)

- The specific gravity of Nitrogen is.

  - 0.6974

  - 0.9764

  - 0.9674 (Modules 2-14)

- Bulkhead and stoppings are not interchangeable terms.

  - True

  - False (Modules 4-10)

- Valves on water and compressed air lines (open or closed), is information that a team should mark on the mine map as the team explores.

  - True (Modules 4-30)

  - False

- The debriefing session is a very important aspect of your team’s exploration.

  - True (Modules 4-33)

  - False

- Temporary seals can be built using wood.

  - True (Modules 5-19)

  - False

- When building temporary seals, one of the most important things to consider is mine production.

  - True

  - False (Modules 5-21)

- Urethane foam is not an effective sealant when used around the perimeter of a seal.

  - True

  - False (Modules 5-23)

- Chlorine is a gas that is produced by the burning of Rubber, Neoprene, and PVC.

  - True (Modules 5-43)

  - False

- Second degree burns covering more than 30 percent of the body is an example of a first priority condition.

  - True (Modules 6-5)

  - False

- You should expect to see some very unpleasant sights when recovering bodies.

  - True (Modules 6-9)

  - False

- The body is 50 percent liquid.

  - True

  - False (Modules 6-9)