Use Indelible Pencil or Ink	PRESHIFT - CERTIFIED EXAMINER’S REPORT	             Report Shall Be Signed When Finished

Date of Examination _______________Time from: ___________ AM/PM To: _____________ AM/PM

Section/Area 			    Reported Outside?  Yes _____ No ____ Time: ________ AM/PM

Reported By: ____________________________________Received By: ________________ INITIAL)  (AUTHORIZED PERSON)

Preshift required within 3 hours prior to any 8-hour interval.

| Location | Hazardous condition | Action taken |
| --- | --- | --- |
| No. 1 entry outby 1st xcut | Draw rock | Pulled drawrock |
| 1st xcut between # 1 and # 2 | Check curtain down | Hung check curtain |
| No. 1 entry bet 1st and 2nd xcut | 2 dislodged timbers | Dangered off |
| No. 1 entry face area | Line curtain down | Hung line curtain |
| No.1 entry face area | Low O2 18.8% | Hung curtain, removed low O2 |
| No. 2 entry outby 1st xcut | Draw rock | Pulled drawrock |
| 1st xcut between # 2 and # 3 | Power center on return side of check curtain | Moved check curtain |
| LOCC between # 2 and # 3 | Water over knee deep | Turn off valve and pump water |
| LOCC between # 2 and # 3 | Low air reading | Dangered off |
| No. 2 entry face area | Line curtain down | Hung line curtain |
| No. 3 entry face area | Line curtain down | Hung line curtain |

Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOCC between # 2 and # 3 | 11340 |  |  |

Velocities

Longwall Headgate :  _____________________                                                Longwall Tailgate:  _____________________

Remarks:

________________________________________	____________________________			_________________

Signed by Preshift Certified Examiner				Date				Certification Number

_________________________________________	____________________________			_________________

Countersigned by Mine Foreman					Date				Certification Number

____________________________________	____________________________			_________________

Countersigned by Operator/Agent 					Date				Certification Number

THIS RECORD TO BE MAINTAINED FOR ONE (1) YEAR