# Buzzi Unicem USA – Signal Mountain Plant

# Annual Refresher Test Question ANSWERS - 2007

NAME                                                                  DATE

| Question | Answer |
| --- | --- |
| Who should correct unsafe conditions and unsafe actions? | Everyone |
| What is one reason for wearing a seat belt? | To keep from being ejected |
| PPE can only work if? | Worn Properly |
| What type of PPE is required when working in the plant? | Depends on the task |
| What type of PPE is required when using a grinder? | Faceshield / Safety glasses |
| Where is the proper place to attach the lanyard to your body harness? | Back D-ring |
| Your anchorage point should be able to withstand how much force? (in pounds) | 5000lbs |
| Where should your anchorage point be located if possible? | Overhead |
| The shock absorber should always be closest to you or your anchor point. [Pick one]. | Closest to you |
| The U-bolt of a Saddle Clamp always goes on the Live or Dead end. [Pick one]. | Dead end |
| How often must a ladder or scaffold be inspected? | Prior to use |
| With an A-frame ladder you must stay off? | Top 2 steps |
| How many rungs on a step ladder should be above the step off point? | 3 rungs |
| A ladder over what height should be tied off to secure it? | 6 foot |
| A scaffold should be built as _____________as possible? [fill in the blank] | Complete |
| When is a harness and tie-off required on a scaffold? | When it is incomplete |
| Who has to put a lock on equipment when maintenance or repair is being done? | Everyone working on the equipment |
| How do you check to be sure equipment is de-energized after locking it out? | Contact the control room – ask them to start it |
| Once a repair is made, what must be done before energizing the equipment? | Replace guards |
| Who can remove your lock? | You and your supervisor |
| What must be replaced before starting the equipment? | The guard |
| What does S.L.A.M. stand for and why do we use it? | Stop Look Analyze Manage – eliminate hazards |
| Who should correct unsafe conditions and unsafe actions? | Everyone |
| What is an example of a confined space? | Raw mill |
| How can we reduce the hazards of working in a confined space? | Use the permit |
| Question | Answer |
| What minimum PPE is required when entering a confined space? | Normal PPE + safety harness |
| Give an example of where a cartridge type respirator would be needed. | Painting |
| What is the major difference between an air purifying and an air supplied respirator? | Air purifying does not support life |
| If your job requires the use of a respirator, you must first obtain this…what is it? | Medical approval |
| How can you determine if you have a good respirator fit. | Perform a positive pressure test |
| If a respirator is not being used what are your options? | Store it in a sealed bag or throw it away |
| What is the rule about working alone? | Must have radio contact with control room |
| On a mine site, who has the Right of Way? | Production equipment |
| You should always do this before entering an active work area. What is it? | Make contact with the operator of the equipment |
| Why is communication important when working around production equipment? | Prevent an injury |
| Who are you required to notify of changes at the mine? | Your supervisor |
| Employees are allowed to ride on equipment if they are tied off? [true or false] | False |
| Employees can work from an equipment bucket if they are tied off?[true or false] | False |
| What must be attached to the fork lift when using a man basket? | Safety chain |
| Employees must wear this when working in a fork lift man basket? | Safety harness |
| Employees can climb out of fork lift man basket when it is elevated?[true or false] | False |
| Before lifting a load, what must be in place at the lift zone? | Barricade and flagger |
| Why do we use tag lines when moving a load with a crane? | Keep hands off the load |
| It is okay to be outside the vehicle with a suspended load as long as you are within eye sight of the load? [true or false] | False |
| Is a raised front-end loader bucket or elevated forklift forks considered a suspended load? | Yes |
| Why use a spotter during lifting operations? | Keep people out of the area |
| How often must equipment inspections be completed? | Daily |
| What should you do, if you find defective equipment? | Report it / tag it out |
| If a miner is exposed to a noise level of 100 dB, how long can he work there before he exceeds his allowable exposure? | 2 hours |
| A noise level of 95 dB seems to be twice as loud as a noise level of 90 dB…True or False? | True |
| Question | Answer |
| Compressed gas cylinders must be ____________ at all time | Secured |
| Cylinders must have a ___________or have a protective ring around the valve. | Cap |
| What are the steps if you leave a cutting torch for any period of time? | Valve it off / bleed it down |
| What must be in the area if you are welding or burning? | Fire extinguisher |
| If you are doing hot work what is one thing you must have in the immediate area? | Stand-by person |
| Compressed gas storage racks must be labeled with what? | A “No Smoking” sign |
| NFPA uses a number system to identify the hazard; _____is no hazard; ____is extreme hazard? | 0 / 4 |
| Which containers must be labeled according to MSHA Part 47 HazCom? | All containers |
| Where do you go to find out information about a chemical? | MSDS database |
| Where is the MSDS information located? | Location varies |
| What does MSDS stand for? | Material Safety Data Sheet |
| Why should you NEVER use Oxygen to cool off with? | O2 enrichment, O3 is an accelerant |
| You must report injuries to your supervisor, when? | Immediately / as soon as possible |
| Before rendering first aid always make sure that ________________________. | The area is safe |
| What is one thing you can do to slow the bleeding when someone is injured? | Direct pressure |
| How can you remember how to treat for shock? (hint ”pale….) | Raise the tail |
| How do you handle amputated parts? | Put in clean gauze and put on ice |
| List 2 signs or symptoms of a heart attack? | Sweating / numbness |
| List one of the signs of heat stress | Pale / nausea |
| How do you stay hydrated during hot weather? | Drink plenty of fluids |
| In CPR….what does A.B.C. stand for? | Airway / Breathing / Circulation |
| What is the ratio of breaths to compressions? | 3 / 20 |
| Employees share the responsibility for safety; what is one thing employees must do to avoid injury? | Abide by the rules |
| In preparing for emergencies, before beginning work in an area, what 2 things do you look for? | Emergency equipment / exit |
| Who should correct unsafe conditions and unsafe actions? | Everyone |
| Question | Answer |