Evacuation & Firefighting Quiz

- Hydrants used for fire fighting purposes must be visually inspected at least every  _____ months for damage or deterioration.

|  | a. one. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. two. |  |  |  |
|  | c. three. |  |  |  |
|  | d. four. |  |  |  |

- Records for fire extinguisher inspections must be maintained certifying the date inspection was performed.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- When the evacuation alarm sounds to evacuate a work area, travel to the designated safe area without delay.  Stay at this location until everyone is accounted for.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- A red arm sticking up in the transparent cap on top of a cartridge operated ABC dry chemical fire extinguisher is a sign that the fire extinguisher vessel has been pressurized.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Onsite fire fighting equipment shall be __________ that can extinguish fires of any class that could occur as a result of hazards present.

|  | a. the type. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. the size. |  |  |  |
|  | c. the quantity. |  |  |  |
|  | d. all of the above. |  |  |  |

- Five things a worker must look for when inspecting a CO2 cartridge operated ABC dry chemical fire extinguisher include …

  - Is inspection tag current?

  - Is there a plastic safety seal from the plunger over the discharge hose to the metal loop on the fire extinguisher shell?

  - Is the red arm sticking up in the transparent cap on top of the fire extinguisher shell?

  - Is access to the fire extinguisher clear?

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Maintenance checks of fire extinguishers are required at least once every 12 months.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Fire extinguishers are required to be visually inspected at least ___________ to determine that they are fully charged and operable.

|  | a. once a week |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. once a month |  |  |  |
|  | c. quarterly |  |  |  |
|  | d. none of the above. |  |  |  |

# Signature _________________________________ PR# _____________ Date _____________________

Instructor ____________________________________