EXPLOSIVES QUIZ

- The blast area is the area in which concussion (shock wave), flying material, or gases from an explosion may cause injury to persons and is determined by –

|  | a. Geology or material to be blasted |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Blast pattern |  |  |  |
|  | c. Burden, depth, diameter, and angle of the holes |  |  |  |
|  | d. Blasting experience of the mine |  |  |  |
|  | e. Delay system, powder factor, and pounds per delay |  |  |  |
|  | f. Type and amount of explosive material |  |  |  |
|  | g. Type and amount of stemming |  |  |  |
|  | h. All of the above |  |  |  |
|  | i. Some of the above |  |  |  |

- Vehicles containing explosive materials must be posted with warning signs that indicate the contents and are visible from each approach.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Smoking and use of open flames is not permitted within _____ feet of explosive materials except when separated by permanent noncombustible barriers.

|  | a. 25 |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. 30 |  |  |  |
|  | c. 40 |  |  |  |
|  | d. 50 |  |  |  |

- A blast site is the area where explosive materials are handled during loading, including the parameter formed by the loaded blast holes and 50 feet in all directions from loaded holes.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- A misfire is the complete or partial failure of explosive material to detonate as planned.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Persons who have been employed for at least 5 years in mining can be in control of blasting operations.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- If explosive material is suspected of burning at a blast site, persons must be evacuated from the area and not permitted to return for at least _____ hour(s) after the burning or suspected burning has stopped.

|  | a. ½ | c. 2 |  |  |
| --- | --- | --- | --- | --- |
|  | b. 1 | d. 3 |  |  |

# Signature ________________________________ Payroll # _____________ Date __________________

Instructor ________________________________ Instructor ___________________________________