BASIC PRINCIPLES OF GUARDING QUIZ

- The emergency stop cord must be sufficiently tight to assure the conveyor drive motor will be readily deactivated when the cord is pulled.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Drive couplings must be totally enclosed to prevent access to moving machine parts.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The backside of a guard for a drive belt and pulleys does not have to be totally enclosed if a worker only greases a fitting once a week.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Moving machine parts on a front-end loader such as the fan and alternator area must be guarded to prevent contact because of inspection and maintenance activities.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The tail pulley mechanism for a conveying system must be guarded on –

|  | a. Each side of tail pulley |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Rear side of tail pulley |  |  |  |
|  | c. Top of tail pulley |  |  |  |
|  | d. All of the above |  |  |  |
|  | e. A and B |  |  |  |

- An effective machine guard will prevent access to all moving machine parts.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Guarded by location means –

|  | a. A person can not reach the overhead hazard |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. The hazard is obvious |  |  |  |
|  | c. A and B |  |  |  |
|  | d. None of the above |  |  |  |

- Emergency stop cords must be located along side an unguarded conveyor so that they –

|  | a. Can be reached by a person who falls on or against the conveyor belt |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. 12 inches above the floor. |  |  |  |
|  | c. 6 inches below the conveyor belt trough rollers |  |  |  |
|  | d. Are not necessary if you have anti-reversing mechanism installed |  |  |  |

- The conveying system structure provides adequate guarding for take-up pulleys.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Area guarding provides adequate protection.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

# Signature ______________________________ Payroll #_________________ Date _________________

Instructor __________________________________ Instructor _________________________________