Respiratory Protection Quiz

- The type of respirator used is based on:

|  | a. The chemical properties of the contaminant. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. The permissible exposure limit of the contaminant. |  |  |  |
|  | c. The oxygen level in the air. |  |  |  |
|  | d. All of the above. |  |  |  |

- If there is not enough oxygen in the work area, use an air-purifying respirator with organic vapor cartridges.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Use of an atmosphere-supplying respirator can be limited by:

|  | a. The concentration of contaminate in the air. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. The amount of oxygen in the air. |  |  |  |
|  | c. The length of the airline, or the operation time of the air cylinder. |  |  |  |
|  | d. The type of air-purifying filter worn on the face piece. |  |  |  |

- Respirators that are used only for emergencies must be inspected each month, and cleaned after each use.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- If you smell or taste contaminants inside of your air-purifying respirator, exit to a safe area immediately because:

|  | a. Your face piece may not have a good seal. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Your cartridges may be saturated. |  |  |  |
|  | c. Levels of contaminant in the air may have increased. |  |  |  |
|  | d. All of the above. |  |  |  |

- Tight-fitting face pieces need to be fit tested:

|  | a. At least annually. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. So you use the correct size. |  |  |  |
|  | c. Only if you have a beard. |  |  |  |
|  | d. Both a. and b. |  |  |  |

- Enclosing the operation or installing exhaust ventilation can control hazardous air contaminants.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Use of an air-purifying respirator can be limited by:

|  | a. The concentration of contaminant in the air. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. The amount of oxygen in the air. |  |  |  |
|  | c. The service life of the filter or cartridge. |  |  |  |
|  | d. All of the above. |  |  |  |

- Respirators are required when engineering controls are not able to lower exposures to permissible limits.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- You need to have training in respirator use:

|  | a. At least annually. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. If changes in operations mean that a different respirator is needed. |  |  |  |
|  | c. If you are not using the respirator correctly. |  |  |  |
|  | d. All of the above. |  |  |  |

- Each time you put on a respirator having a tight-fitting face piece, you must perform _________ seal checks.

|  | a. One |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Two |  |  |  |
|  | c. Three |  |  |  |
|  | d. None of the above. |  |  |  |

- There is no need to ensure that the engineering controls in your work area are functioning properly as long as you are wearing a tight-fitting respirator.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- If a respirator needs repairs:

|  | a. Only the manufacturer’s replacement parts can be used. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. You can use other parts as long as your supervisor approves them. |  |  |  |
|  | c. Either of the above. |  |  |  |
|  | d. None of the above. |  |  |  |

- Some of the medical signs and symptoms that may indicate that your respirator is ineffective are:

|  | a. Shortness of breath; dizziness; coughing. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Chest pain; wheezing. |  |  |  |
|  | c. Lung disease; cardiovascular or heart conditions. |  |  |  |
|  | d. None of the above. |  |  |  |
|  | e. a, b, and c. |  |  |  |

- Contaminants can be generated from direct handling of chemical containing products or as a by-product from regular operations.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

# Signature _______________________________ PR# ______________ Date ______________________

Instructor ___________________________________