## Slide 1: MSHA’s Final Respirable Dust Rules

## Slide 2: Major Sections Modified
Part 70 (Underground coal mines)
Part 71 (Surface coal mines/facilities)
Part 90 (Miners with lung disease)
Part 72 (Compliance determinations, Medical monitoring, Respiratory Protection)
Part 75 (Ventilation, Ventilation plan, Dust control examinations)

## Slide 3: Part 70 New Terms
Normal Production Shift
Representative Samples
Excessive Concentration Value (ECV)

## Slide 4: Part 70 - Standards
2.0 mg/m3 on effective date
1.5 mg/m3 24 months after effective date
Intake air
  1.0 mg/m3 on effective date
  0.5 mg/m3 24 months after effective date

## Slide 5: Part 70 Standards
Quartz
  Quartz standard 0.100 mg/m3 (100 µg/m3)
  Reduced standard established based on
    Exceeding 100 µg/m3
    Formula: 10 divided by percent quartz

## Slide 6: Part 70 Sampling General
CMDPSU for Designated Occupations (DO) and Designated Area (DA) sampling at effective date
CPDM 18 months after effective date for
  DO sampling
  Other Designated Occupations (ODO) sampling (former DAs on the MMU)
CMDPSU used for (DA) sampling unless operator notifies District Manager of use of CPDM (18 months after effective date) at least 90 days prior to intended use

## Slide 7: Part 70 Sampling General (Cont.)
Miners required to wear CPDM trained on unit prior to wearing and every 12 months
All sampling will be full-shift, portal-to-portal
  Change out of CMDPSU pump to complete full shift
  Change out of CPDM unit to complete full shift

## Slide 8: Part 70 Sampling General (Cont.)
Control filters required when sampling with CMDPSU
  Control filter must have same pre-weight date
  Carried to same area of mine as sample
  Remain plugged entire shift
  Transmitted with sample to MSHA
  Dust data card completed
  Certified person to handle

## Slide 9: Part 70 Sampling General (Cont.)
Operator record length of each shift – maintain record for 6 months
Operator record production for each MMU for each shift – maintain record 6 months
  Operator will use to determine average over the last 30 production shifts

## Slide 10: Part 70 Sampling Certification
Persons certified by MSHA to conduct sampling
Persons certified by MSHA to maintain and calibrate sampling units

## Slide 11: Part 70 Sampling Certification
Re-certified every 3 years
MSHA may revoke certification
Certified in sampling may collect samples
Certified in Maintenance can work on sampling units
  Maintenance certification not cover sampling duties

## Slide 12: Part 70 Sampling Pre-Shift Checks
Pre-shift CMDPSU within 3 hours of sample shift
  Examination of components
  Examination of cyclone interior
  Examination of external tubing
  Examination of clamping/positioning
  Testing of voltage under load

## Slide 13: Part 70 Sampling Pre-Shift Checks
Pre-shift of CPDM within 3 hours of sample shift
  Follow procedures required by manufacturer
  Pre-operational examination
  Testing
  Set-up

## Slide 14: Part 70 Flowrate
Operate at
  2.0 lit/min for CMDPSU
  2.2 lit/min for CPDM
  Other flowrate recommended by manufacturer or Sec. of Labor
CMDPSU checked during 2nd and last hour of operation
CPDM – examine unit at mid-shift or more often if specified in ventilation plan

## Slide 15: Part 70 Bimonthly Sampling – MMU (First 18 Months)
5 samples each bimonthly period on DO
  Consecutive normal production shifts
  Normal production shifts worked on consecutive days
Samples exceeding standard by 0.1 will be used in compliance/noncompliance decision regardless of production
New reduced standard due to quartz
  Standard effective 7 days after date of notification

## Slide 16: Part 70 Bimonthly Sampling – MMU Compliance
1 sample ≥ ECV in Table 70-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 17
TABLE 71-1 EXCESSIVE CONCENTRATION VALUES (ECV) BASED ON SINGLE, FULL-SHIFT CMDPSU/CPDM CONCENTRATION MEASUREMENTS |  | 
Applicable Standard (mg/m3) | ECV (mg/m3) | 
 | CMDPSU | CPDM
2.0 | 2.33 | 2.26
1.9 | 2.22 | 2.15
1.8 | 2.12 | 2.04
1.7 | 2.01 | 1.92
1.6 | 1.90 | 1.81
1.5 | 1.79 | 1.70
1.4 | 1.69 | 1.58
1.3 | 1.59 | 1.47
1.2 | 1.47 | 1.36
1.1 | 1.37 | 1.25
1.0 | 1.26 | 1.13
0.9 | 1.16 | 1.02
0.8 | 1.05 | 0.91
0.7 | 0.95 | 0.79
0.6 | 0.85 | 0.68
0.5 | 0.74 | 0.57
0.4 | 0.65 | 0.46
0.3 | 0.54 | 0.34
0.2 | 0.44 | 0.23

## Slide 18
TABLE 70-2 EXCESSIVE CONCENTRATION VALUES (ECV) BASED ON THE AVERAGE OF 5 OR 15 FULL-SHIFT CMDPSU/CPDM CONCENTRATION MEASUREMENTS |  |  |  |  |  | 
Applicable Standard | ECV (mg/m3) based on 5-Sample Average |  |  | ECV (mg/m3) based on 15-Sample Average |  | 
(mg/m3) | CMDPSU | CPDM |  | CMDPSU | CPDM | 
2.0 | 2.15 | 2.12 |  | 2.09 | 2.07 | 
1.9 | 2.05 | 2.01 |  | 1.99 | 1.97 | 
1.8 | 1.94 | 1.91 |  | 1.89 | 1.87 | 
1.7 | 1.84 | 1.80 |  | 1.78 | 1.76 | 
1.6 | 1.74 | 1.70 |  | 1.68 | 1.66 | 
1.5 | 1.63 | 1.59 |  | 1.58 | 1.56 | 
1.4 | 1.53 | 1.49 |  | 1.48 | 1.45 | 
1.3 | 1.43 | 1.38 |  | 1.38 | 1.35 | 
1.2 | 1.33 | 1.27 |  | 1.28 | 1.25 | 
1.1 | 1.22 | 1.17 |  | 1.17 | 1.14 | 
1.0 | 1.12 | 1.06 |  | 1.07 | 1.04 | 
0.9 | 1.02 | 0.96 |  | 0.97 | 0.94 | 
0.8 | 0.92 | 0.85 |  | 0.87 | 0.83 | 
0.7 | 0.81 | 0.75 |  | 0.77 | 0.73 | 
0.6 | 0.71 | 0.64 |  | 0.67 | 0.63 | 
0.5 | 0.61 | 0.53 |  | 0.57 | 0.52 | 
0.4 | 0.51 | 0.43 |  | 0.47 | 0.42 | 
0.3 | 0.41 | 0.32 |  | 0.37 | 0.32 | 
0.2 | 0.31 | 0.22 |  | 0.27 | 0.21 | 

## Slide 19: Part 70 Bimonthly Sampling – MMU Noncompliance
2 or more CMDPSU samples ≥ the Excessive Concentration Value (ECV) in Table 70-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 70-2

## Slide 20: Part 70 Bimonthly Sampling - MMU Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miners
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
  Within 8 calendar days after date of citation, sample consecutive shifts until 5 valid samples collected

## Slide 21: Part 70 Bimonthly Sampling - MMU Noncompliance (cont.)
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard
  Submit revised ventilation plan incorporating the corrective actions used
  Revised ventilation plan approved by DM

## Slide 22: Part 70 Bimonthly Sampling - DA
First 18 months after effective date
  One valid sample each bimonthly period
    If sample > applicable standard, collect 5 samples within 15 calendar days
    Must start first day there is a production shift after receipt of notification
  If standard changes due to quartz – new standard effective 7 calendar days after date of notification

## Slide 23: Part 70 Bimonthly Sampling – DA Compliance
1 sample ≥ ECV in Table 70-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 24: Part 70 Bimonthly Sampling – DA Noncompliance
2 or more CMDPSU samples ≥ the Excessive Concentration Value (ECV) in Table 70-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 70-2

## Slide 25: Part 70 Bimonthly Sampling - DA Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miners
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
  Within 8 calendar days after date of citation, sample consecutive shifts until 5 valid samples collected

## Slide 26: Part 70 Bimonthly Sampling - DA Noncompliance (cont.)
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard
  Submit revised ventilation plan incorporating the corrective actions used
  Revised ventilation plan approved by DM

## Slide 27: Part 70 Quarterly Sampling – MMU (after 18 Months)
Conducted with CPDM unless notified
Sample DO consecutive shifts until 15 valid samples collected
  Additional 15 shift groups may be required
    District Manager discretion
    Required if found not following approved ventilation plan

## Slide 28: Part 70 Quarterly Sampling - MMU
Sample ODOs (formerly DAs on MMU) consecutive shifts until 15 valid samples collected
  ODO sampling not start until DO sampling complete
  Different ODO types sampled over separate time period during quarter
    Example: RB sampled over 15 shifts after DO 15 shift sampling complete
    Example: SCs sampled over 15 shifts after the DO 15 shift sampling and the RB 15 shift sampling is complete

## Slide 29: Part 70 Quarterly Sampling - MMU (cont.)
DOs, ODOs to be sampled specified in rule
Other ODOs may be designated by the DM
New reduced standard due to quartz will be effective 7 calendar days after the date of notification
Samples exceeding applicable standard by 0.1 mg/m3 or more will be used regardless of production

## Slide 30: Part 70 Quarterly Sampling - MMU Compliance
For each sample ≥ ECV in Table 70-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 31: Part 70 Quarterly Sampling - MMU Noncompliance
3 or more CPDM samples ≥ the Excessive Concentration Value (ECV) in Table 70-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 70-2

## Slide 32: Part 70 Quarterly Sampling - MMU Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miners
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
  Within 8 calendar days after date of citation, sample consecutive shifts until collect 5 valid samples

## Slide 33: Part 70 Quarterly Sampling - MMU Noncompliance (cont.)
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard
  Submit revised ventilation plan incorporating the corrective actions used
  Revised ventilation plan approved by DM

## Slide 34: Part 70 Quarterly Sampling - DAs
After 18 months sample each DA 5 consecutive shifts each quarter
  No consecutive days cycle
Quartz present – resulting in reduced standard
  New standard effective 7 calendar days after date of notification

## Slide 35: Part 70 Quarterly Sampling - DA Compliance
For each sample ≥ ECV in Table 70-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 36: Part 70 Quarterly Sampling - DA Noncompliance
2 or more CPDM samples ≥ the Excessive Concentration Value (ECV) in Table 70-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 70-2

## Slide 37: Part 70 Quarterly Sampling - DA Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miners
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
  Within 8 calendar days after date of citation, sample consecutive shifts until collect 5 valid samples

## Slide 38: Part 70 Quarterly Sampling - DA Noncompliance (cont.)
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard
  Submit revised ventilation plan incorporating the corrective actions used
  Revised ventilation plan approved by DM

## Slide 39: Part 70 Transmission of Samples/Data
CMDPSU
  Transmit sample/control filter within 24 hours after end of sampling shift
  Data card completed and signed
  Not tamper with seal or alter weight
CPDM
  Mine official validate, certify and transmit electronically within 24 hours after end of sampling shift
    Sample data file
    Sample status conditions file
  Operator maintain data files at least 12 months
  Not tamper with CPDM or alter any data files

## Slide 40: Part 70 Report and Posting
CMDPSU
  MSHA provide report of sample results
  Report posted at least 31 days
CPDM
  End-of-shift sample results – operator post within 12 hours after end of sampling shift
  Information remain posted until receipt of MSHA provided samples report
  MSHA sample results report posted at least 31 days

## Slide 41: Part 70 Status Changes
Change in operational status of sampling entity reported within 3 days
  In writing or electronically

## Slide 42: Part 72 – 72.100 Medical Monitoring
Chest X-rays and spirometry examinations for all coal miners (Surface and Underground)
  Must use NIOSH approved facility
  Provided at frequency of at least 5 years (Voluntary)
  New miners – within 30 days of first work (Mandatory)
  Operators to develop plan for examinations
    Plan must be approved by NIOSH
    Plan submittal must include a roster of employees
  Approved plan posted on mine bulletin board at all times

## Slide 43: Part 72 – 72.700 Respiratory Equipment
Operators make available NIOSH approved respirators as required by Parts 70, 71 and 90
Respirator training when required by 70, 71 and 90
  Provided prior to the miners’ next scheduled shift
  Cover: care, fit, use and limitations of each type made available
  Maintain record of training for at least 2 years
    Includes name, date and subjects covered
Respirator not a substitute for environmental controls

## Slide 44: Part 72 – 72.800 Single Sample Determinations
Secretary will use a single, full-shift sample to determine compliance/noncompliance with respirable dust standards
  Sample meets or exceeds ECV in Table 70-1, 71-1 or 90-1
Citation for meeting or exceeding the ECV associated with the applicable standard will be terminated as specified in Parts 70, 71 and 90.

## Slide 45: Part 75 – 75.325 Air quantity
Air measurements must be taken at the end of the face ventilating device with a scrubber (if used) turned off

## Slide 46: Part 75 – 75.350 Belt Air Course Ventilation
Respirable dust standard remains at 1.0 mg/m3 on effective date of rule
Standard reduced to 0.5 mg/m3 24 months after effective date of rule
If a reduced standard is applicable on the working section that is less than the 1.0 mg/m3 or 0.5 mg/m3 standard, then the lowest applicable standard applies to the belt entry

## Slide 47: Part 75 – 75.362 (a)(2) On-shift Examinations
Examination to assure compliance with respirable dust controls in plan
  Within 1 hour of shift change if there is no break in production
  Prior to resuming production if there is a break in production at shift change
Deficiencies corrected prior to production beginning or resuming

## Slide 48: Part 75 – 75.362 (a)(2) On-shift Examinations
Examination includes:
  Air quantities and velocities
  Water pressures & flow rate
  Excessive leakage in water delivery system
  Water spray number and orientation
  Section ventilation & control placement
  Roof bolter dust collector vacuum
  Scrubber air flow rate
  Work practices in plan
  Any other dust suppression measures

## Slide 49: Part 75 – 75.362 (g)(2) On-shift Examinations
Examination and corrective actions must be recorded
Certification of exam (date, time, initials) to be recorded on a board maintained on the MMU so that miners can see that controls were checked
Record of exam verified and counter signed in a secure book
  Certified person verify record in book by initials and date by the end of the shift exam conducted
  Mine foreman or equivalent countersign after verified by certified person – no later than end of next scheduled work shift
Record book retained at least 1 year

## Slide 50: Part 75 – 75.371(f) & (j) Mine Ventilation Plan; Contents
Minimum quantity of air each MMU
Description of each different dust system on equipment
Specific details of dust controls on each MMU:
  Water spray information
  Maximum ventilation device from working face
  Maintenance of roof bolter dust collector
  Work practices for equipment operators
Specify type and size of scrubber screen
Description of maintenance procedures for dust collectors on equipment

## Slide 51: Part 71 New Terms
Normal Work Shift
Representative Samples
Excessive Concentration Value (ECV)

## Slide 52: Part 71 Standards
2.0 mg/m3 on effective date
1.5 mg/m3 24 months after effective date

## Slide 53: Part 71 Standards
Quartz
  Quartz standard 0.100 mg/m3 (100 µg/m3)
  Reduced standard established based on
    Exceeding 100 µg/m3
    Formula: 10 divided by percent quartz

## Slide 54: Part 71 Sampling General
All sampling will be full-shift
Control filters required when sampling with CMDPSU
Miners required to wear CPDM trained on unit prior to wearing and every 12 months
Operator record length of each shift – maintain record for 6 months

## Slide 55: Part 71 Sampling General (Cont.)
Control filters required when sampling with CMDPSU
  Control filter must have same pre-weight date
  Carried to same area of mine as sample
  Remain plugged entire shift
  Transmitted with sample to MSHA
  Dust data card completed
  Certified person to handle

## Slide 56: Part 71 Certification
Persons certified by MSHA to conduct sampling
Persons certified by MSHA to maintain and calibrate sampling units

## Slide 57: Part 71 Certification
Re-certified every 3 years
MSHA may revoke certification
Certified in sampling may collect samples
Certified in Maintenance can work on sampling units
  Maintenance certification not cover sampling duties

## Slide 58: Part 71 Pre-Shift Checks
Pre-shift CMDPSU within 3 hours of sample shift
  Examination of components
  Examination of cyclone interior
  Examination of external tubing
  Examination of clamping/positioning
  Testing of voltage under load

## Slide 59: Part 71 Pre-Shift Checks
Pre-shift of CPDM within 3 hours of sample shift
  Follow procedures required by manufacturer
  Pre-operational examination
  Testing
  Set-up

## Slide 60: Part 71 Flowrate
Operate at
  2.0 lit/min for CMDPSU
  2.2 lit/min for CPDM
  Other flowrate recommended by manufacturer or Sec. of Labor
CMDPSU checked during 2nd and last hour of operation
CPDM – examine unit at mid-shift or more often if specified in dust control plan

## Slide 61: Part 71 DWP Sampling
1 Sample each quarter
Specific work positions required to be sampled
  Each highwall drill operator
  Bulldozer operators
  Other positions designated by the DM

## Slide 62: Part 71 DWP Sampling (cont.)
Mines with multiple work positions in bulldozer and other work positions
  Sample as the DWP, the position with greatest exposure performing activity/task in same location exposed to same dust generation source
Identify work positions to DM
  Within 60 days after the effective date of rule for current active mines
  Within 30 calendar days of new mine being activated
  Within 7 days of operational status change

## Slide 63: Part 71 Sampling General
Samples collected on normal work shift
Any sample exceeding standard by 0.1 mg/m3 or more used to determine compliance
DWP samples collected on equipment operator or within 36 inches
Non-equipment operator: on the miner at the location with highest dust exposure

## Slide 64: Part 71 Sampling General
DM may designate additional DWPs based on MSHA sampling
  Work position exceeds 50% of the standard
  Work position placed on a reduced standard due to quartz – exceeds 50% of the reduced standard
DM may withdraw DWP from sampling
  Applicable only to those additional DWPs established by the DM
  No highwall drill or bulldozer DWP can be withdrawn from sampling
DWP quartz
  New standard effective 7 days after date of notification

## Slide 65: Part 71 Exceed Standard
If the one representative quarterly sample exceeds the applicable standard
  Sample DWP each normal shift until 5 valid representative samples taken
  Begin sampling first normal work shift after notification
  Five samples used to determine compliance for sampling period

## Slide 66: Part 71 Quarterly Sampling - DWP Compliance
For each sample ≥ ECV in Table 71-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 67: Part 71 Quarterly Sampling - DWP Noncompliance
2 or more samples ≥ the Excessive Concentration Value (ECV) in Table 71-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 71-2

## Slide 68: Part 71 Quarterly Sampling - DWP Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miners
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
  Within 8 calendar days after date of citation, sample consecutive shifts until collect 5 valid samples

## Slide 69: Part 71 Quarterly Sampling - DWP Noncompliance (cont.)
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard

## Slide 70: Part 71 Transmission of Samples/Data
CMDPSU
  Transmit sample/control filter within 24 hours
  Data card completed and signed
    Certified person who performed sample shift checks
  Not tamper with seal or alter weight
CPDM
  Certified person sampling must validate, certify and transmit electronically within 24 hours after end of sampling shift
    Sample data file
    Sample status conditions file
  Operator maintain data files at least 12 months
  Not tamper with CPDM or alter any data file

## Slide 71: Part 71 Report and Posting
CMDPSU
  MSHA provide report of sample results
  Report posted at least 31 days
CPDM
  End-of-shift sample results – operator post within 12 hours after end of sampling shift
  Information remain posted until receipt of MSHA provided samples report
  MSHA sample results report posted at least 31 days

## Slide 72: Part 71 Status Changes
Change in operational status of sampling entity reported within 3 days
  In writing or electronically

## Slide 73: Part 71 – 71.300 Respirable Dust Control Plan
Plan required for a DWP within 15 days after termination date of citation for excessive dust
Provisions for comments from representative of miners
  Operator notify representative of miners 5 days prior to submission, provide copy if requested
  Copy of proposed plan or revision available for inspection by representative
  Representative may submit comments
Copy of proposed plan or revision posted on mine bulletin board
Specific information on DWP and controls used

## Slide 74: Part 71 – 71.301 DWP Plan Approval
Approved on a mine-by-mine basis
Controls likely to maintain dust levels
Provisions can be objectively determined
Approved plan made available to representative of miners
  Copy to representative upon request
  Available for inspection by representative
  Posted on mine bulletin board while in effect

## Slide 75: Part 90
Applies to all coal miners – miners working at underground coal mines, surface coal mines or surface coal facilities

## Slide 76: Part 90 New Terms
Normal Work Shift
Representative Samples
Excessive Concentration Value (ECV)

## Slide 77: Part 90 Standard
1.0 mg/m3 standard on effective date of rule
0.5 mg/m3 24 months after effective date of rule

## Slide 78: Part 90 Standard
Quartz
  Quartz standard 0.100 mg/m3 (100 µg/m3)
  Reduced standard established based on
    Exceeding 100 µg/m3
    Formula: 10 divided by percent quartz
      No standard greater than the base standard for Part 90

## Slide 79: Part 90 Transfer
Existing position on same shift
Different mine, shift or newly created position if miner agrees in writing
Operator required to notify MSHA of any transfer

## Slide 80: Part 90 Compensation
Not less than rate of pay prior to exercising option
Wage increases accrued to the position transferred to

## Slide 81: Part 90 Waiver/Re-exercise
Miner may waive rights under Part 90
Miner may re-exercise Part 90 rights at any time

## Slide 82: Part 90 Sampling General (cont.)
CMDPSU used for sampling on effective date of rule
CPDM used for sampling 18 months after effective date of rule

## Slide 83: Part 90 Sampling General (cont.)
Miners required to wear CPDM trained on unit prior to wearing and every 12 months
All sampling will be full-shift, portal-to-portal
  Change out of CMDPSU pump to complete full shift
  Change out of CPDM unit to complete full shift

## Slide 84: Part 90 Sampling General (cont.)
Control filters required when sampling with CMDPSU
  Control filter must have same pre-weight date
  Carried to same area of mine as sample
  Remain plugged entire shift
  Transmitted with sample to MSHA
  Dust data card completed
  Certified person to handle

## Slide 85: Part 90 Sampling General (cont.)
Operator must record the length of each shift that Part 90 miner works

## Slide 86: Part 90 Certifications
Persons certified by MSHA to conduct sampling
Persons certified by MSHA to maintain and calibrate sampling units

## Slide 87: Part 90 Certifications
Re-certified every 3 years
MSHA may revoke certification
Certified in sampling may collect samples
Certified in Maintenance can work on sampling units
  Maintenance certification not cover sampling duties

## Slide 88: Part 90 Sampling Pre-Shift Checks
Pre-shift CMDPSU within 3 hours of shift
  Examination of components
  Examination of cyclone interior
  Examination of external tubing
  Examination of clamping/positioning
  Testing of voltage under load

## Slide 89: Part 90 Sampling Pre-Shift Checks
Pre-shift of CPDM
  Follow procedures required by manufacturer
  Pre-operational examination
  Testing
  Set-up

## Slide 90: Part 90 Flowrate
Operate at
  2.0 lit/min for CMDPSU
  2.2 lit/min for CPDM
  Other flowrate recommended by manufacturer or Sec. of Labor
CMDPSU checked during 2nd and last hour of operation
CPDM – examine unit at mid-shift or more often if specified in respirable dust control plan

## Slide 91: Part 90 Transfer Sampling
5 samples within 15 days after:
  20 day grace period
  Implementing a transfer after the 20 day grace period

## Slide 92: Part 90 Compliance Sampling
5 samples each quarter
  Consecutive work days
New reduced standard due to quartz
  Standard effective 7 days after date of notification

## Slide 93: Part 90 Sampling Compliance
1 sample ≥ ECV in Table 90-1
  Make respirators available
  Immediately take corrective action to lower to or below applicable standard
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year

## Slide 94: Part 90 Noncompliance
2 or more samples ≥ the Excessive Concentration Value (ECV) in Table 90-1 or
Average of all samples collected during a sampling period ≥ the ECV in Table 90-2

## Slide 95: Part 90 Noncompliance
Citation for excessive dust issued – sequential actions to be taken:
  Respirators available to affected miner
  Immediately take corrective actions to lower to or below applicable standard
    If corrective actions involve reducing dust levels:
      Implement corrective actions
      Within 8 calendar days after date of citation, sample until 5 valid samples collected
    If transferring Part 90 miner:
      Comply with transfer requirements (90.102)
      Within 15 calendar days after date of transfer, sample until 5 valid samples collected

## Slide 96: Part 90 Noncompliance (Cont.)
  Make record of corrective action
    Certify by mine foreman or equivalent
    In secure book
    Maintained at mine for at least 1 year
Citation terminated after
  Equivalent concentration of each of the 5 valid samples ≤ applicable standard

## Slide 97: Part 90 Transmission of Samples/Data
CMDPSU
  Transmit sample/control filter within 24 hours after end of shift
  Data card completed and signed
  Not tamper with seal or alter weight
CPDM
  Certified person sampling must validate, certify and transmit electronically within 24 hours after end of sampling shift
    Sample data file
    Sample status conditions file
  Operator maintain data files at least 12 months
  Not tamper with CPDM or alter any data files

## Slide 98: Part 90 Report and Posting
CMDPSU
  MSHA provide report of sample results
  Operator provide copy of report to Part 90 miner
  Do NOT post report
CPDM
  Certified person in sampling shall provide to each Part 90 miner a paper record (dust data card) of sample run signed by certified person within first hour next work shift
  Operator shall NOT post sample information

## Slide 99: Part 90 Status Changes
Change in status of Part 90 miner reported within 3 days
  In writing or electronically

## Slide 100: Part 90 Respirable Dust Control Plan Filing
Plan required for a Part 90 miner after citation for excessive dust if operator elected to reduce dust exposure by reducing the dust level in current position
Include MIIN of Part 90 and specific details of controls
Specific information on how control measures will continue to be used

## Slide 101: Part 90 Respirable Dust Control Plan Approval
Approved on a mine-by-mine basis
Controls likely to maintain dust levels
Provisions can be objectively determined
Approved plan provided to Part 90 miner
Approved plan NOT posted on mine bulletin board
Operator may submit revisions for DM approval