## Slide 1: EXTENSION CORD SAFETY

## Slide 2
JUST A FEW STATISTICS
EMERGENCY ROOMS REPORT 4,000 INJURIES YEARLY ASSOCIATED WITH EXTENSION CORDS.
50% INVOLVE FRACTURES, LACERATIONS AND CONTUSIONS FROM TRIPPING.
13% INVOLVE SMALL CHILDREN UNDER 5 YEARS OF AGE
½ OF THE 13% INVOLVING CHILDREN ARE BURNS TO THE MOUTH.

## Slide 3
OVERLOADED, WORN, OR DAMAGED CORDS MAY CAUSE A FIRE
CORD LENGTH | GAUGE | MAX AMPS |  | CORD LENGTH | GAUGE | MAX AMPS
25’ | 18 | 10 |  | 25’ | 16 | 13
50’ | 18 | 5 |  | 50’ | 16 | 10
75’ | 18 | 5 |  | 75’ | 16 | 10
25’ | 14 | 15 |  | 100’ | 16 | 5
50’ | 14 | 15 |  | 100’ | 12 | 15
75’ | 14 | 15 |  | 150’ | 12 | 13

## Slide 4
EXTENSION CORD SAFETY TIPS
USE ONLY WHEN NECESSARY AND ON A TEMPORARY BASIS
DO NOT LET CORDS DANGLE FROM COUNTERS OR TABLES
REPLACE WORN OR CRACKED CORDS
INSERT PLUGS FULLY SO THAT NO PART OF THE PRONG IS EXPOSED
WHEN DISCONNECTING, PULL FROM THE PLUG END, NOT THE CORD
TEACH CHILDREN NOT TO PLAY WITH EXTENSION CORDS AND BUY PLASTIC END CAPS
DO NOT USE STAPLES OR NAILS TO SECURE EXTENSION CORDS
USE OUTSIDE RATED CORDS FOR ALL OUTSIDE USES
USE ONLY 3 PRONG CORDS FOR 3 PRONGED APPLIANCES, NEVER REMOVE THE U-GROUND
Notes: LEAVING EXTENSION CORDS IN SERVICE OVER TIME DOSE NOT ALLOW TO INSPECTION OR ANY THOUGHT OF MAINT.
CORDS DANGLEING ARE A FAVORITE TARGET FOR CHILDREN, PETS AND DRUNKS
EXPOSED CONDUCTORS MAY CAUSE SHOCK, ALSO IT IS A GOOD IDEA TO BUY PLASTIC BLANKS FOR ALL OUTLETS
PULLING FROM THE CORD MAY CAUSE DAMAGE, SHORT CIRCUIT OR FIRE
AND WHILE YOUR AT IT, TEACH THEM ABOUT THE DANGERS OF ELECTRICITY, OUTLETS ETC,
HOW MANY TIMES HAVE YOU STAPLED THROUGHT A STRAND OF CHRISTMAS LIGHTS?
IF YOU ARE GOING TO USE EXTENSION CORDS OUTSIDE, MAKE SURE THEY ARE RATED FOR OUTSIDE, THE LOAD AND I WOULD STRONGLY SUGGEST EITHER HAVING THEM PLUGGED INTO A GFCI PROTECTED OUTLET OR USE A GFCI PIGTAIL. HERE AT WORK, YOU SHOULD USE A GFCI PIGTAIL, IF YOU DON’T HAVE ONE, I HAVE A FEW AND WE CAN ORDER WHAT YOU NEED.
THAT LITTLE GROUNDING PRONG WAS NOT THERE JUST TO GET YOU UPSET THAT IT WONT FIT INTO AN OLD WALL RECEPTICAL, IT IS THERE TO SAVE YOUR LIFE.