## Slide 1: Noise Levels
Guess the decibel Level!

## Slide 2: Hearing Protection Policy
Ear plugs and/or muffs will be worn whenever personnel may be exposed to excessive noise levels as determined and designated by the Safety & Health Services Department
Hearing protection is required at 85 dBA
Dual hearing protection is required at 105 dBA
Do not do the task if the level exceeds 115 dBA

## Slide 3: Exposure Time Limits: Without Hearing Protection

## Slide 4: What is the decibel level of our everyday tools
Air Hammer
107.1 dBA

## Slide 5
Needle Gun
With Chisel
100.8 dBA

## Slide 6
Air Arc
114.7 dBA

## Slide 7
102.0 dBA
½”
3/8”
Impact Wrenches
101.0 dBA
¾”
1”
110.8 dBA
105.5 dBA
Wide open rev
115.0

## Slide 8
Air Die Grinder
88.7 dBA
Right Angle Grinder
88.6 dBA

## Slide 9
Air Drill
98.8 dBA

## Slide 10
89.3 dBA
In the Cab
115.7 dBA
Stay in the Cab
Load Boxing a Haul Truck
On the Deck
104.5 dBA
On the Ground

## Slide 11
Sledge Hammer on Metal Pin
99.1 dBA

## Slide 12
Shop Vacuum
88.3 dBA

## Slide 13
Tire Shop Tools
98.6-94.6 dBA
Tire De-Air System
99.2 dBA
Using a grinder inside of a truck tire

## Slide 14
Tire Shop Tools
114.6 dBA
¾” Impact on wheel motor
88.3- 91.8 dBA
Tire Changer

## Slide 15
Too loud and is under investgation to find a safer way
Bead Seater

## Slide 16
Ipod at full blast
120 dBA

## Slide 17
Distance and barriers
from the source
changes the decibel level

## Slide 18
Some Approved
Hearing Protection

## Slide 19
Questions?