## Slide 1: Ladder Safety Training

## Slide 2: Agenda
Awareness/Statistics
General Condition
Duty Rating
Proper Use
Proper Ladder Length

## Slide 3
Awareness/Statistics

## Slide 4: Did You Know?
4,609 fatal work incidents in 2011
666 were the result of a falls, slips, or trips
  Roughly 7%
Falls rank 2nd
  behind automobile accidents
Roughly 1 out of 4 took place at 10 feet or less.

## Slide 5: Questions to ask yourself
What potential hazards exist in the areas I will be using a ladder?
How do I know if a ladder is strong enough to carry my weight?
What ladder is best for the job I’m doing?
How can I be sure a ladder is in good working condition?

## Slide 6
General Condition

## Slide 7: General Condition Wood Ladders
  Constructed of a high-density wood
  Free of sharp edges and splinters
  No decay, or irregularities
  Rungs not broken, in good condition

## Slide 8: General Condition Metal Ladders
  Free of sharp edges and are structurally sound
  Must have rungs that are knurled, dimpled or treated to improve slip resistance

## Slide 9: General Condition Fiberglass Ladders
  OSHA does not address fiberglass ladders.
  ANSI guidelines
    Should be made of good, commercial-grade, thermosetting polyester resin reinforced with glass fibers.

## Slide 11: Storage and Maintenance
Proper storage and maintenance will extend the life of a ladder and ensure its safety.
Extension ladders should be hung horizontally and supported every six feet.
All ladders should be stored in a well-ventilated area away from extreme heat and cold
Do not store items on top of ladder.

## Slide 12: Storage and Maintenance
Clean and lubricate the ladder’s moving parts.
Keep the rungs and steps free of oil and dirt.
Wood ladders can be treated with a protective coating but must not be painted. Paint will cover defects.
When transporting a on a vehicle, make sure both ends are secure to prevent road shock that could damage the ladder.

## Slide 13
Duty Rating

## Slide 14: Duty Rating
Your weight +
Weight of PPE +
Weight of tool belt +
Weight of other supplies or tools brought up the ladder
Determine “Your” Weight Capacity
Total Weight
200 lbs 225 lbs 250 lbs 300 lbs
Type 3 Type 2 Type 1 Type 1a

## Slide 15: Duty Rating
175 lb employee +
5 lbs of tools +
30 lb sign
210 lbs total
Type 2 ladder
Your Weight +
Weight of Tools+
Weight of sign
Total Weight
Type of Ladder

## Slide 16
Proper Ladder Length

## Slide 17: Proper Ladder Length
20 feet
5 feet
The bottom of the ladder must be one foot away from the wall for every four feet of the building’s height to the point where the ladder rests against it. The further distance the ladder is from the base of the building, the longer the ladder must be to reach the same height.
A² + B² = C²

## Slide 18: Proper Ladder Length
20 feet
5 feet
The bottom of the ladder must be one foot away from the wall for every four feet of the building’s height to the point where the ladder rests against it. The further distance the ladder is from the base of the building, the longer the ladder must be to reach the same height.
A² + B² = C²
21feet

## Slide 19: Proper Ladder Length
3 feet
The ladder must extend 3 feet beyond the roof line if you are going to climb onto the structure

## Slide 20: Proper Ladder Length
1/12
The fly and the base sections must overlap approximately 1/12 of the total working height of the ladder.

## Slide 21: How much ladder is needed?
3 feet
3 feet
8 feet
32 feet
33 feet
A² + B² = C²
39 Feet

## Slide 22
Proper Use

## Slide 23: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.

## Slide 24: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.

## Slide 25: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.

## Slide 26: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.
Ladders must not be placed on boxes, barrels or other unstable bases to obtain additional height.

## Slide 27: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.
Ladders must not be placed on boxes, barrels or other unstable bases to obtain additional height.

## Slide 28: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.
Ladders must not be placed on boxes, barrels or other unstable bases to obtain additional height.
Do not place ladders in front of door openings toward the ladder unless the door is blocked, locked or guarded.

## Slide 29: Proper Use
Ladders must be placed to prevent slipping, or they should be lashed or held in position.
Ladders must not be used for anything other than their intended purpose.
Ladders must not be placed on boxes, barrels or other unstable bases to obtain additional height.
Do not place ladders in front of door openings toward the ladder unless the door is blocked, locked or guarded.

## Slide 30: Proper Use
Duty Rating

## Slide 31
Questions?