2011 Northern Mine Rescue

Written Test – Field Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

- The specific gravity of normal air is:

- 0.01

- 1.1

- 0.001

- 1.0

- None of the above.

- A fresh air base is usually established at the point where conditions no longer permit barefaced exploration.

- True

- False

- If the mine has a manager as well as a superintendent, the superintendent usually carries full responsibility for the rescue and recovery operation.

- True

- False

- __________ fires involve combustible metals such as magnesium, titanium, zirconium, sodium, and potassium.

- Class A

- Class B

- Class C

- Class D

- None of the above

- __________ is a mixture of carbon monoxide and air which results from a mine fire.

- Afterdamp

- Firedamp

- Whitedamp

- Blackdamp

- The captain of the mine rescue team determines whether or not to alter ventilation.

- True

- False

- Factors that influence body deterioration are:

- Air temperature

- Body Size

- Body Fluid

- All of the above

- A _________ is a large hinged door used to close off a mine passage.

- Man door

- Mine door

- Regulator

- None of the above

- The explosive range of butane is:

- 4.0 to 74.2%

- 2.12 to 9.35%

- 1.86 to 8.41%

- 5 to 15%

- None of the above

- To operate a wheeled extinguisher, you must first open the valve on the nitrogen cylinder.

- True

- False

- One of the main factors governing the time for unsealing a fire area is the effect of barometric pressure on the enclosed area.

- True

- False

- ______________ is a mixture of carbon dioxide, nitrogen, and air.

- Stinkdamp

- Firedamp

- Afterdamp

- Blackdamp

- As the team advances through the mine during exploration, the command center only needs to be told the type of damage found.

A.   True

B.   False

- ___________ is a second priority condition.

A.  Multiple fractures

B.  Abrasions

C.  Moderate shock

D.  Chest injuries

E.  A and C

- Team members should not drink alcoholic beverages for at least ________ hours before getting under oxygen.

  - 8 to 10

  - 24

  - 12 to 18

  - 6

  - None of the above

- A main cause of oxygen deficiency in a mine is:

A.  Insufficient ventilation

B.  Displacement by other gases

C.  A fire or explosion

D.  Consumption by workers

E.  All of the above

- It is the duty of the mine supervisor to alert adjoining mines if they are connected underground with the affected mine.

A.  True

B.  False

- The team captain must make sure that each team member’s apparatus has been properly repaired and tested after arriving at the fresh air base.

A.  True

B.  False

- __________ ventilation is the most common method of recovery in multi-level mines.

A.  Direct

B.  Progressive

C.  Indirect

D.  Automatic

E.  None of the above

- Ethane, propane, and butane gases collect in low areas of a mine.

A.  True

B.  False

- The location of personal items, such as a lunch bucket, only needs to be marked on the side of the mine near where they are found.

A.  True

B.  False

- _________ has the odor and taste of blasting powder fumes.

A.  Carbon dioxide

B.  Nitrogen Dioxide

C.  Sulfur Dioxide

D.  Radon

E.  None of the above

- The difference in pressure within and without a sealed area usually described as “breathing in” means:

A.  Positive pressure in sealed area

B.  Negative pressure in sealed area

C.  Positive pressure outside sealed area

D.  Negative pressure outside sealed area

E.  None of the above

- __________ is highly soluble in water.

A.  Oxygen

B.  Nitrogen

C.  Carbon Monoxide

D.  Radon

E.  None of the above

- Only Federal officials can establish a command center and oversee all aspects of a rescue and recovery operation.

A.  True

B.  False

- The most accurate method of determining air velocity with smoke tubes is to take readings at quarter points within the airway.

A.  True

B.  False

- _________ determines how quickly a gas will diffuse or disperse.

A.  Specific gravity

B.  Temperature

C.  Atmospheric pressure

D.  A and C

E.  All of the above

- __________ is the process by which a team systematically explores all crosscuts and adjacent entries as they advance so they are never forward of an unexplored area.

A.  Cross checking

B.  Tying in

C.  Traveling

D.  Pacing

E.  None of the above

- Oxygen deficiency causes tightness in forehead, headaches, and dizziness at __________.

  - 14%

  - 13%

  - 15%

  - 9%

- The more obese an individual is; the quicker rigor mortis will develop.

A.  True

B.  False