Mine Rescue Team # ____________________

Team Name ___________________________

Your Name ____________________________

- _______

- _______

- _______

- _______

- _______

- _______

- _______

- _______

- _______

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

- _____

Colorado State Metal and Nonmetal

Mine Rescue, First Aid & Team Technician Contest

Idaho Springs, Colorado

July 12th, 13th, & 14th 2011

- MSHA requires Periodic Maintenance should be performed at least __________ on Mine Rescue Breathing Apparatus.

  - Daily

  - Weekly

  - Every 30 days

  - Quarterly

- In a properly working positive pressure NIOSH/MSHA approved Closed Circuit breathing apparatus the pressure inside the breathing loop/circuit is:

  - Lower than ambient

  - The same as ambient

  - The same as cylinder pressure

  - Slightly higher than ambient

- If a slight leak occurs in the breathing loop/circuit or facemask seal, the user generally will:

  - Hit the demand valve more often

  - Reduce duration

  - Increase oxygen consumption

  - All of the Above

  - None of the Above

- Under extremely heavy work conditions, if the user inhales and collapses the diaphragm as far as it can travel, it activates the;

  - By-Pass Valve

  - Demand Valve

  - Relief Valve

  - Check Valve

- What specifically controls the directional flow of the breathing gasses:

  - The hoses

  - The mask

  - The breathing bag or chamber

  - The CO2 scrubber/absorber

  - The check valves

- The function of the regulator is to:

  - Increase cylinder pressure in the apparatus

  - Moisture control

  - Decrease cylinder pressure in the apparatus plumbing and pneumatics

  - A & C

- If you hear the Demand every time you inhale, and you are not working hard, you should:

  - Use the Emergency By-Pass Valve

  - Breathe slower

  - Turn off the oxygen cylinder

  - Check your facemask fit and adjust it for a better seal

- The approved NIOSH/MSHA and manufacturer rated duration of my Closed Circuit Breathing Apparatus is:

  - 1-Hour

  - 2-Hours

  - Variable

  - 3-Hours

  - 4-hours

- Symptoms of breathing higher than normal levels of  CO2 may be:

  - Increased breathing rate

  - Headache, Dizziness, Light headed

  - Singing

  - Hunger

  - A & B

- If after removing my apparatus I leave the oxygen cylinder open, which valve will be wide open and  deplete the left over oxygen supplies:

  - Demand valve

  - Emergency Bypass valve

  - Relief valve

  - None of the Above

- When installing or filling CO2 absorption material into my apparatus  it is important to:

  - Follow the manufacturer’s instructions

  - Inspect the packaging for expiration date

  - Properly seal the apparatus from ambient air

  - Properly dry the material so it can be reused

  - All EXCEPT D

- When installing my pressurized oxygen cylinder in a ready to go apparatus, caution should be used to ensure:

  - Oils from my fingers and hands do not get on the valve

  - The cylinder and valve are clean

  - It is filled with the correct gas

  - It is pressurized to the correct amount

  - All the above

- A small leak in the breathing circuit/loop will cause the ____________ valve to open frequently.

  - Relief/Vent

  - Demand

  - Bypass

  - None of the Above

- If Positive Pressure could be attributed to ONLY ONE component in the apparatus what would it be:

  - The spring(s)

  - The breathing chamber or breathing bag

  - Oxygen pressure

  - Bypass valve

- Manual overuse of the __________ will significantly reduce the duration of the apparatus.

  - Relief/Vent valve

  - Purge valve

  - On/Off Valve

  - Emergency Bypass

- The functional bump test is intended to be a measure of the accuracy of the instrument.

  - True

  - False

- The Industrial Scientific Corporation iTX and the iBrid gas instruments have an operating temperature range from 20 °F to 116 °F.

  - True

  - False

- Industrial Scientific recommends that a full instrument calibration be performed using certified concentration(s) of Industrial Scientific branded calibration gas(es) _______ to ensure maximum accuracy.

  - Daily

  - Weekly

  - Monthly

  - None of the above

- If there is an oxygen sensor installed in the instrument, it is calibrated during the zeroing operation.

  - True

  - False

- The range for an Oxygen (O2) sensor is 0% to 25%.

  - True

  - False

- During calibration, what is the recommended flow rate for both the iTX and the iBrid?

  - 1.5 liter per minute (LPM)

  - 2.0 liter per minute (LPM)

  - 3.0 liter per minute (LPM)

  - None of the above

- Marginal calibration occurs if the (gas) sensor's full span value or span reserve is between 40% to 60% of the applied (calibration) gas value concentration.

  - True

  - False

- Both the iTX and the iBrid gas instruments can accept zinc-ion battery types.

  - True

  - False

- All over-range conditions will clear automatically when the gas concentration has decreased to a level within the display range of the gas instrument in non-latching mode.

  - True

  - False

- Prior to entering the normal GAS READING mode during start-up, the gas instrument will display all installed sensor types.

  - True

  - False

- The specific gravity of nitrogen dioxide is;

  - 1.5894

  - 1.5291

  - 1.1054

  - 1.1906

- Although smoke may irritate your lungs when you inhale it, it is not normally considered to be an asphyxiant.

  - True

  - False

- Blackdamp is a mixture of carbon monoxide and air which results from a mine fire.

  - True

  - False

- The smoke tube is used to show the direction and velocity of slow-moving air (below __________ feet per minute).

  - 100

  - 110

  - 120

  - 130

  - 210

- The pitot tube has a J-tube water gauge or some other differential pressure gauge for determining the velocity pressure inside the duct or tubing.

  - True

  - False

Bonus Question worth Zero points

A __________________ is a unit made up of a group of individuals working towards a common goal.