Date of Examination			Time From:		AM/PM  To:			AM/PM

Section/Area			       Reported Outside?   Yes	 No	  Time:			AM/PM

Reported By:				  Received By:			  INITIAL (AUTHORIZED PERSON)

Preshift required within 3 hours prior to any 8-hour interval.

| Location | Hazardous Condition | CH4 | Action Taken |
| --- | --- | --- | --- |
| #1 Entry | Powder mag. By pump cable |  | Pump cable de-energized |
| #1 Entry | Non-permissible 110 v pump |  | Pump de-energized |
| #1 Entry | No fire extinguisher at pump | 0.0% | Pump de-energized |
| #1 Entry | 3 sticks of powder |  | Moved to powder mag. |
| #1 Entry | Over Knee deep water in return |  | Dangered and Reported |
| Entry #1 Face | Vent device too far back | 0.0% | Advanced vent device |
| #2 Entry | AMS sensor back to far for belt air |  | Moved sensor |
| #2 Entry | Life line back from T.P. | 0.0% | Advanced up |
| #2 Entry | Rock dust pod blocking escapeway |  | Dangered and reported |
| #2 Entry face |  | 0.0% |  |
| Entry #2 to #3, XC #2 | Check curtain |  | Dangered and reported |
| Entry #2 to #3, XC #1 | No balls on life line for door |  | Dangered and reported |
| #3 Entry | Roof bolter bolting no air |  | Installed line curtain |
| Power Center | Only 5 lb. ext. at Pwr. Center | 0.0% | Added 5 lb. extingusher |
| Entry #3 face | **Gas reading | 0.0% |  |

Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOX | 26560 |  |  |

Velocities

Longwall Headgate:  			  				Longwall Tailgate:

CH4:		  O2:

Remarks:

Signed by Preshift Certified Examiner		      Date					     Certification Number

Countersigned by Mine Foreman		      Date					     Certification Number

Countersigned by Operator/Agent		      Date					     Certification Number