Written Field Test

2012 Nevada Regional Contest

March 14-15, 2012

Winnemucca, NV

Name __________________________  Company ____________________________

Team Name ____________________   Contest Position No. __________________

Team Member No. ______________

Instructions:  Please select your answer by circling the letter next to it.  If you make a mistake please fully erase your circle.

- A gas detector that is used for mine rescue must measure at least 9,999 parts per million for carbon monoxide.

  - True

  - False

- If oxygen content drops below 10%, hydrogen will not explode.

  - True

  - False

- You can allow a rescued miner to walk out of the mine alone if the miner appears to be in good shape.

  - True

  - False

- Carbon monoxide is produced by the burning or detonation of explosives.

  - True

  - False

- Which of the following are highly toxic gases?

  - carbon monoxide

  - sulfur dioxide

  - acetylene

  - all of the above

  - A and B above

  - none of the above

- Normal air is composed of oxygen, nitrogen, argon, carbon dioxide, neon, helium, krypton, xenon, hydrogen, methane, ozone, and nitrous oxide.

  - True

  - False

- What property is common to Carbon Dioxide, Nitrogen Dioxide and Sulfur Dioxide?

  - heavier than air

  - non-explosive

  - both of the above

  - none of the above

- The most accurate method to take readings with a smoke tube is to stand in the middle of the drift.

  - True

  - False

- When constructing a temporary bulkhead from a crosscut, the bulkhead should be ____ feet into the passageway.

  - 10 to 12

  - 1 to 2

  - 4 to 6

  - None of the above

- The cross-sectional area of the airway is determined by multiplying the width times the length.

  - True

  - False

- Which of the following is not a characteristic of sulfur dioxide?

  - toxic

  - irritant

  - soluble

  - explosive

- A body at 21 degrees C or higher will decay very rapidly.

  - True

  - False

- Which of the following is not a second priority condition?

  - multiple fractures

  - second degree burns involving 15 to 30% of body

  - chest injuries

  - moderate heat exhaustion

- CO2 is not soluble in water.

  - True

  - False

- Exposure to carbon monoxide concentrations as low as ____% can kill you within three hours

  - .5

  - .25

  - .05

  - .01

- Exposure to an atmosphere containing 5% carbon dioxide can increase respiration rates to _____%.

  - 500

  - 150

  - 300

  - None of the above

- This gas is hard to disperse; it is very toxic; as little as 0.04 to 0.05% is dangerous to life.

  - H2S

  - CO2

  - SO2

  - NO2

- The recommended type of extinguisher for mine rescue teams is a multi-purpose dry chemical type that contains.

  - sodium bicarbonate

  - potassium chloride

  - carbon tetrachloride

  - monoammonium diphosphate

  - none of the above

- High expansion foam is useful only in fighting class _____ fires.

  - A, B, and C

  - A or C

  - C or D

  - A or B

- A chain of command is established so that surface arrangements can be handled smoothly.

  - True

  - False

- The chain of command is responsible for making arrangements for sleeping quarters.

  - True

  - False

- The press room and the family waiting area can be the same room.

  - True

  - False

- Checking and mapping the condition of compressed airlines is important because:

  - Some firefighting equipment uses compressed air.

  - Trapped miners might use the airlines for breathing air.

  - Air powered fans could be affected.

  - A and C only

  - All of the above

- Usually the gases analyzed to determine the time for unsealing a fire area is:

  - CO, O2, CO2, CH4, H2, N2, C2H6

  - CO2, CO, O2, CH4, N2, H2

  - O2, CO2, CO, NO2, H, N2

  - CH2, O2, CO2, CO, CH4

- The electrical power in the sealed area must be cut off to prepare to open a sealed area.

  - True

  - False

- The disadvantage of progressive ventilation is:

  - that it may be too fast to determine gas readings

  - that it is only effective in multiple level mines

  - that it is a slow process

  - none of the above

- The only practical means of eliminating the possibility of rekindling the fire is to remove the heated material.

  - True

  - False

- The fresh air base may contain all of these except:

  - a coordinator

  - an advisory committee

  - federal and state officials

  - union representatives

  - all may be at the fresh air base

  - only the coordinator may be at the fresh air base

- Synchronizing all watches is a function performed by the team captain before going underground.

  - True

  - False

- The following map symbol ( indicates what?

  - air flow

  - escape route

  - temporary stopping with a regulator

  - none of the above