Team Technician (BG 4) Written Test

2012 Nevada Regional Contest

March 14-15, 2012

Winnemucca, NV

Name: ____________________________   Company: ___________________________

Team Name: _______________________	Contest Position #: ____________

Team Member #: ______________

Please circle your answer. If you make a mistake make sure you fully erase any marks.

1. The speech diaphragm is a thin foil?

A True		B False

2. High medium pressure can cause low dosage?

A True		B False

3. Bypass system damaged can cause high dosage?

A True		B False

4. The tester should be on negative pressure to conduct the function test for the low          pressure warning.

A True		B False

5. The exhalation valve test is done with the tester set on Negative Pressure?

A True		B.False

6. The minimum valve should open at a value between 1.0 and 2 mbar .

A True		B False

7. Test is incorrect while testing the minimum valve can be caused by___

A. cylinder valve not opened

B. Spring pressure is incorrect

C. Tilt valve defective

D. All the above

8.  Positive pressure is used to check the mask for leaks, using the mask test bladder and adaptor?

A True		B False

9. O-ring on plug in coupling should be replaced every 6 years?

A True		B False

10. Excessive disinfectant concentrations and over long disinfecting times can damage the mask?

A True		B. False

Directions: Circle the letter preceding the correct answer to each of the following questions.  Circle only one answer per question.

Industrial Scientific Corporation Gas Instruments:

11.  According to the gas instrument manual, a functional (bump) test is defined as a brief

exposure of the monitor to a known concentration of gas(es) for the purpose of  verifying sensor and alarm operation and is not intended to be a measure of the accuracy of the instrument.

A. True

B. False

12.  In non-latching mode for the gas instrument, all high alarm conditions (and not in Over Range condition) will clear or turn off automatically when the gas concentration has decreased to a level below the high alarm setpoint.

A. True

B. False

13.  The iTX and MX6 gas instruments can  not accept zinc-carbon battery types.

A. True

B. False

14.  According to the gas manufacturer's recommendation, a full instrument calibration should be performed bi-monthly to ensure maximum accuracy

A. True

B. False

15.  When the gas instrument is in non-latching mode, alarms set according to the

Technician Team Competition in Contest Rule Book and exposed to 19.9% Oxygen, 0.2% Methane, 40 ppm Carbon Monoxide and 4 ppm Nitrogen Dioxide, it will ___.

A. be in high alarm condition

B. display "40" for the Carbon Monoxide reading

C. display "4" for the Nitrogen Dioxide reading

D. all of the above

E. none of the above

16.  When the gas instrument is exposed to 99 PPM nitrogen dioxide, it will ________

A. remove power from the nitrogen dioxide sensor.

B. display “+OR” or "OR" for the nitrogen dioxide reading.

C. display “99.0” on the nitrogen dioxide reading.

D. both A and B

E. None of the above

17.  The maximum display range for the (catalytic) combustible\methane\LEL sensor is ______________

- 10% Methane

- 100% Methane

- 50% LEL

- None of the above

18.  If the sensor's full span value or span reserve is less than ___________ of the

applied (calibration) gas value\concentration, the gas sensor will fail calibration.

A. 30%

B. 50%

C. 70%

D. 90%

E. 100%

19.  What is the recommended flow rate during calibration of the gas instrument?

A. 2.0 liter per minute (LPM)

B. 2.5 liter per minute (LPM)

C. 3.0 liter per minute (LPM)

D. 4.0 liter per minute (LPM)

E. none of the above

20.  According to the gas instrument manual, silicone compound vapors may cause      readings of combustible (methane) gas to be _________ than gas concentrations.

### A. higher

### B. the same

C. lower

21.	Oxygen is an explosive gas and supports combustion.

A. True

B. False

22.	Specific gravity (or relative weight) of a gas is its weight in relation to an equal amount of normal air under the same temperature and pressure.

A. True

B. False

23.	The basic principle underlying mine ventilation is that air always moves from high pressure regions to low pressure regions.

A. True

B. False

24.  	The traverse method is used when ______________

- taking a reading with a smoke tube.

- taking a reading with an anemometer.

- taking a reading with a psychrometer.

- erecting bulkheads to form an air lock

- none of the above.

25.         High NO2 readings could indicate that

- Explosives are burning

- Malfunctioning electrical equipment is arcing

- Inadequate ventilation with diesel equipment operating

- All of the above

26. 	The rule-of-thumb when altering ventilation is to direct only fresh air into an

unexplored area.

A. True

B.  False

27.    	Exposure to an atmosphere containing 6% of oxygen or less will almost always  result in death

- True

- False

28.  	Temporary bulkheads can be constructed by fitting brattice around a piece of equipment.

- True

- False

29.  	A medium- velocity (or “regular”) anemometer is used to measure air velocities from 100 to 2,000 feet per minute?

- True

- False

30.  	Which of the following gases is not toxic?

- Oxides of Nitrogen

- Ethane

- Acetylene

- All of the Above