Trainer Written Test

2012 Southeast/Central Kentucky Mine Rescue Contest

June 19, 2012

Maysville, Kentucky

Trainer Name ____________________Company _______________________

Team Name ____________________

Circle the letter for your answer.  Circle only one answer.

- In the Federal Mine Safety and Health Act of 1977, “person” means any individual, partnership, association, corporation, firm, subsidiary of a corporation, or other organization.

  - true*

  - false

CONTEST RULES 2012

- A team consists of five members and a fresh air base attendant and an assistant.  If necessary, the assistant can be used to substitute for another team member.

  - true

  - false*

- If placards have not been changed after ______ seconds, teams must assume that their actions were not successful.

  - 10

  - 15*

  - 20

  - None of the above

- The standard horn signal for advance is:

  - 4

  - 3

  - 2*

  - 1

- Which one of the following statements is false:

  - Entrances to all mine openings shall be examined while under oxygen.

  - In air clear of smoke, the above checks may be made without a lifeline, provided the entire team does not go into the entrance.

  - The examination  above should not cover more than 25 feet.

  - All of the above are true*

  - All of the above are false

- A belt feeder is the dump end of a belt system.  To disperse ore on the belt.

  - true*

  - false

30 CFR PART 49

- Advanced mine rescue training and procedures is not part of the annual 40 hours of training.

  - true

  - false*

- Among the equipment required for a mine rescue team is that there be at least four gas detectors appropriate for each type of gas that may be encountered at the mines served.

  - true*

  - false

- The person performing the inspection and testing of the apparatus not to exceed 30 days shall certify by signature and date when the inspections and test was performed.

  - true*

  - false

- When an inspection of the apparatus indicates that a corrective action is necessary, the corrective action shall be recorded.

  - true*

  - false

BRADY FIRST RESPONDER 8th EDITION

- A responsive patient who is not having difficulty breathing is almost always breathing adequately.

  - true*

  - false

- Nausea/vomiting is the primary symptom of a heart attach.

  - true

  - false*

- When lifting a patient, your feet should be placed:

  - one in front of the other

  - a comfortable distance apart

  - shoulder width apart*

  - as close together as possible

- The __________ prevents food and other material from entering the trachea.

  - tongue

  - alveoli

  - pharynx

  - epiglottis*

- Shock occurs in a step by step progression.

  - true*

  - false

IG 6 2008 MODULES

- In the surface organization which one of the following persons has the duty to organize underground operations for each shift in cooperation with the person in charge, federal inspectors, and others?

  - mine clerk

  - MSHA inspector

  - mine supervisor*

  - chief engineer

- Which one of the following is not true about Carbon Dioxide?

  - soluble in water

  - colorless and odorless

  - a product of incomplete combustion*

  - all are true

- Sulfur Dioxide is one of the most soluble gases found in mines.

  - true*

  - false

- Which one of the following is not classed as a heavy hydrocarbon?

  - ethane

  - propane

  - butane

  - acetylene*

- The WLM (working level months) is a measure of the potential beta particle energy of radon daughters in the mine atmosphere.

  - true

  - false*

- One method of measuring air velocity with a smoke tube is to take the reading only in the center of the airway.

  - true*

  - false

- Mine rescue teams erecting temporary bulkheads in atmospheres with elevated hydrogen or methane readings should:

  - use only inflatable seals.

  - leave a corner of the bulkhead open for the hydrogen or methane to exit.

  - use non-sparking tools and nails. *

  - never enter such atmosphere.

- Area (of an airway)—Average width multiplied by average height of an airway, expressed in cubic feet.

  - true

  - false*

- In relation to advancing the fresh air base in multi-level mines, the fresh air base is often set up in one place and remains there throughout the operation.

  - true*

  - false

- If the team is stopped at one location for an extended period, it’s common practice for the fresh air base to signal one long pull about every 5 minutes to check on the team’s condition.

  - true*

  - false

- Class C fires are those that involve flammable or combustible liquids such as gasoline or diesel.

  - true

  - false*

- The hazards of indirect firefighting include:

  - electrocution, heat, smoke, and steam

  - toxic and explosive gases

  - oxygen deficiency

  - all of the above

  - none of the above*

- The more muscular the individual, the slower rigor mortis will develop.

  - true

  - false*

- Don’t examine the victim’s clothing for personal possessions unless you have the team captain’s approval.

  - true*

  - false

- A consideration when re-ventilating after an explosion is sources of ignition.

  - true*

  - false