2012 North Central Regional Mine Rescue Contest

Technician Team Examination

Biomarine Biopak 240R and 240S

Name:____________________________________	   Company:_________________________________

Team Name:___________________________________________

1.  Circle the letter corresponding to the correct answer.

2.  Circle only one letter per question.

3.  If no letter is circled for a given question, or more than one letter is circled, that question will be considered to

have been answered incorrectly.

4.  A total of 60 minutes will be allowed for completing all examinations.

- Hydrogen:

  - can be an asphyxiant

  - is heavier than oxygen.

  - is lighter than air.

  - both a and c		MSHA 3027  p. 2-6, 2-18

2)   When testing the Dräger detector tube bellows pump for leaks, which of the following best describes the proper procedure?

- Squeeze bellows completely closed with an open gas tube inserted and time 30 seconds for the bellows to return to their complete relaxed state.

- Visually inspect the bellows for cuts tears and holes, then collapse them several times to flush out any contaminated air that may be stored. Visually inspect the unit again, reset the sample counter and fully collapse the bellows to ensure the internal scissors spring is evenly pushing the bellows back into their original position.

- Insert an unopened tube and see if the bellows remain in the collapsed position for 30 seconds. Attach to a polymeter to test for proper intake flow.

- Insert an unopened Dräger-Tube and squeeze the pump completely.  After releasing, the position of the pump body should not change within one minute.  Squeeze the pump completely.  After releasing, the pump must open instantly.

Dräger Tubes and CMS Handbook, 15th edition, p. 29

3)  The specific gravity of oxygen is 1.000.

a) True

b) False		MSHA 3027  p. 2-47

- If a 36,000 cfm airflow passes through a duct with a cross-sectional area of 3 square feet, the air velocity through the duct could be accurately measured using a:

  - smoke tube.

  - medium-velocity vane type anemometer.

  - high-velocity vane type anemometer with multiplier gauge.

  - pitot tube		velocity = 36,00= 12,000 fpm   MSHA 3027 p. 3-160/3

  - both c and d

- A medium-velocity vane type anemometer measures:

  - air speed

  - air velocity

  - linear feet of travel   	MSHA 3027 p. 3-16

  - airflow

- Are there any conditions under which sulfur dioxide (SO2) can be made to explode?

  - yes

  - no     MSHA 3027 p. 2-21

- The heavy hydrocarbons are ethane, propane, and butane.  Of the three, butane has the largest explosive range in normal air:

  - True

  - False		MSHA 3027 p. 2-23

8)  The five “Damps” are whitedamp, stinkdamp, blackdamp, _________ and _________.

a.  rockdamp and powderdamp

b.  firedamp and coaldamp

c.  afterdamp and firedamp  		MSHA 3027 p. 2-26 & 2-27

d.  flamedamp and waterdamp

e.  none of the above

9)  These explosive gases are all lighter than air:

a.  methane, ethane, propane, acetylene

b.  methane, ethane, carbon monoxide, butane

c.  methane, hydrogen sulfide, hydrogen, acetylene

d.  methane, hydrogen, acetylene, carbon monoxide     MSHA 3027 p. 2-47

e.  none of the above

10) These gases are all odorless:

- oxygen, carbon monoxide, acetylene, ethane    MSHA 3027 p. 2-47

- butane, oxygen, carbon dioxide, methane

- nitrogen dioxide, carbon dioxide, oxygen, hydrogen

- carbon monoxide, carbon dioxide, oxygen, nitrogen dioxide

- none of the above

11)  Oxygen deficient atmospheres have no effect on the combustible gas (methane) readings of the gas detector.

a. True

b. False   	iTX page 3, 1st item of manual, rev 6 and MX6 page3, 6th item of manual, rev 3, Solaris manual rev 2, page 1-2, last bullet

12)  Silicone compound vapors may cause readings of nitrogen dioxide gas to be lower than gas concentrations.

a. True

b. False 	(answer on page 3 of manual, TMX (rev 10)-4th item; iTX (rev 6)-4th item; and MX6 (rev 3)-9th item) states "combustible gas" Solaris manual rev 2; page 1-2, 2nd bullet

13)  High Over-Range (+OR) combustible gas readings may indicate an explosive concentration of combustible gas. This condition locks the instrument.  When the instrument is removed from the Over-Range combustible gas condition, the alarm will cease operation.

a. True

b. False	After moving to safe, fresh-air environment, reset the alarm by turning OFF the instrument and turning it ON again. Solaris Manual (rev 2) pg.2-7, MX6iBrid Module 3, Slide 70, iTX Manual (rev 6) pg. 3

14)  Any rapid up-scale CH4 reading followed by a declining or erratic CH4 reading can be an indication that there is enough CH4 gas for an explosion.

a. True	Solaris manual rev 2; page 2-7, WARNING page 4 iTX rev 6 manual, last

CAUTION & MX6 rev 3 manual, 2nd CAUTION

b. False

15)  The maximum display range for the (catalytic) combustible\methane\LEL sensor is ______________ .

a.  5.0% Methane

b.  100% LEL

c.  50% LEL

d.  Both A and B		on page 27 TMX412 (rev 10); page 30 iTX (rev 6) and on slide 19 of on- l

line Features Training Video for the MX6 Solaris manual rev 2; page 6-2

e.  Both A and C

16)  What is the resolution for NO2?

a. 0.01 ppm

b.  0.1 ppm          Solaris manual rev 2; page 6-2; iTX rev 6; page 30; slide 19 on slide 19 of on-line Features Training Video for the MX6

c.  1 ppm

d.  2 ppm

e.  5 ppm

17)  Which of the following may cause erroneous readings for the combustible/methane gas sensor?

a. Silicone compound vapors

b. Oxygen deficient atmospheres

c. Sudden changes in atmospheric pressure

d. all of the above

e. only A and B

Solaris manual rev 2, page 1-2, 2nd bullet answer on page 3 of manual,

iTX (rev 6); and MX6 (rev 3)

18)  Which of the following substance(s) may cause readings of the combustible gas sensor to be lower than actual gas concentrations?

a. Hydrogen

b. Benzene

c. Silicone	(answer on page 3 of manual, TMX412 (rev 10)-4th item;  iTX (rev 6)-4th item and MX6 (rev 3)-9th item) Solaris manual rev 2, page 1-2, 2nd bullet

d. All of the Above

e. None of the Above

19)  With the confidence beep/operating beep on, the gas instrument will emit a beep approximately every __________.

a. 1 minute

b. 45 seconds

c. 30 seconds     iTX manual rev 6, page 18 & slide 92 of Configuration Training Video Tutorial video;

MX6 slide 31 of Configuration Training Video Tutorial Solaris manual; page 2-11

d. 15 seconds

20)  What is the recommended flow rate during calibration of the gas instrument?

a. 1.5 liter per minute (LPM)

b. 1.25 liter per minute (LPM)

c. 3.0 liter per minute (LPM)

d. 2.5 liter per minute (LPM)

e. none of the above

answer in manuals on page 13 TMX412 (rev10), first NOTE states  “Calibration gas flow rate should be between 0.5 and 1.0 liters per minute), on page 24 iTX (rev 6), 2nd paragraph states "0.5 LPM and on page 19 of the MX6 iBrid (rev 3) manual Solaris manual rev. 2 page 2-6, 0.25 LPM

21)  For units that are in use at least monthly, Biomarine recommends that Biopaks should be visually inspected, flow tested, and high and low pressure tested on a ____________ basis.

a.	weekly

b.	bi-weekly (every two weeks)

c.	monthly			240R p. 13    240S p. 19

d.	none of the above

22)  The nominal pressure of the fully charged oxygen cylinder is __________.

a.  1500 psi (100 bar)

b.  2200 psi (150 bar

c.  3000 psi (207 bar)  	240R p. 6   240S p. 10

d. 4500 psi (310 bar)

23)  Under normal conditions, the Biopak apparatus provides a constant flow of oxygen at an approximate flow rate of ________ into the breathing loop.

a.  1.2 liters per minute

b.  1.4 liters per minute

c.  1.6 liters per minute

d.  1.8 liters per minute       240R p. 6    240S p. 10

e.  none of the above

24)  Hydrostatic testing of the oxygen cylinder is required every 5 years.

a.  True     240R p. 15   240S p. 15

b.  False

25)  It is acceptable to use a “pick tool” to remove O-rings.

a.  True    240R  p. 15    240S  p. 23

b.  False

26)  Christ-Lube and Dow 1111 are the only two lubricants approved by Biomarine for use in Biopak breathing apparatus.

a.  True

b.  False    240R p. 15   240S p. 23

27)  Biopak breathing apparatus will provide adequate protection to users exposed to any toxic and/or  oxygen deficient atmosphere.

a.  True

b.  False       240R  p. 3   240S p. 6

28)  Can a Biopak breathing apparatus be used at an ambient temperature of 25(F (-4(C)?

a.  Yes         240R  p. 40    240S  p. 41

b.  No

29)  According to the Biomarine long-term maintenance procedure, when performing leak tests of the high pressure oxygen supply plumbing, how long should you watch for leaks at a connection?

a.  10 seconds

b.  20 seconds

c.  30 seconds

d.  1 minute    240R  p. 13    240S  p. 19

e.  none of the above

30) When cleaning breathing apparatus parts that have been in contact with exhaled air, alcohol-based cleaning pads are recommended to protect team members from infectious diseases.

    - True

    - False    240R Benchman’s quiz (question 8) and Training Guide (quiz answers), page 22

240S p. 13

NOTE:  Where MSHA 3027 is referenced, it is referring to the 2008 edition

NOTE:  Unless indicated otherwise, the references for the answers to the Biopak questions are Biomarine Biopak 240R Benchman Manual (Publication A47D257 Revision G, July 2010) and Biomarine Biopak 240S Benchman Instruction Manual (Publication A46D030, Revision K)

NOTE:  Unless indicated otherwise, the reference for the answers to the Dräger BG 4 questions is Dräger PSS BG 4 AP/CP Closed Circuit Breathing Apparatus Instructions for Use (Publication 90 21 584 – GA 1114.114 enUS, 2nd edition, July 2004)