Southwest Regional Mine Rescue Contest 2012

Carlsbad, NM

BG4-Technician Team Written Test

1. The speech diaphragm is a thin foil?

A True*		B False

2. High medium pressure can cause low dosage ?

A True		B False*

3. Bypass system damaged can cause high dosage ?

A True*		B False

4. The tester should be on negative pressure to conduct the function test

for the low pressure warning.

A True		B False*

5. The exhalation valve test is done with the tester set on Negative

pressure ?

A True*		B. False

6. The minimum valve should open at a value between 1.0 and 2 mbar .

A True		B False*

7. Test is incorrect while testing the minimum valve can be caused by

A. cylinder valve not opened

B. Spring pressure is incorrect

C. Tilt valve defective

D. All the above*

8.  Positive pressure is used to check the mask for leaks, using the

mask test bladder and adaptor?

A True*		B False

9. O-ring on plug in coupling should be replaced every 6 years ?

A True*		B False

10. Excessive disinfectant concentrations and over long disinfecting

times can damage the mask ?

A True*		B. False

From MSHA Publication 3027 Module 2 Mine Gases

- A gas is a substance with neither a definite shape nor volume.

  - True*

  - False

12.  An increase in pressure causes a gas to contract.

A.  True*

B.  False

- An increase in temperature causes a gas to expand.

A.  True*

B.   False

- Pressure exerted on a gas is _____ atmospheric pressure.

  - never

  - always

  - usually*

- The rate of diffusion is greatly decreased by higher velocities of air currents

  - True

  - False*

From MSHA Publication 3027 Module 3 Ventilation

- Blower fans are used mostly in mines having:

  - excessive overburden

  - no overburden

  - little overburden*

- Urethane foam is ______ used by rescue teams for sealing the edges of a temporary bulkhead to make it more airtight.

  - always

  - sometimes*

  - never

- Mine doors should _____ be closed after you pass through them.

  - never

  - occasionally

  - always*

- A regulator can be made by knocking blocks out of a permanent

bulkhead.

A. True*

B.  False

- Mine rescue teams have the latitude to alter ventilation

without direct orders from the command center

  - True

  - False*

From MX6 iBrid Manual Rev 3 and iTX Manual Rev 6

21.  Oxygen deficient atmospheres may cause readings of combustible (methane) gas      to be ______________ than actual concentrations.

- higher

- the same

- lower*

22. Silicone compound vapors may cause readings of combustible (methane) gas to be ______________ than actual gas concentrations.

### A. higher

### B. the same

C. lower*

23. Obstruction of the gas sensor aperture areas and/or contamination of the water barriers may cause readings to be ______________ than actual gas concentrations.

### A. higher

### B. the same

C. lower*

24. Sudden changes in atmospheric pressure may cause temporary fluctuations in the    ______________ reading.

### carbon monoxide

### methane

- nitrogen dioxide

- oxygen*

- all of the above

25. A functional (bump) test is defined as a brief exposure of the monitor to a known concentration of gas(es) for the purpose of verifying sensor and alarm operation and to measure the accuracy of the instrument.

A. True

B. False*

26. The calibration of the combustible gas sensor should be verified after any incident where the combustible gas content has caused the instrument to display an over range condition.

A. True*

B. False

27.  If an instrument fails to operate properly following any functional bump test:

A. the batteries should immediately be replaced

B. the instrument should immediately sent back to the manufacturer for repair

C. all sensors should be replaced

D. a full instrument calibration should be performed prior to use*

28. According to the manufacturer's recommendation, how often should a functional “bump” test be performed on a gas instrument?

A. Before each day’s use*

B. When the gas instrument shows a noticeable loss of sensor sensitivity

C. Once a week

D. Once a month

29. According to the gas instrument's manual, the recommended flow rate for calibration is 1.5 liter per minute (LPM).

A. True

B. False*

30. Substitution of iTX or MX6 iBrid components may impair the intrinsic safety of these instruments and may cause an unsafe condition.

A. True*

B. False