CRAIG, COLO. PRESHIFT CONTEST – 2013

CONTESTANT: _________________________ WORKING No.:_____

JUDGES INSTRUCTIONS

- Show contestant time clock and check in/out board.  Contestant only has to hang tag on board and does not have to sign and date board.

- Contestant must provide own distance measuring device, blank index cards, pen/pencil, paper, clip board, anemometer, watch, roof testing device, and detector.

- When contestant is ready, provide him/her with the blank mine map, statement, and ventilation and roof control plans.  Contestant has 5 minutes to review these and cannot travel into the mine until the clock is started.  THE 5-MINUTE REVIEW IS DONE WITH THE CLOCK NOT YET STARTED.

- Contestants have 30 minutes after starting clock to complete the problem.  Judges will notify contestant when 1 minute is left.

- Don’t take contestant back on field after clock is stopped & don’t discuss discounts.

JUDGING INFORMATION

OUTSIDE							      CHECK IF DONE

START CLOCK....................................................................................    ________

CHECK IN............................................................................................    ________

CHECK SCSR......................................................................................    ________

CHECK GAS DETECTOR (Must be left on during problem)................   ________

CHECK IF CONTESTANT HAS REQUIRED EQUIPMENT

SAFETY CAP................................................................................    ________

SAFETY BOOTS (not shoes)........................................................    ________

MINING BELT w/ID TAG THAT MATCHES CHECK-IN TAG.......    ________

CHECK IN TAG ………………………………………………………     ________

MSHA APPROVED CAP LIGHT (must work but can be left off)....   ________

SCSR..............................................................................................   ________

ANEMOMETER ……………...........................................................   ________

WATCH ………………………………………………………………...    ________

MSHA APPROVED GAS DETECTOR (must be left on).................   ________

ROOF TESTING DEVICE...............................................................   ________

DISTANCE MEASURING DEVICE.................................................   ________

BLANK INDEX CARDS....................................................................  ________

JUDGING INFORMATION

GAS TESTS & DTI’s						TEST 		   DTI

MADE		 TEST

No. 1 Entry (anywhere in entry).............................................. ______	______

No. 2 Entry (anywhere in entry).............................................. ______	______

No. 3 Entry (anywhere in entry).............................................. ______	______

No. 1 Face ……………………………...................................... ______	______

No. 2 Face.............................................................................. ______	______

No. 3 Face ……………………................................................. ______	______

Section Power Center …………..…......................................... ______	______

ROOF TESTS (verbally state visual exam in each entry)		   TEST MADE

No. 1 Entry............................................................................................ __________

No. 2 Entry............................................................................................ __________

No. 3 Entry............................................................................................ __________

HAZARDOUS CONDITIONS (verbally identify)			      IDENTIFY

No. 1 Entry

None

Note: if contestant turns off all power to section, ankle deep water changes to knee deep and now becomes a hazard for identifying and needs to be dangered off (can’t fix) and recorded.

No. 2 Entry

CO sensor in wrong location (move to correct location)…. ___________

Methane in Face ( ventilate)…………………………… …….…... ___________                           		Vent Tube back (see note)……………….………………..………. ___________

Miner energized (Turn off power to miner)……………..………... ___________		Note: if tube is extended with fan running endangered themselves, need to install line curtain to face to ventilate methane

No. 3 Entry

Roof bolter energized (Turn off power to bolter)…………. ..___________

Methane in face (install curtain)…………………………………..  ___________

Row of bolts only has 3 bolts (danger sign)…………………….. ___________

Warning signs on wrong row (put new danger signs)………….. ___________

No air in face area (install curtain)……………………………….. ___________

AIR READINGS (the last open is 19’ wide X 7’ high.;;;  CORRECTLY  TAKEN

210 fpm - LOX with the face fan off;

98 fpm – LOX with the face fan on; ……………….............................................. _________

NOTES:

- Must take air readings for 60 seconds.

- Not taking LOX air reading in proper location. Rule 9.

- Contestant may use either anemometer held in proper direction of air flow.

- Not taking a total LOX air reading noted above. Rule 7.

- If placard not present at required gas test location, 02 = 20.9%, CH4 = 0.0%.

- If contestant travels to the row with 3 roof bolts to check face or move sign in #3 face, contestant endangers self. Rule 16

- If contestant advances vent tube in #2 with fan running, endangers self.  Rule 16