Date of Examination	4/25/13		Time From:		AM/PM  To:			AM/PM

Section/Area	004		       Reported Outside?   Yes	 No	  Time:			AM/PM

Reported By:				  Received By:			  INITIAL (AUTHORIZED PERSON)

Preshift required within 3 hours prior to any 8-hour interval.

| Location | Hazardous Condition | CH4 | O2 | Action Taken |
| --- | --- | --- | --- | --- |
| Entry #1 , XC #1 | Combustibles rock dust bags |  |  | removed |
| Entry #1, XC #1 | Oil container |  |  | removed |
| Entry #1, XC #1 | Empty oil can |  |  | removed |
| Entry #1 XC #2 | Knee deep water |  |  | Pump turned on |
| Entry #1, XC 2 | Fire outlet not at tail piece |  |  | Dangered |
| Entry #1 face |  | 0.0% | 20.9% | None observed |
| Entry #2 face | Vent tube too far back | 0.0% | 20.9% | extended |
| Entry #2 face | No warning indicator bolts |  |  | Warning installed |
| Entry #3 face |  | 0.0% | 20.9% | None observed |
| Entry #2, XC#1 | No door indicator on life line |  |  | Installed indicator |
| Power Center |  | 0.0% | 20.9% |  |
| Entry #3 | Gas reading | 0.0% | 20.9% |  |
| Entry #3 | Door indicator on life line no door |  |  | Removed indicator |
| Entry #1 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |
| Entry #2 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |
| Entry #3 | Gas reading may be part of other entry above | 0.0% | 20.9% |  |

Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOX | 25085 |  |  |
| Entry #1 | 5045* | *Not required |  |
| Entry #2 | 3080* |  |  |

Velocities

Longwall Headgate:  			  				Longwall Tailgate:

CH4:		  O2:

Remarks:

Signed by Preshift Certified Examiner		      Date					     Certification Number

Countersigned by Mine Foreman		      Date					     Certification Number

Countersigned by Operator/Agent		      Date					     Certification Number