Judge’s Instructions

- Show the contestant the time clock and the check in/out board.

- Provide contestant with the blank map, written statement, and ventilation and roof control plans.  The contestant has 5 minutes to review the plans prior starting the clock and the underground portion of the contest.

- Show the contestant the entries and which area he or she is to pre-shift.  Entries are labeled left to right facing inby.

Contestant needs to take air reading #1 face, #2 and the #3 face to be able to insure compliance with vent plan.

For taking the air reading on the section, give the contestant the following information:

LOX 		Width = 	20 feet

Height = 	8 feet

Area = 	160			CORRECT LOCATION

Velocity =	148 fpm for LOX

CFM =            23680 CFM

#1 face =      255 FPM Area measurements behind curtain 2 by 8 = 4080 cfm

#2 face =      832 FPM Area measurements behind curtain 2.5 by 8 = 16640 cfm

#3 face =      76 FPM Area measurements behind curtain 3 by 8 = 1824 cfm

If contestant does not take an air reading in the proper location for the LOX; deduct for improper location

Provide the contestant the following gas reading for the outby areas 0.0% CH4 and 20.9% O2.

Contestant must simulate taking the air reading for 60 seconds.

Contestant can correct following hazards;  life line over belt after turning the belt off, low ventilation in #1 face; Diesel running in #1 face turn off diesel;  low ventilation in #2 face; low ventilation in #3 face;.

The contestant will have 30 minutes to work the problem.  Notify the contestant when 1 minute remains.