2012 National Metal and Nonmetal

Mine Rescue Contest

Mine Rescue Field Competition

Written Test

Directions:

- Find the correct answer to each of the questions.

- Select only one answer per question.

- Then, fill in the corresponding circle on the answer sheet for each numbered question.

Good Luck!

July 31, 2012

2012 Metal/Nonmetal National Mine Rescue Contest

Mine Rescue Field Competition – Written Test

Please do not write on this test.  Use the answer sheet provided.

- Federal regulations require mines to have and post a Mine Rescue and Recovery Plan for notifying all the mine rescue team members that will be needed to assist in the rescue and recovery operation (30 CFR Section 49.9).

  - True

  - False

- During a rescue and/or recovery operation, the team is under the direct supervision of the _______.

  - fresh air base coordinator

  - command Center

  - safety director

  - team captain

- If shafts are used as the two main airways, the intake airway is called the downcast shaft and the return airway is referred to as the upcast shaft.

  - True

  - False

- In natural ventilation, air flows because of the natural difference in pressure _____.

  - between the underground intake and return entries

  - created by the ventilation controls in the mine

  - inside and outside the mine

  - None of the above

- Clean, dry normal air at sea level ________.

  - supplies us with the oxygen we need to live

  - contains 78 percent nitrogen and 21 percent oxygen

  - has a specific gravity of 1.0

  - All of the above

- Overcasts and undercasts are used to permit the two air currents to cross without the intake air short-circuiting into the exhaust.

  - True

  - False

- Normal air contains about _______ percent of carbon dioxide (CO2).

  - 0.30

  - 0.003

  - 0.03

  - 3.00

- Although each situation is different, experience indicates that no attempt should be made to unseal a fire area until –

  - the oxygen content of air behind the seal is low enough to make an explosion impossible

  - the seals can be removed while the main fan is operating

  - there are enough teams available to rebuild the seals if necessary

  - carbon monoxide has disappeared or nearly disappeared from the air in front of the seals

  - All of the above

- Progressive ventilation is the re-ventilation of the entire sealed area at once.

  - True

  - False

- Before entering a mine to search for missing miners, there are several questions to which the team should have answers.  These include:

  - How many miners are missing?

  - When did the miners’ shift start?

  - Where do the miners normally take their breaks?

  - What areas were they supposed to work in?

  - Both A. and D.

- Survivors can be categorized into three priority groups according to their condition or injuries.  Multiple lacerations, moderate shock, and back injuries with or without spinal injuries, are examples of ____________.

  - First Priority conditions

  - Second Priority conditions

  - Third Priority conditions

  - A mix of all three Priority conditions

- Survivors should be allowed to walk out on their own if they appear to be in good shape.

  - True

  - False

- For a fire or explosion to occur, three elements must be present at the same time:  fuel, sufficient oxygen, and heat (ignition).

  - True

  - False

- A jump in the pressure recording chart for the main fan is a definite indication that an explosion has occurred underground.

  - True

  - False

- Hydrogen Sulfide (H2S) _________.

  - is one of the least poisonous gases known

  - is explosive in concentrations of 4.3 to 42.5 percent in normal air

  - has a specific gravity of 1.9106

  - None of the above

- Oxides of Nitrogen (NO, NO2, and N2O4) _______.

  - are highly toxic

  - can burn, but will not explode

  - tend to collect in low areas in the mine

  - appear reddish-brown in higher concentrations

  - All of the above, except B.

- The presence of sulfur hexafluoride (SF6) could indicate that an explosion has taken place in an area with low oxygen content, such as a sealed area.

  - True

  - False

- Acetylene (C2H2) __________.

  - is colorless and tasteless, but has a slight garlic odor

  - is formed when methane is burned or heated in air having high oxygen content

  - has an explosive range between 2.5 to 70 percent in normal air

  - is combustible and will support combustion

- During a rescue operation, the rescue of survivors is the _______ priority of the mine rescue team.

  - first

  - second

  - third

  - None of the above

- In accordance with 30 CFR Section 49.6(a)(3), each mine rescue station shall be equipped with at least two extra, fully-charged oxygen bottles for every self-contained breathing apparatus.

  - True

  - False

- Before everyone is moved up to the new fresh air base, the area between the old and new fresh air base should be explored by the team.

  - True

  - False

- A partially opened man door cannot be used as a regulator.

  - True

  - False

- Which instrument can be used to measure air velocities greater than 2,000 feet per minute (fpm)?

  - a high-velocity anemometer

  - a medium-velocity anemometer

  - a Pitot tube with an attached differential pressure gauge

  - Both A. and C.

- There are two methods of measuring velocity with a smoke tube.  The more accurate method is to take a smoke reading only at the center of the airway.

  - True

  - False

- During recovery work, the role of a mine rescue team varies as the operation progresses and conditions change.  Until ventilation is re-established, apparatus crews will be needed to:

  - assess ground conditions

  - clear debris and stabilize ground conditions

  - rebuild bulkheads

  - All of the above

- Indirect firefighting methods work by ___________.

  - removing potential ignition sources from the fire area

  - exhausting the fuel source in the fire area

  - eliminating oxygen from the fire

  - None of the above

- These gases are explosive, flammable, and highly toxic.

  - CO, H2S, and CH4

  - H2, H2S, and CO

  - CH4, H2S, and CO2

  - CO and H2S

- This gas is a product of complete combustion.

  - CO2

  - CO

  - Both A. and B.

  - Neither A. nor B.

- These gases are heavier than normal air under the same temperature and pressure conditions.

  - CO, H2, H2S, and CH4

  - H2, CO, and CH4

  - CO2, H2S, NO2, and SO2

  - CO, H2S, NO2, and SO2

- Any flammable gas can explode under certain conditions.  That is, there must be enough of the gas in the air, enough oxygen, and a source of ignition.

  - True

  - False