2013 Southern Mine Rescue Association                    Mine Rescue Contest, May 7-9

Bio Marine 240R/S Bench Written Test

Instructions:

Circle the correct letter or answer on this quiz that represents the BEST answer.

If you need to change and correct your answer, make sure that all erasures are complete.

Please print your name & company CLEARLY in the space below.

Name:					Company:

Circle “TRUE” or “FALSE”

1. You must use the tool provided in the Test/Service kit when installing the components for the vent valve in order to get a tight proper seal.

T or F

2. NEW oxygen cylinders for the 240R/S have a service life of 25 years.

T or F

3. When the valve on the oxygen cylinder is opened, the bottle pressure is feed to the high pressure section of the regulator assembly.

T or F

4. When the emergency by-pass is activated, the additional release of oxygen will temporarily increase the constant flow.

T or F

5. The BioPak 240R/S should not be used and it should be thoroughly inspected if the Turnaround Maintenance Tag has not been dated.

T or F

6. All breathing oxygen must first pass through the Carbon Monoxide scrubber   before going through the cooling section.

T or F

7. It is an accepted practice to train with the BioPak 240R/S without installing the either the frozen Gel-Tube or Ice Packs.

T or F

8. Due to the flow restrictor installed in the high-pressure line, it takes the 240R/S up to 90 seconds before it will supply breathing air when the valve on the Oxygen Cylinder is first opened.

T or F

9. Due to the 240R/S being a positive pressure unit, the user will not get contaminated breathing air in his system even if he has a leak in his mask due to facile hair.

T or F

10. Under heavy work conditions, if the user exhales and moves the diaphragm as far as it can travel, it will activate the demand valve.

T or F

11. The BioPak 240R/S alarm activates at 25% of full cylinder pressure giving the user an indication that he has only one hour left of oxygen.

T or F

12. The Oxygen Cylinder to Regulator mating seal should be kept lubricated with Cristo-Lube ONLY.

T or F

13. The large o-ring on the breathing chamber that seals the Carbon Dioxide scrubber medium in the breathing system, when damaged, could cause Carbon Monoxide to not be scrubbed from the breathing air.

T or F

14. During normal operation of the BioPak 240R/S, it is recommended to depress the emergency by-pass valve one or two seconds to keep the face mask from fogging.

T or F

15. The 240R/S oxygen cylinder is constructed of carbon fiber wrapped aluminum and has a service life of twenty five years.

T or F

16. Under heavy work conditions, if the user inhales and moves the diaphragm as far as it can travel, it will activate the demand valve.

T or F

17. Reduced duration (less than 4 hours) in the BioPak 240R/S may be caused by excessive use of the EMERGENCY BY-PASS, leaks in the BioPak breathing loop, poor face mask seal, or beards and eyeglasses that break the face mask seal.

T or F

18. If you hear the demand valve hit every time you inhale and you are not working hard, you should check you face mask for fit and adjust it for a better seal.

T or F

19. Under heavy work conditions, if the user exhales and moves the diaphragm as far as it can travel, it will activate the Vent Valve.

T or F

20. In a positive pressure respirator, the face piece pressure is maintained above the pressure outside the face piece.

T or F