PRICE, UTAH - PRESHIFT CONTEST – 2014

CONTESTANT: _________________________ WORKING No.:_____

JUDGES INSTRUCTIONS

- Show contestant time clock and check in/out board.  Contestant only has to hang tag on board and does not have to sign and date board.

- Contestant must provide own distance measuring device, tool apron, blank index cards, pen/pencil, paper, clip board, anemometer, watch, roof testing device, and detector.

- When contestant is ready, provide him/her with the blank mine map, statement, and ventilation and roof control plans.  Contestant has 5 minutes to review these and cannot travel into the mine until the clock is started.  THE 5-MINUTE REVIEW IS DONE WITH THE CLOCK NOT YET STARTED.

- Contestants have 30 minutes after starting clock to complete the problem.  Judges will notify contestant when 1 minute is left.

- Don’t take contestant back on field after clock is stopped & don’t discuss discounts.

JUDGING INFORMATION

OUTSIDE							      CHECK IF DONE

START CLOCK....................................................................................    ________

CHECK IN............................................................................................    ________

CHECK SCSR......................................................................................    ________

CHECK GAS DETECTOR (Must be left on during problem)................   ________

CHECK IF CONTESTANT HAS REQUIRED EQUIPMENT

SAFETY CAP................................................................................    ________

SAFETY BOOTS (not shoes)........................................................    ________

MINING BELT w/ID TAG THAT MATCHES CHECK-IN TAG.......    ________

MSHA APPROVED CAP LIGHT (must work but can be left off)....   ________

SCSR..............................................................................................   ________

ANEMOMETER..............................................................................   ________

WATCH...........................................................................................   ________

MSHA APPROVED GAS DETECTOR (must be left on).................   ________

ROOF TESTING DEVICE...............................................................   ________

DISTANCE MEASURING DEVICE.................................................   ________

TOOL APRON (Not required)..........................................................   ________

BLANK INDEX CARDS....................................................................  ________

PEN/PENCIL/MARKER....................................................................  ________

PAPER (Not required)......................................................................  ________

CLIPBOARD(Not required) .............................................................  ________

JUDGING INFORMATION

GAS TESTS & DTI’s						TEST 		   DTI

MADE		 TEST

No. 1 Entry (anywhere in entry).............................................. ______	______

No. 2 Entry (anywhere in entry).............................................. ______	______

No. 3 Entry (anywhere in entry).............................................. ______	______

No. 1 Face ……………………………...................................... ______	______

No. 2 Face.............................................................................. ______	______

No. 3 Face ……………………................................................. ______	______

Section Power Center …………..…......................................... ______	______

ROOF TESTS (verbally state visual exam in each entry)		   TEST MADE

No. 1 Entry............................................................................................ __________

No. 2 Entry............................................................................................ __________

No. 3 Entry............................................................................................ __________

HAZARDOUS CONDITIONS (verbally identify)			      IDENTIFY

No. 1 Entry

Equipment door not as air lock (DTI, Report)…..………….…... ___________

Excessive methane at cave (correct ventilation)….………....... ___________

Excessive methane in face (correct ventilation)…………......... ___________

(Must retest faces for methane following ventilation change) Rule 5

No. 2 Entry

Old belt fabric in walkway (DTI and report)…….… …….…... ___________                           		Hot bottom roller on belt (install check curtain)…………..…. ___________

No timbers at toe of cave xc #4 (DTI and report)……………. ___________

Last open low air reading (put check curtains in) .............___________

No. 3 Entry

Pump labeled wrong (DTI and report) ………………..........___________

Life line in backwards (repair) …………………………...___________

Excessive methane in face (correct ventilation)…………......... ___________

AIR READING (Last open is 19’ wide X 7 high)  CORRECTLY  TAKEN

185 fpm - LOX between Nos. 2 & 3 Entries ......... 24,605 CFM  .................... _________

220 fpm after curtains hung in belt line and open cross cut. 29260 CFM

NOTES:

- Must take air readings for 60 seconds.

- Not taking LOX air reading in proper location. Rule 9.

- Contestant may use either anemometer held in proper direction of air flow.

- Not taking a total LOX air reading noted above. Rule 7.

- If placard not present at required gas test location, 02 = 20.9%, CH4 = 0.0%.

- Not taking measurement of area for air reading. Rule 8.

- Acts of endangerment, i.e. crossing moving belt.  Rule 16

- Acts that could result in explosion, explosive methane over ignition source.  Rule 15

Contestant can correct following hazards;

1. Re-string life line,

2. vent methane in #3 and #1 faces and at cave,

3. install check curtain in x-cut or entry methane #3 face,

4. fix low air in LOX install curtain entry or belt line,

5. hot roller on belt turn off belt.