2016 Northern Mine Rescue Contest

Written Exam

Field Competition

June 14, 2016

Clymer, New York

2016 Northern Mine Rescue Contest

Written Exam – Field Competition

Directions:  Fill in the corresponding bubble on your Scantron sheet to indicate the letter preceding the correct answer to each of the following questions.   Select only one answer per question.

- As part of the “triage” system, survivors can be categorized into three priority groups according to their condition or injury.   A survivor with multiple fractures would be a ______ condition.

  - Low, or third priority

  - Second priority

  - First priority

  - Described condition not included in any of the above priority categories.

- Before entering a mine to search for missing miners, there are several questions to which you should have answers.  These include:

  - How many miners are missing?

  - What areas were they supposed to be working in?

  - Are the miners trained to shelter in place?

  - Both A and B

- If bodies are not recovered soon after death, they will begin to decompose.  Some of the factors that influence body deterioration are:

  - Air temperature in the area

  - Body size of the victim

  - Amount of physical trauma incurred by the victim

  - All of the above

- One thing to remember when dealing with any injury is to stay as calm as possible.  Sometimes when faced with a gruesome or unnerving sight, the best thing to do is take a deep breath and continue to breathe fully and deeply until the job is finished.

  - True

  - False

- All decisions concerning the mine rescue teams (scheduling, assignments, tracking, rotations, and methods of exploration or firefighting) are made by the _______.

  - Mine superintendent

  - MSHA district manager

  - Command center

  - Fresh air base coordinator

- It is important to establish a clear chain-of-command so that rescue and recovery work can be well coordinated.  Thus, the team is under the direct supervision of the team captain.

  - True

  - False

- A standby team is scheduled to be on the surface in ready reserve when rescue teams are working underground.

  - True

  - False

- In the fire triangle, each leg of the triangle is labeled with one of the elements necessary for a fire: fuel, oxygen or heat.  Smothering a fire with noncombustible materials removes the _____.

  - Fuel

  - Oxygen

  - Heat

  - All of the above

- A dry chemical extinguisher containing monoammonium phosphate is effective _____ fires.

  - Only on Class A

  - Only on Class A and Class B

  - On Class A, Class B, and Class C

  - On Class A, Class B, Class C and Class D

- Water can also be used to put out fires.  Water acts to cool the fire, removing heat from the fire triangle.  Water is an effective extinguishing agent _____ fires.

  - Only on Class A

  - Only on Class A and Class B

  - On Class A, Class B, and Class C

  - On Class A, Class B, Class C and Class D

- High expansion foam is used mainly to contain and control fire by removing ____ and ____.

  - Oxygen and fuel

  - Heat and oxygen

  - Fuel and heat

  - None of the above

- Determining the exact time to unseal a fire area is based on the laws of physics and chemistry, as well as on experience and sound judgement.  The main factors governing the time for unsealing a fire area include:

  - Extent and intensity of fire at the time of sealing

  - Gas conditions as indicated by analysis of air samples taken in front of the seals

  - Location of the fire area with respect to ventilation

  - Both A and C

- The two basic methods for unsealing a fire area are progressive and indirect ventilation.

  - True

  - False

- During a recovery using progressive ventilation, the sealed area is explored and re-ventilated in successive blocks by the use of airlocks.  The main disadvantage of progressive ventilation is that it is a slow process.

  - True

  - False

- Barefaced exploration should stop _____.

  - When the crew encounters smoke or damage

  - When gas tests indicate the presence of carbon monoxide or other noxious gases

  - When disruption in ventilation are found

  - All of the above

- In single-level, room-and-pillar mines, a fresh air base can be established in a drift, entry or crosscut close to the affected area.  In these cases, _____ must be constructed to isolate the fresh air base from the unexplored area beyond it.

  - A temporary stopping

  - An air lock

  - A permanent bulkhead

  - None of the above

- The ____ is responsible for just about everything that goes on at the fresh air base.

  - Command center

  - Fresh air base coordinator

  - Backup team captain

  - Both B and C

- Once a fresh air base is established, apparatus teams will begin to explore the affected area.  The number of trips needed to complete exploration and the time it will take depends on:

  - The extent of the area involved

  - The conditions within the affected area

  - The number of teams underground

  - Both A and B

- As you explore, your first priority is team safety.  Your second priority is _____.

  - Rescue of survivors

  - Extinguish or seal any fires

  - Re-establish ventilation

  - Map all conditions found in the affected area

- When establishing an area for a fresh air base, the area should be free of oil and grease, large enough to accommodate all of the people using it, and isolated from any stray or direct current.

  - True

  - False

- The purpose of mine ventilation is to provide a volume of air sufficient to disperse and remove harmful gases, dust, smoke, and fumes and to provide adequate oxygen.

  - True

  - False

- In order to get the air to flow from the intake to the exhaust entries, the intake air must be at a higher pressure than the exhaust.

  - True

  - False

- Regulators are used to control and adjust the quantity of airflow in the mine in order to ensure proper distribution.  A partially opened _____ can be used as a regulator.

  - Man door

  - Temporary stopping

  - Sliding door in a permanent bulkhead

  - All of the above

- The “rule of thumb” when altering ventilation is not to change the ventilation ______.

  - Without direct orders from the command center

  - Into an unexplored area

  - By simply reversing the main fan

  - All of the Above.

- Another way to test for gases is to collect air samples in special syringes or evacuated bottles.  Although it is a more time-consuming process, complete chemical analysis of the samples can reveal the presence of gases that portable detectors are not designed to detect.

  - True

  - False

- When a mine is sealed off for any length of time, water can collect in it.  Pools of water can release ____ gases into the air when they are stirred up.

  - Water-soluble

  - Explosive and non-explosive

  - Poisonous and toxic

  - All of the above

- The volume of a gas changes in response to any change in _____.

  - The ventilating air currents in the mine

  - Its specific gravity

  - Atmospheric pressure or temperature

  - All of the Above

- Any flammable gas can explode if ______.

  - There is enough of the gas present in the air

  - There is enough oxygen present in the air / gas mixture

  - There is an ignition source in the area

  - A, B and C must be present at the same time

- Although color, odor, and taste are physical properties which can help you to identify a gas during barefaced exploration, you cannot rely solely on your senses to positively identify a gas.

  - True

  - False

- Which of the following is not true for carbon monoxide (CO)?

  - It is an explosive and flammable gas

  - It is highly toxic and its poisoning effects are cumulative over time

  - It is lighter than air and can be measured using a portable detector at chest level

  - It is a product of the complete combustion of any carbon material

ANSWER KEY

Written Exam – Field Competition

All questions taken from MSHA Publication 3027

Question	Answer		Source

1  		B.  		Module 6, pg. 6-6

2.  		D.		Module 6, pg. 6-3

3.		D.		Module 6, pages 6-9 and 6-10

4.   		A.		Module 6, pg. 6-6

5.   		C.		Module 1, pg. 1-3

6.   		A.		Module 1, pg. 1-6

7.   		A.		Module 1, pg. 1-14

8.   		B.		Module 5, pg. 5-4

9.   		C.		Module 5, pg. 5-6

10.   		A.  		Module 5, pg. 5-8

11.   		B.	  	Module 5, pg. 5-10

12.  		D.  		Module 7, pg. 7-5

13.  		B.  		Module 7, pg. 7-5

14.  		A.  		Module 7, pg. 7-7

15.  		D.  		Module 4, pg. 4-6

16.  		B.  		Module 4, pg. 4-7

17. 		B.  		Module 4, pg. 4-9

18.  		D.  		Module 4, pg. 4-11

19.  		A.  		Module 4, pg. 4-12

20. 		A.  		Module 4, pg. 4-7

21.  		A.  		Module 3, pg. 3-4

22.  		A.  		Module 3, pg. 3-5

23.  		D.  		Module 3, pg. 3-12

24.  		B.  		Module 3, pg. 3-15

25.  		A.  		Module 2, pg. 2-4

26.  		D.  		Module 2, pages 2-10, (2-19 - 2-20 for H2S), (2-21 for SO2)

27.  		C.  		Module 2, pg. 2-5

28.  		D.  		Module 2, pg. 2-7

29.  		A.  		Module 2, pg. 2-8

30.  		D.  		Module 2, pages 2-16 - 2-17

# Text boxes

2010

2016