Missouri Mine Rescue Contest

Rolla, MO

October 3 – October 6, 2016

Written Test – Field Competition

- While exploring and preparing an area for re-ventilation, teams should be on alert for and eliminate any possible source of ignition.

  - True (Module pg. 7-11)

  - False

- During recovery the ______ will determine when conditions appear safe to reenter the mine.

  - Mine Manager

  - Command Center (Modules 7-10)

  - Team Trainer

  - Gas Man

- Butane has an explosive range of 1.86 to 8.41 percent in normal air.

  - True (Modules 2-23)

  - False

- The specific gravity for Propane is_________.

  - 1.0625

  - 1.5265

  - 1.5625 (Modules 2-23)

  - 1.0526

- Ethane is not a Heavy Hydrocarbon.

  - True

  - False (Modules 2-23)

- In certain concentrations propane and ethane may produce a characteristic “gassy” odor.

  - True

  - False (Modules 2-23)

- 0.5545 is the specific gravity of Methane.

  - True (Modules 2-22)

  - False

- Exposure to .10 to .20% or more of Hydrogen Sulfide can cause rapid death.

  - True (Modules 2-61)

  - False

- Hydrogen has an explosive range of 4.0 to 74.2% in air with as little as 8% oxygen.

  - True

  - False (Modules 2-59)

- The specific gravity for Nitrogen Dioxide is:

  - 1.5894 (Modules 2-57)

  - 1.8459

  - 1.5984

  - None of the above

- _______ is a mixture of methane and air that will burn or explode when ignited.

  - Blackdamp

  - Stinkdamp

  - Firedamp (Modules 2-27)

  - Afterdamp

- “Damps” are the names early miners gave to mixtures of gases?

  - True (Modules 2-26)

  - False

- Because the command center must make their decisions based on what you see, it is extremely important that you assess the ventilation accurately.

  - True (Modules 3-3)

  - False

- The only natural energy source that can create and sustain an adequate airflow is kinetic energy due to temperature difference.

  - True

  - False (Modules 3-5)

- Reestablishing ventilation and bringing fresh air to an area damaged by fire or explosion is the main task of mine rescue teams in an exploration operation.

  - True

  - False (Modules 7-4)

- After a fire, explosion, or flood in a mine, rescue teams are usually needed to go into the mine to assess and reestablish_________.

  - Production

  - Electrical Power

  - Ventilation (Modules 3-3)

  - Ground Control

- The mine fan(s) can create pressure differential either by exhausting air into the mine or blowing air from the mine.

  - True

  - False

- If a body is in cold water, it will remain in almost perfect condition for 3 or 4 days.

  - True

  - False (Modules 6-10)

- Blower fans are used mostly in mines having a lot of overburden.

  - True

  - False (Modules 3-4)

- When a team locates a body, the usual procedure is to report the location to the command center.

  - True (Modules 6-8)

  - False

- If shafts are used as the two main airways, the intake airway is called the downcast shaft, and the exhaust airway is referred to as the upcast shaft.

  - True (Modules 3-4)

  - False

- If pressure difference exists naturally between the two airways, then the mine has _____ ventilation.

  - Mechanical

  - High Pressure

  - High Volume

  - Natural (Modules 3-5)

- The teams map person is responsible for marking down information on the map as the team explores and assesse ground conditions.

  - True

  - False

- Temporary bulkheads are usually built of canvas brattice cloth or plastic.

  - True (Modules 3-9)

  - False

- Check curtains are fastened at the bottom only and can be either one piece or have a slit in them or overlapping flaps.

  - True

  - False (Modules 3-9)

- A line brattice is especially useful for rescue teams to use when they need to flush out or ventilate a small area of the mine.

  - True (Modules 3-10)

  - False

- Locomotives can be used during barefaced exploration as long as there is no smoke and no evidence of explosive gases.

  - True (Modules 4-6)

  - False

- The fresh air base also functions as a base of communication for the operation linking the team, the command center, and the media.

  - True

  - False (Modules 4-6)

- The fresh air base should be situated where it’s assured a supply of good water.

  - True

  - False (Modules 4-7)

- An example of a first priority condition is second degree burns covering more than ____% of the body.

  - 20

  - 25

  - 30 (Modules 6-5)

  - Only third degree burns can be first priority.