2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test – Field Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

Q#1)	The location where teams enter into the mine’s irrespirable atmosphere is considered the:

- Fresh Air Base;

- Command Center;

- Bench Area;

- Triage Area.

Q#2)	Section 7(3) of the MINER Act of 2006 requires that the primary communicator with the operator, miner’s families, the press and the public be:

- Mine Manager

- MSHA;

- Mine HR Manager;

- Company person picked by the company.

Q#3)	MSHA will arrive at the mine site to:

- Advise with company personnel on how the operation might be best carried out;

- Take charge of an operation is deemed necessary.

- Both A & B;

- Neither A or B.

Q#4)	If required for the event a ______ should be established to set a clear order of team usage during the operation.

- Notification plan;

- Command center;

- Rotation schedule;

- Bench area.

Q#5)	In some large multi-levels mines, a ______ fan is used to help maintain the correct ventilation.

- Booster;

- Blower;

- Exhaust;

- Auxiliary.

Q#6)	On a mine map the symbol _________ represents?

A)	Track;

B)	Temporary bulkhead or stopping;

C)	Permanent bulkhead or stopping;

D)	Conveyor belt.

Q#7)	On a mine map the symbol X          represents?

A)	Auxiliary fan and tubing;

B)	Undercast

C)	Man Door;

D)	Main Fan.

Q#8)	Barefaced exploration should stop when:

- There is sufficient oxygen;

- They encounter smoke or damage;

- The ventilation system is working properly;

- All of the above.

Q#9)	When determining the rate of travel, the team captain should consider:

- The surrounding conditions;

- The team’s condition;

- The equipment being carried;

- All of the above.

Q#10)	The team stationed at the fresh air base ready to go is considered the:

- Standby team;

- Bench Team;

- Briefing Team;

- Backup Team.

Q#11)	If a team member experiences problems their apparatus beyond the fresh air base the team member should;

- Switch to the extra apparatus that the team carried with them;

- Be immediately sent back to the fresh air base;

- With the entire team, return immediately to the fresh air base;

- Be sent back to the fresh air base with another team member.

Q#12)	Water is best used on what type of fire:

- Class D;

- Class C;

- Class B;

- Class A.

Q#13)	Class B fires involve:

- Combustible metals;

- Combustible liquids;

- Electric equipment;

- Combustible materials.

Q#14)	When fighting an obstacle fire with burning equipment at its center and using a fire extinguisher, it is best to:

- Use a 2-man team and approach from each side;

- Aim directly at the burning equipment;

- Use a 2-man team and approach from the same side;

- Use a 2man team- 1st man actively fighting the fire, the 2nd man watching for the fire reigniting.

Q#15)	When survivors are found, their behavior may range from apprehension to uncontrollable hysteria is considered a:

- Physic Factor;

- Psychological Factor;

- Conditional Factor;

- Physical Factor.

Q#16)	Triage is a system of assigning priorities to:

- Recovery of the mine;

- Re-establishing the ventilation system;

- Where mine entry will occur;

- Medical treatment of injured miners.

Q#17)	The safest way for getting survivors out of a refuge chamber is to:

- Tear down the barricade to quickly access area;

- Quickly open the door & move team in;

- Advance fresh air to the area;

- All of the above.

Q#18)	If survivors are found in questionable air and is able to walk, the team should;

- Place him on a stretcher & transport him to the fresh air base;

- Give him breathing protection and allow him to walk to the fresh air base while the team continues to explore;

- Give him breathing protection tell him you will be back for him as soon as possible;

- Give him breathing protection, position him between members of the team to be walked to the fresh air base.

Q#19)	During recovery operations air locking at a sealed fire should always begin:

- On the exhaust side of the fire;

- On the intake side of the fire;

- At the fresh air base;

- All of the above.

Q#20)	The affected area is recovered and re-ventilated as a whole is called:

- Direct ventilation

- Progressive ventilation;

- Regressive ventilation;

- Proposed ventilation.

Q#21)	To determine the rate of diffusion of a gas the team needs to know:

- Atmospheric pressure;

- Temperature

- Air current;

- All of the above.

Q#22)	Physical properties of a gas can help identify it.  A reddish-brown color could indicate:

- Carbon monoxide;

- Hydrogen sulfide;

- Nitrogen oxides;

- Oxygen.

Q#23)	A gas that can cause harm by either breathing it or by coming in contact with it is considered to be:

- Flammable;

- Asphyxiating;

- Toxic;

- Soluble.

Q#24)	How does an asphyxiating gas produce an oxygen-deficient atmosphere:

- By destroying oxygen;

- By combining with oxygen;

- By displacing oxygen;

- By liquefying oxygen.

Q#25)	Breathing air with 5 percent (%) Carbon dioxide can cause:

- Death;

- No effect;

- Violent panting;

- Difficult breathing.

Q#26)	Oxides of Nitrogen are:

- Explosive;

- Toxic;

- Flammable;

- All of the above.

Q#27)	Hydrogen sulfide is:

- Flammable;

- Toxic;

- Explosive;

- All of the above.

Q#28)	When pumping or walking through water, concentrations of the following gases could increase:

- Sulfur Dioxide;

- Carbon Monoxide;

- Hydrogen Sulfide;

- All of the above.

Q#29)	If methane is present it’s important to monitor it carefully do to its being:

- Toxic;

- Asphyxiating;

- Explosive;

- None of the above.

Q#30)	To test for Methane, the detector should be held:

- Above the head;

- At eye level;

- At chest level;

- At your feet.

Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test Answers – Field Competition

A#1) 	A) Module 1; Page 14; Paragraph 5.

A#2) 	B) Module 1; Page 5; Paragraph 4.

A#3) 	C) Module 1; Page 6; Paragraph 3.

A#4) 	C) Module 1; Page 14; Paragraph 7.

A#5) 	A) Module 3; Page 5; Paragraph 2.

A#6) 	B) Module 3; Page 25; Sample Mine Map symbols.

A#7) 	D) Module 3; Page 25; Sample Mine Map symbols.

A#8) 	B) Module 4; Page 6; Paragraph 5.

A#9) 	D) Module 4; Page 25; Paragraph 1&2

A#10) 	D) Module 4; Page 53; Paragraph 2

A#11) 	C) Module 4; Page 32; Paragraph 1

A#12) 	D) Module 5; Page 5; Paragraph 4

A#13) 	B) Module 5; Page 5; Paragraph 5

A#14) 	A) Module 5; Page 7; Paragraph 8

A#15) 	B) Module 6; Page 8; Paragraph 1

A#16) 	D) Module 6; Page 14; Paragraph 10

A#17) 	C) Module 6; Page 4; Paragraph 6

A#18) 	D) Module 6; Page 7; Paragraph 5

A#19) 	B) Module 7; Page 8; Paragraph 4

A#20) 	A) Module 7; Page 9; Paragraph 5

A#21) 	D) Module 2; Page 5; Paragraph 5.

A#22) 	C) Module 2; Page 8; Paragraph 2.

A#23) 	C) Module 2; Page 9; Paragraph 1.

A#24) 	C) Module 2; Page 11; Q-7.

A#25) 	D) Module 2; Page 15; Paragraph 8-Health Hazards.

A#26) 	B) Module 2; Page 17; Paragraph 4&5.

A#27) 	D) Module 2; Page 19; Paragraph 11 & 12.

A#28) 	B) Module 2; Page 20; Paragraph 6-Where found.

A#29) 	C) Module 2; Page 23; Paragraph 2-Meaning of findings.

A#30) 	B) Module 2; Page 22; Paragraph 9-Where found.