2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test – Team Tech Competition (BG4)

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

Q#1)	A fan that pulls or sucks air out of a mine is called a:

- Blower fan;

- Exhaust fan;

- Booster fan;

- Auxiliary fan.

Q#2)	In mines with a possible explosive atmosphere the team should have with them:

- Auxiliary fans;

- Mechanic’s tools;

- Non-sparking tools;

- Explosives.

Q#3)	When fans are used to create the pressure differential to needed for ventilating a mine it is considered:

- Natural ventilation;

- Ventilation plan;

- Mechanical ventilation;

- Auxiliary fan system.

Q#4)	Temporary bulkheads can be built from:

- Canvas brattice;

- Wood or metal;

- Parachute stopping;

- All of the above.

Q#5)	Air locks are used by mine rescue teams:

- When opening a door or knocking out a bulkhead behind which conditions are not definitely known;

- Before opening a barricade in bad air behind which trapped miners may be located;

- To establish a fresh air base;

- All of the above.

Q#6)	An increase in temperature causes a gas to:

- Expand;

- Contract;

- Liquefy

- Increase in specific gravity.

Q#7)	If the barometric pressure is high, concentrations of explosive gases can:

- Go away;

- Build up;

- Expand;

- Disburse.

Q#8)	An increase in temperature will cause a gas to:

- Concentrate;

- Expand;

- Not change;

- Doesn’t matter.

Q#9)	Heavier gases (Specific Gravity great than 1) will:

- Be easy to diffuse;

- Be easy to disperse;

- Not diffuse rapidly;

- Be easy to remove.

Q#10)	Prolonged or successive exposure of the team’s self-contained breathing apparatus to petroleum-based fumes can cause the unit:

- No effect;

- To explode;

- Not to provide adequate protection;

- The face mask to fog up.

Q#11)	When bump testing the MX6, the sensor being tested must reach a gas reading of 50% or greater within:

- 15 seconds;

- 30 seconds;

- 45 seconds;

- 60 seconds.

Q#12)	When calibrating the MX6 the user has ___ minutes to apply gas before the calibration times out.

- 1;

- 3;

- 5;

- 10.

Q#13)	When the battery icon flashes on the display and it has an audible battery low alarm, the MX6 battery life remaining is:

- Less than 2 hours;

- Less than 1.5 hours;

- Less than 1 hour;

- Less than 30 minutes.

Q#14)	On the MX6 the Low-level Visual alarm is:

- No change in LEDs;

- LEDs are pulsed with a long delay;

- LEDs are pulsed with a short delay;

- None of the above.

Q#15)	To change the clock setting/ time on the MX6, the user must access it by the following menu options:

- Data; Users/Sites; Set Current Site.

- View; Configure; Display: Time

- View; Display; Numeric

- View; Configure; Admin; Clock.

Q#16)	To measure the MX6 sensor’s accuracy the user must do the following procedure:

- Zero;

- Bump test;

- Configuration;

- Calibration

Q#17)	On a MX6, the NO2 (Nitrogen Dioxide) sensor is of the following type:

- Infrared;

- Catalytic;

- Electrochemical;

- Photoionization.

Q#18)	On a MX6 the clearing of the peak readings should be done:

- After a bump test;

- Before a change of location;

- After an alarm is addressed and cleared;

- All of the above.

Q#19)	On the MX6, once initiated, a gas-related alarm will:

- Remain on for 10 seconds;

- Remain on while the alarm condition is present;

- Remain on until the instrument is reset;

- Turn off once the alarm is acknowledged.

Q#20)	For the MX6, which of the following should only be done in nonhazardous locations?

- Service the unit;

- Charge the battery;

- Change the pump filter;

- All of the above.

Q#21)	In the BG4, the regeneration cartridge is to:

- Supply oxygen at a constant rate;

- Absorb carbon monoxide;

- Cool the breathing air.

- Absorb carbon dioxide.

Q#22)	On the BG4 the high pressure carbon O2 cylinder has a lifespan of _____.

- 6 Months;

- 5 years;

- 10 years;

- 15 years.

Q#23)	On the BG4, the high pressure steel O2 cylinder is hydrotested at intervals of_____.

- After each use;

- 1 year;

- 5 years

- 10 years.

Q#24)	For the BG4 under moderate service conditions for temperatures up to 104 Degree F the period of use is up to _____ with ice in the cooler.

- 15 minutes;

- 1 hour;

- 2 hours;

- 4 hours.

Q#25)	Even if the recommended period of use is exceeded, the BG4 will operate correctly. Only the _____ of the inhaled air will ______.

- %O2; increase.

- %O2; decrease.

- Temperature; increase.

- Temperature; decrease.

Q#26)	For storage of the BG4 all rubber parts must be particularly protected from direct exposure to:

- Extreme high temperatures;

- Extreme low temperatures;

- Radiation

- All of the above.

Q#27)	While trouble shooting the BG4 if the test value for the minimum valve is incorrect you should do the following EXCEPT:

- Replace the pressure transducer;

- Repair the tilt valve;

- Open the cylinder valve;

- Replace springs.

Q#28)	On the BG4 when using the leak test with positive pressure to check the drain valve, the pressure must not change by more than 1mbar during:

- 15 seconds

- 30 seconds

- 1 minute

- 2 minutes

Q#29)	Testing of the BG4 inhalation and exhalation valve should be done:

- After use;

- Half-yearly;

- Yearly;

- Every 3 years.

Q#30)	To prevent ambient air from enter the system the BG4 breathing circuit works under:

- High pressure;

- Low pressure;

- Negative pressure;

- Positive pressure.

2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test Answers – Team Tech (BG4) Competition

A#1) 	B) Module 3; Page 4; Paragraph 2.

A#2) 	C) Module 3; Page 22; Paragraph 4.

A#3) 	C) Module 3; Page 5; Paragraph 6.

A#4) 	B) Module 3; Page 9; Paragraph 4.

A#5) 	D) Module 3; Page 23; Paragraph 6-8.

A#6)	A) Module 2; Page 5; Paragraph 3.

A#7) 	B) Module 2; Page 6; Paragraph 1.

A#8) 	B) Module 2; Page 6; Paragraph 3.

A#9) 	C) Module 2; Page 7; Paragraph 2.

A#10) 	C) Module 2; Page 10; Paragraph 1.

A#11) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.38; Paragraph #4.

A#12) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.37; Paragraph #3.

A#13) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.35; NOTE

A#14) 	B) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.6; Visual Alarm.

A#15) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.10.

A#16) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.11 Calibration.

A#17) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.47; NO2 Sensor info.

A#18) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.12; 1st paragraph

A#19) 	B) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.19; 2nd paragraph.

A#20) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.4; 7th Warning.

A#21) 	D) PSS BG4 Service Manual Rev O Page# 3; Paragraph 1.

A#22) 	D) PSS BG4 Service Manual Rev O Page# 45.

A#23) 	C) PSS BG4 Service Manual Rev O Page# 45.

A#24) 	D) PSS BG4 Service Manual Rev O Page# 42 Technical Data Maximum Temperature ranges.

A#25) 	C) PSS BG4 Service Manual Rev O Page# 42 Technical Data Maximum Temperature ranges.

A#26) 	C) PSS BG4 Service Manual Rev O Page# 38 Storage.

A#27) 	A) PSS BG4 Service Manual Rev O Page# 35 Trouble Shooting #7

A#28) 	C) PSS BG4 Service Manual Rev O Page# 26 –Leak test with Positive pressure #3.

A#29) 	A) PSS BG4 Service Manual Rev O Page# 38

A#30) 	D) PSS BG4 Service Manual Rev O Page# 3; Paragraph 5.