2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test – Team Trainer Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

Q#1)	A mine ventilation system is designed to:

- Supply Oxygen;

- Bring in fresh air;

- Remove harmful gases;

- All of the above.

Q#2)	The rescue team stationed at the fresh air base is considered the:

- Standby Team

- Backup Team

- Reserveg Team

- Working Team

Q#3)	Temporary bulkheads built in a passageway should be placed at least 4 to 6 feet into the passageway in order that:

- It will not be affected by fire;

- Provide a rest area for the team;

- Sufficient space is available to construct a permanent bulkhead;

- It will not be affected by a fire.

Q#4)	The base of operations from which rescue and recovery work advances into irrespirable atmospheres is called the ______.

- Triage Area;

- Command Center;

- Fresh air base;

- Benching area.

Q#5)	The three sides of the fire triangle are fuel, oxygen and______.

- Chemical reaction;

- Heat;

- Explosive gases;

- Current.

Q#6)	Preconditions for unsealing a fire area include:

- Area behind seal has had sufficient cooling time;

- Oxygen content behind seal low enough to make a explosion impossible;

- Carbon monoxide not present behind seal;

- All of the above.

Q#7)	The best definition of the term “stressor” is anything that:

- Causes significant behavioral changes;

- Puts pressure on the body;

- Consumes the attention of the person experiencing stress;

- Causes wear and tear on the body’s resources.

Q#8)	The recovery position is also known as the ___ position.

- Lateral;

- Stroke;

- Lateral recumbent

- Superior.

Q#9)	What can be assessed by watching and feeling the chest and abdomen move during breathing?

- Skin signs;

- Pulse rate;

- Respiratory rate;

- Blood pressure.

Q#10)	A patient who presents with normal vital signs and show no indications of a life-threatening problem may be described as:

- Routine;

- Unstable;

- Stable;

- Normal.

Q#11)	Which one of the following is NOT a typical characteristic of arterial bleeding?

- The color of the blood is bright red;

- Blood loss is often profuse in a short period of time;

- Blood flows steadily from the wound;

- Blood spurts from the wound.

Q#12)	Why does a patient’s pulse rate increase as shock develops?

- To create more blood to compensate for fluid loss;

- To force oxygenated blood out of the patient’s body core;

- To maintain adequate perfusion;

- To counteract the high blood pressure.

Q#13)	Underground mines that have not been approved for alternative mine rescue capability must establish at least ____ mine rescue teams which are available at all times when miners are underground,

- One;

- Two;

- Three

- Four.

Q#14)	How many extra fully charged oxygen bottles are required for every six apparatus?

- One;

- Two;

- Three;

- Four.

Q#15)	MSHA Form 5000-3 must be kept on file for a period of:

- For the full time the member is on the team;

- Two years;

- One year;

- None of the above.

Q#16)	A record of correction action (breathing apparatus) shall be maintained at the mine rescue station for a period of ______ year(s)?

- One;

- Two;

- Three;

- Four.

Q#17)	Mine rescue team communication systems must be at least _________ feet in length.

- 2,000;

- 1,000;

- 1,300;

- 1,800.

Q#18)	A mine rescue team member will be ineligible to serve on a team if more than ______ of training is missed during one year.

- 24 Hours;

- 16 Hours;

- 8 Hours;

- One Day.

Q#19)	Any team whose member(s) intentionally disturb or destroy any component on a competition field will immediately be assessed a _____ point discount.

- 10

- 50

- 100

- 200

Q#20)	The Number 1 judge must:

- Have current  Mine Rescue Judges training;

- Have been briefed on the particular problem;

- Be a MSHA employee.

- All of the above.

Q#21)	When using the standard horn blasts or other audible signals between team members, 3 blasts on the horn means:

- Distress;

- Advance;

- Stop;

- Retreat.

Q#22)	The procedure for team checks shall be followed at not more than_____ minute intervals.

- Thirty;

- Ten;

- Twenty;

- Twenty five.

Q#23)	During the first aid competition, not checking the accident scene to ensure personal safety will receive ______ discounts per infraction.

- 20;

- 10;

- 5;

- 0 (none).

Q#24)	An excavation in the shaft or mine made below the mining level to collect water is called a:

- Stopping;

- Undercast;

- Sump;

- Winze.

Q#25)	All sensors on a MX6:

- Will last indefinitely;

- Should be replaced after every use;

- Do not need calibration once in instrument;

- Gradually degrade over time.

Q#26)	MSHA’s approval/certification for the use of the MX6 is under CFR30, _____.

- Part 62;

- Part 58;

- Part 46;

- Part 22.

Q#27)	The MX6 High-level audio gas alarm is a:

- Low frequency beeps with a long delay;

- Continuous claxon;

- High frequency with short delays;

- Vibration only.

Q#28)	As part of the Technician team apparatus checks, ___ discounts will be assessed for each deficiency not found.

- 1

- 5

- 10

- 15

Q#29)	As part of the Technician team apparatus checks, ___ discounts will be assessed for each monthly check not performed.

- 15

- 10

- 5

- 3

Q#30)	To work the apparatus problem, the technician team will be provided by the judge:

- Testing equipment;

- Tools;

- Apparatus;

- All of the above.

2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test Answers – Team Trainer Competition

A#1) 	D) Module 2; Page 3; Paragraph 1.

A#2) 	B) Module 1; Page 14; Paragraph 1.

A#3) 	C) Module 3; Page 22; Paragraph 1.

A#4) 	C) Module 4; Page 6; Paragraph 7

A#5) 	B) Module 5; Page 4; Paragraph 4

A#6) 	D) Module 7; Page 17; Visual 2

A#7) 	D) Brady 10th Ed., Chapter 3, Page 46

A#8) 	C) Brady 10th Ed., Chapter 4, Page 57

A#9) 	C) Brady 10th Ed., Chapter 12, Page 224

A#10) 	C) Brady 10th Ed., Chapter 13, Page 243

A#11) 	C) Brady 10th Ed., Chapter 18, Page 358

A#12) 	C) Brady 10th Ed., Chapter 19, Page 395

A#13) 	B) Part 49.2(a)(1)

A#14) 	B) Part 49.6(a)(3)

A#15) 	B) Part 49.7(c).

A#16) 	A) Part 49.6(b)(3)

A#17) 	B) Part 49.8(a)(8)(ii)

A#18) 	C) Part 49.8(c)

A#19) 	C) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 5; Rule #12

A#20) 	D) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 19; Paragraph 4

A#21) 	D) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 25; Paragraph 2

A#22) 	C) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 27; Paragraph 5

A#23) 	C) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 101; A-1

A#24) 	C) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 110; Sump definition

A#25) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.11; Last Paragraph

A#26) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.2; MSHA.

A#27) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.6; Audio Indicator.

A#28) 	D) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 72; Rule #8.

A#29) 	C) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 73; Rule #10.

A#30) 	D) 2019 – 2020 Metal and Nonmetal Mine Rescue Contest Rules Page 72; Rule #2.