2019 Southwestern Regional Mine Rescue Contest

Ruidoso, NM

Written Test – Field Competition

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

1)	The team uses gas detectors to test the mine air:

- Every 10 feet;

- Whenever they feel like it;

- Repeatedly as they advance.

- Just at the fresh air base.

Q#2)	If you know the specific gravity of a gas, the team will know:

- Where it will be located in the mine;

- Where it should be tested for;

- Neither A or B;

- Both A & B.

Q#3)	Physical properties of a gas can help identify it.  A rotten egg odor could indicate:

- Carbon monoxide;

- Hydrogen sulfide;

- Nitrogen oxides;

- Oxygen.

Q#4)	In Normal Air the oxygen concentration is around:

- 79%

- 31%

- 21%

- 16%

Q#5)	A 15 percent (%) concentration of Oxygen will cause:

- Death;

- Dizziness and headaches;

- No effect;

- Loss of consciousness.

Q#6)	The first symptoms of carbon monoxide poisoning is:

- Slight tightening across your chest; and possibly a headache

- Sore throat; and possibly a headache

- Slight tightening across your forehead; and possibly a headache

- Dizziness; and possibly a headache

Q#7)	To test for Carbon monoxide the detectors should be held:

- Above the head;

- At eye level;

- At chest level;

- At your feet.

Q#8)	Malfunctioning electrical equipment producing arcs and sparks could cause:

- Elevated readings of Oxygen;

- Elevated readings of Oxides of Nitrogen;

- Elevated readings of Carbon Monoxide;

- Elevated readings of Hydrogen Sulfide.

Q#9)	Hydrogen sulfide concentrations as low as ___ can lead to death.

- 0.11 percent;

- 0.07 percent;

- 0.02 percent;

- 0.005 percent.

Q#10)	Smoke can be a problem during a mine rescue event due to it possibly being:

- An asphyxiant;

- Explosive

- Limits visibility;

- All of the above.

Q#11)	A system of assigning priorities of medical treatment to injured persons is known as:

- Chain of command

- Command Center

- Rotation Schedule

- Triage

Q#12)	During an event the team is under the direct supervision of the:

- Mine Clerk;

- Outside Supervisor;

- Team Captain;

- Chief Engineer.

Q#13)	Depending on the nature of the emergency, arrangements for the following medical services should be made:

- Temporary hospital;

- Temporary morgue;

- Standby ambulances;

- Both A & C

Q#14)	Existing ventilation can be altered by the team when:

- The team decides;

- The team captain decides;

- Directed by the command center;

- They encounter smoke.

Q#15)	What two measurements are need to determine the quantity of the airflow:

- Velocity and direction;

- Velocity and volume of airway;

- Area of airway and direction;

- Area of airway and velocity.

Q#16)	If a body is in cold water it will remain in almost perfect condition for _______

- 1 to 2 days

- 2 to 3 days

- 3 to 4 days

- up to a week

Q#17)	Reasons for a Team Check include;

- To make sure each team member is fit and ready to continue

- To make sure each team member’s apparatus is functioning properly

- To give the team a chance to rest

- All of the above

Q#18)	To determine the safest route for entering the mine, the mine openings should be examined:

- As encountered underground by the team;

- Before anyone goes underground;

- After the first team has made entry;

- All of the above.

Q#19)	Barefaced exploration should be conducted only when:

- The ventilation system is operating properly

- Frequent gas tests indicate there is sufficient oxygen and no buildup of dangerous gases;

- A backup team with apparatus is stationed outside the area.

- All of the above

Q#20)	Spatial disorientation can occur when traveling through:

- Bad ground;

- Heavy smoke;

- Water;

- Low roof.

Q#21)	After arriving on the surface team debriefings are held to:

- Inform family members of developments;

- Inform debriefing official(s) of what you did, saw, and found;

- Inform news reporters of developments;

- All of the above.

Q#22)	Method of firefighting where the fire area is sealed or filled with material is considered:

- Direct;

- Indirect;

- Neither of the above;

- Both of the above.

Q#23)	Class C fires involve:

- Combustible metals;

- Combustible liquids;

- Electric equipment;

- Combustible materials.

Q#24)	To best fight a fire using a dry chemical extinguisher you should direct the stream of dry chemical ________________ flame:

- Directly at the

- About 6 inches ahead of the

- About 12 inches ahead of the

- Directly at the base of the

Q#25)	A first priority condition to be treated when several survivors suffering from trauma have been located is:

- Multiple fractures;

- Mild hysteria;

- Chest injuries;

- Moderate Shock.

Q#26)	During an emergency a refuge chamber is where

- The team  preps to go under air.

- The fresh air base is located;

- Miners go if unable to reach the surface;

- The command center is located.

Q#27)	To extricate a body is to:

- Disentangle it.

- Identify it;

- Map it;

- Report it.

Q#28)	Once an airlock is constructed and after entering the barricade the opening should be:

- Guarded to prevent miners from exiting;

- Left open to dilute the air;

- Left open to allow easier access;

- Covered immediately.

Q#29)	The main task of a mine rescue team during recovery operations is to:

- Account for all missing miners

- Bring all survivors to surface

- Reestablish ventilation

- All of the above

Q#30)	During progressive ventilation as the work continues oxygen and gas levels _____.

- Can be ignored;

- Must be carefully monitored;

- Doesn’t matter;

- A & C.

2019 Southwestern Regional Mine Rescue Contest

Ruidoso, NM

Written Test Answers – Field Competition

A#1) 	C) Module 2; Page 4; Paragraph 2.

A#2) 	D) Module 2; Page 6; Paragraph 6.

A#3) 	B) Module 2; Page 8; Paragraph 2.

A#4) 	C) Module 2; Page 12; Paragraph 2.

A#5) 	B) Module 2; Page 14; Paragraph 1.

A#6) 	C) Module 2; Page 16; Paragraph 8-Health Hazards.

A#7) 	C) Module 2; Page 17; Paragraph 2-Where Found.

A#8) 	B) Module 2; Page 18; Paragraph 8-Meaning of Findings.

A#9) 	B) Module 2; Page 19; Paragraph 12.

A#10) 	D) Module 2; Page 26; Paragraph 2, 3, 5.

A#11) 	D) Module 1; Page 14; Paragraph 9.

A#12) 	C) Module 1; Page 6; Paragraph 4.

A#13) 	D) Module 1; Page 5; Paragraph 1.

A#14) 	C) Module 3; Page 3; Paragraph 4.

A#15) 	D) Module 3; Page 19; Paragraph 6.

A#16) 	B) Module 6; Page 10

A#17) 	D) Module 4; Page 20

A#18) 	B) Module 4; Page 5; Paragraph 5.

A#19) 	D) Module 4; Page 6; Paragraph 2.

A#20) 	B) Module 4; Page 25; Paragraph 4

A#21) 	B) Module 4; Page 32; Paragraph 7

A#22) 	B) Module 5; Page 17; Paragraph 1

A#23) 	C) Module 5; Page 5; Paragraph 6

A#24) 	B) Module 5; Page 7; Paragraph 3

A#25) 	C) Module 6; Page 5; Paragraph 5

A#26) 	C) Module 6; Page 14; Paragraph 6

A#27) 	A) Module 6; Page 14; Paragraph 3

A#28) 	D) Module 6; Page 5; Paragraph 2

A#29) 	C) Module 7; Page 4; Paragraph 5

A#30) 	B) Module 7; Page 8; Paragraph 1