2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test – Team Tech Competition (Bio 240 S)

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

Q#1)	A fan that pulls or sucks air out of a mine is called a:

- Blower fan;

- Exhaust fan;

- Booster fan;

- Auxiliary fan.

Q#2)	In mines with a possible explosive atmosphere the team should have with them:

- Auxiliary fans;

- Mechanic’s tools;

- Non-sparking tools;

- Explosives.

Q#3)	When fans are used to create the pressure differential to needed for ventilating a mine it is considered:

- Natural ventilation;

- Ventilation plan;

- Mechanical ventilation;

- Auxiliary fan system.

Q#4)	Temporary bulkheads can be built from:

- Canvas brattice;

- Wood or metal;

- Parachute stopping;

- All of the above.

Q#5)	Air locks are used by mine rescue teams:

- When opening a door or knocking out a bulkhead behind which conditions are not definitely known;

- Before opening a barricade in bad air behind which trapped miners may be located;

- To establish a fresh air base;

- All of the above.

Q#6)	An increase in temperature causes a gas to:

- Expand;

- Contract;

- Liquefy

- Increase in specific gravity.

Q#7)	If the barometric pressure is high, concentrations of explosive gases can:

- Go away;

- Build up;

- Expand;

- Disburse.

Q#8)	An increase in temperature will cause a gas to:

- Concentrate;

- Expand;

- Not change;

- Doesn’t matter.

Q#9)	Heavier gases (Specific Gravity great than 1) will:

- Be easy to diffuse;

- Be easy to disperse;

- Not diffuse rapidly;

- Be easy to remove.

Q#10)	Prolonged or successive exposure of the team’s self-contained breathing apparatus to petroleum-based fumes can cause the unit:

- No effect;

- To explode;

- Not to provide adequate protection;

- The face mask to fog up.

Q#11)	When bump testing the MX6, the sensor being tested must reach a gas reading of 50% or greater within:

- 15 seconds;

- 30 seconds;

- 45 seconds;

- 60 seconds.

Q#12)	When calibrating the MX6 the user has ___ minutes to apply gas before the calibration times out.

- 1;

- 3;

- 5;

- 10.

Q#13)	When the battery icon flashes on the display and it has an audible battery low alarm, the MX6 battery life remaining is:

- Less than 2 hours;

- Less than 1.5 hours;

- Less than 1 hour;

- Less than 30 minutes.

Q#14)	On the MX6 the Low-level Visual alarm is:

- No change in LEDs;

- LEDs are pulsed with a long delay;

- LEDs are pulsed with a short delay;

- None of the above.

Q#15)	To change the clock setting/ time on the MX6, the user must access it by the following menu options:

- Data; Users/Sites; Set Current Site.

- View; Configure; Display: Time

- View; Display; Numeric

- View; Configure; Admin; Clock.

Q#16)	To measure the MX6 sensor’s accuracy the user must do the following procedure:

- Zero;

- Bump test;

- Configuration;

- Calibration

Q#17)	On a MX6, the NO2 (Nitrogen Dioxide) sensor is of the following type:

- Infrared;

- Catalytic;

- Electrochemical;

- Photoionization.

Q#18)	On a MX6 the clearing of the peak readings should be done:

- After a bump test;

- Before a change of location;

- After an alarm is addressed and cleared;

- All of the above.

Q#19)	On the MX6, once initiated, a gas-related alarm will:

- Remain on for 10 seconds;

- Remain on while the alarm condition is present;

- Remain on until the instrument is reset;

- Turn off once the alarm is acknowledged.

Q#20)	For the MX6, which of the following should only be done in nonhazardous locations?

- Service the unit;

- Charge the battery;

- Change the pump filter;

- All of the above.

Q#21)	When handling the Bio 240S Oxygen cylinder do not allow ______ to come in contact with it to prevent a possible ignition.

- Grease;

- Combustible materials;

- Oil;

- All of the above.

Q#22)	Of the 3 sub-systems of the Bio 240S the Breathing loop:

- Delivers reduced pressure oxygen;

- Reduces the pressure of on-board oxygen to acceptable levels;

- Consist of all components in direct contact with breathing atmosphere;

- None of the above.

Q#23)	For the Bio 240 S the High pressure plumbing consists of:

- Coolant Canister;

- Bypass Valve;

- Breathing Chamber;

- Oxygen cylinder.

Q#24)	When handling the soda lime for the Bio 240 S:

- No PPE is required;

- Rubber gloves should be worn;

- Safety glasses should be worn;

- Both B & C.

Q#25)	Hydrostatic testing of the oxygen cylinder should be done every ____ years.

- 8

- 5

- 3

- 1

Q#26)	Failure to remove the test key from the Bio 240 S will result in:

- Possible damage to the breathing chamber;

- Improper unit function;

- Excessively high breathing resistence;

- All of the above.

Q#27)	The breathing chamber O-rings on the Bio 240 S should be inspected and re-lubricated:

- Every usage;

- Every 5 uses;

- Every 10 uses;

- Every 50 uses.

Q#28)	To perform a negative pressure check on the Bio 240 S facepiece the ______port/s should be blocked.

- Red;

- Green;

- Both;

- Neither.

Q#29)	If no _____ is heard when the oxygen cylinder is opened the alarm valve may not have armed or may not function correctly.

- Air leaking noise;

- Claxon;

- Chirp;

- Bell.

Q#30)	Do not use the Bio 240 S if:

- The turn-around maintenance tag is missing;

- The date on the turn-around maintenance tag is greater than one year prior to use;

- Neither A or B;

- Both A & B.

2019 Southern Regional Mine Rescue Contest

New Iberia, LA

Written Test – Team Tech Competition (Bio 240 S)

A#1) 	B) Module 3; Page 4; Paragraph 2.

A#2) 	C) Module 3; Page 22; Paragraph 4.

A#3) 	C) Module 3; Page 5; Paragraph 6.

A#4) 	B) Module 3; Page 9; Paragraph 4.

A#5) 	D) Module 3; Page 23; Paragraph 6-8.

A#6)	A) Module 2; Page 5; Paragraph 3.

A#7) 	B) Module 2; Page 6; Paragraph 1.

A#8) 	B) Module 2; Page 6; Paragraph 3.

A#9) 	C) Module 2; Page 7; Paragraph 2.

A#10) 	C) Module 2; Page 10; Paragraph 1.

A#11) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.38; Paragraph #4.

A#12) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.37; Paragraph #3.

A#13) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.35; NOTE

A#14) 	B) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.6; Visual Alarm.

A#15) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.10.

A#16) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.11 Calibration.

A#17) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.47; NO2 Sensor info.

A#18) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.12; 1st paragraph

A#19) 	B) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.19; 2nd paragraph.

A#20) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.4; 7th Warning.

A#21) 	D) Bio 240S Benchman Instruction Manual Rev L; Pg. 5 OAH paragraph.

A#22) 	C) Bio 240S Benchman Instruction Manual Rev L; Pg. 7 3rd paragraph.

A#23) 	D) Bio 240S Benchman Instruction Manual Rev L; Pg. 10 High Pressure Plumbing Section

A#24) 	D Bio 240S Benchman Instruction Manual Rev L; Pg. 13 1st Caution

A#25) 	B) Bio 240S Benchman Instruction Manual Rev L; Pg. 14 Section 2e.

A#26) 	D) Bio 240S Benchman Instruction Manual Rev L; Pg. 20 Section 8 –Warning.

A#27) 	B) Bio 240S Benchman Instruction Manual Rev L; Pg. 23 Breathing Chamber O-rings.

A#28) 	B) Bio 240S User Instruction Manual Rev F; Pg. 7 Item 10.

A#29) 	C) Bio 240S User Instruction Manual Rev F; Pg. 8 Warning.

A#30) 	D) Bio 240S User Instruction Manual Rev F; Pg. 6; 1st Warning.