2019 Southwestern Regional Mine Rescue Contest

Ruidoso, NM

Written Test – Team Tech Competition (BG4)

Name____________________________	Company___________________________

Team Name_______________________	Contest Position No.__________________

Team Member No._________________

Directions: Use answer sheet & fill in completely.

Q#1)	Existing ventilation can be altered by the team when:

- The team decides;

- The team captain decides;

- They encounter smoke;

- Directed by the command center.

Q#2)	What device is used to measure air movement?

- Voltmeter;

- Smoke tube;

- Gas tube;

- Gas detector.

Q#3)	A rescue team is usually needed to go into the mine to assess and reestablish ventilation after:

- A new fan installation;

- A new exhaust shaft is put in service;

- A fire or explosion has occurred;

- All of the above.

Q#4)	A plastic curtain that is hung across a passage way and opens to allow miners and equipment to pass through is considered a:

- Airlock

- Temporary bulkhead;

- Line brattice;

- Check curtain.

Q#5)	Air that is unfit for breathing is considered to be:

- Irreplaceable;

- Irregular;

- Irrespirable;

- Irrevocable.

Q#6)	A gas has:

- A definite volume, but changes shape;

- A definite shape and volume;

- Neither a definite shape or volume;

- None of the above.

Q#7)	The atmospheric pressure in a mine:

- Is constant;

- Doesn’t matter;

- Cannot be measured;

- Varies.

Q#8)	A decrease in temperature will cause a gas to:

- Not Change;

- Doesn’t matter

- Expand

- Contract.

Q#9)	Carbon monoxide can be detected by:

- Detector only;

- Smelling it;

- Seeing it;

- Tasting it.

Q#10)	For all mine rescue events, the team must know how to test for:

- Oxygen and carbon dioxide levels;

- Carbon monoxide and Nitrogen oxides levels;

- Carbon monoxide and Hydrogen sulfide levels;

- Oxygen and carbon monoxide levels.

Q#11)	For the BG4, ice is required:

- When the ambient temperature is below 32 Degrees F;

- Always;

- When the ambient temperature is above 32 Degrees F;

- When the ambient temperature is high.

Q#12)	On the BG4 there are 2 sealing relief valves – the Over pressure relief valve and the _____.

- Air trap vale;

- Moisture trap valve;

- High Pressure valve;

- Low pressure valve.

Q#13)	On the BG4, the high pressure steel O2 cylinder is full at _____psi.

- 1500

- 3000

- 3135

- 3300.

Q#14)	The high pressure o2 cylinder contains _____ liters of 99% O2.

- 400

- 300

- 200

- 100

Q#15)	For the BG4 under moderate service conditions for temperatures up to 105 to 140 Degree F the period of use is up to _____ with ice in the cooler.

- 15 minutes;

- 1 hour;

- 2 hours;

- 4 hours.

Q#16)	For the BG4 the temperature for drying must not exceed:

- 60 Degree F;

- 60 Degree C;

- 150 Degree F;

- 150 Degree C.

Q#17)	If while trouble shooting the BG4 the residual pressure first warning value is incorrect potential remedies include:

- Replace battery;

- Replace switch box;

- Replace Sentinel pressure transducer;

- Any of the above.

Q#18)	If when doing the BG4 High-pressure leak test the reading is lower than 2600psi / 180 bar:

- Charge the oxygen cylinder;

- Change the sentinel battery;

- Replace the breathing bag;

- Replace the CO2 absorber.

Q#19)	Exceptionally, if the breathing circuit is opened for more than 5 minutes, the CO2 absorber apertures should be sealed with ______ PE plug(s) to prevent escape of gas.

- 4

- 3

- 2

- 1

Q#20)	The BG4 speech diaphragm must be replaced:

- After use of unit;

- Yearly;

- Shows sign of damage;

- Every 4 years.

Q#21)	When bump testing the MX6, the sensor being tested within 60 seconds must reach a gas reading of _____ or greater.

- 10%

- 25%

- 50%

- 75%

Q#22)	If there is more than one sensor that failed the MX6 bump test, they are calibrated in what order?

- Any depending on the gas used;

- Top row left to right, bottom row left to right;

- Top row left to right, bottom row right to left;

- Bottom row left to right, top row left to right.

Q#23)	During calibration of the MX6 the gas should be applied at a flow rate of ___ lpm.

- 1.5;

- 1.0;

- 0.5;

- None of the above.

Q#24)	The MX6 must be calibrated according to the procedure specified in the:

- CFR 3049 Part 49;

- Mine rescue Rules book;

- Mine rescue Module 2 – Mine gases;

- Instruction manual.

Q#25)	To start the MX6 Bump Test option, the user must access it by following the menu options:

- Data; View Data; Event Log.

- Sensor; Calibration.

- Sensor; Bump Test.

- View; Configure.

Q#26)	Zero air must be applied to zero a ____ sensor on a MX6.

- O2;

- NO2;

- CO2;

- CO.

Q#27)	To view MX6 sensor’s most recent calibration date and its span trends begin with the following menu options.

- Data; View Data.

- Sensor; Location.

- Sensor; Calibration.

- Sensor; Sensors.

Q#28)	All sensors on a MX6:

- Will last indefinitely;

- Should be replaced after every use;

- Do not need calibration once in instrument;

- Gradually degrade over time.

Q#29)	The MX6 should be calibrated:

- Before first use and monthly thereafter;

- After the installation of new sensors;

- After the unit falls;

- Any of the above.

Q#30)	The MX6 High-level audio gas alarm is a:

- Low frequency beeps with a long delay;

- Continuous claxon;

- High frequency with short delays;

- Vibration only.

2019 Southwestern Regional Mine Rescue Contest

Ruidoso, NM

Written Test Answers – Team Tech (BG4) Competition

A#1) 	D) Module 3; Page 3; Paragraph 4.

A#2) 	B) Module 3; Page 16; Paragraph 3.

A#3) 	C) Module 3; Page 3; Paragraph 3.

A#4) 	D) Module 3; Page 9; Paragraph 9.

A#5) 	C) Module 3; Page 54; Paragraph 2.

A#6)	C)   Module 2; Page 5; Paragraph 2.

A#7) 	D) Module 2; Page 5; Paragraph 7.

A#8) 	D) Module 2; Page 6; Paragraph 3.

A#9) 	A) Module 2; Page 8; Paragraph 3.

A#10) 	D) Module 2; Page 12; Paragraph 7.

A#11) 	C) PSS BG4 Service Manual Rev O Page# 3; Paragraph 5.

A#12) 	B) PSS BG4 Service Manual Rev O Page# 50.

A#13) 	C) PSS BG4 Service Manual Rev O Page# 45.

A#14) 	A) PSS BG4 Service Manual Rev O Page# 45.

A#15) 	B) PSS BG4 Service Manual Rev O Page# 42 Technical Data Maximum Temperature ranges.

A#16) 	B) PSS BG4 Service Manual Rev O Page# 38 Drying

A#17) 	D) PSS BG4 Service Manual Rev O Page# 35 Trouble Shooting #10

A#18) 	A) PSS BG4 Service Manual Rev O Page# 28.

A#19) 	B) PSS BG4 Service Manual Rev O Page# 22 –3rd paragraph under Inserted CO2 absorber.

A#20) 	C) PSS BG4 Service Manual Rev O Page# 10; Paragraph 3.

A#21) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.38; Paragraph #4.

A#22) 	B) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.38; Paragraph #7.

A#23) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.37; Paragraph #3.

A#24) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.5; 5th CAUTION.

A#25) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.9.

A#26) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.36; 4th Paragraph.

A#27) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.24 &25.

A#28) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.11; Last Paragraph

A#29) 	D) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.12; 5th paragraph.

A#30) 	C) MX6 iBird Op’s Guide (ED 17; Aug 10, 2018) Pg.6; Audio Indicator.