Use Indelible Pencil or Ink	PRESHIFT-CERTIFIED EXAMINER’S REPORT	Report Shall be Signed When Made

| Date of Examination: |  |  | Time From:: |  | AM PM | To: |  | AM PM |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Section/Area: |  |  | Reported Outside? | Yes |  | No |  | Time: |  | AM PM |
| Reported By: |  |  | Received By: |  | (INITIAL) |

Pre-Shift required within 3 hours prior to any 8-hour interval

| Location | Hazardous Condition | Action Taken | CH4 |
| --- | --- | --- | --- |
| No. 1 entry outby 1st xcut | Unsafe roof | Danger off both sides |  |
| No. 1 entry face area | None observed |  | 0.0% |
| 3rd xcut between # 2 and # 3 | Fire hose equip- not enough hose | Danger off |  |
| 3rd xcut between # 2 and # 3 | Fire hose equip- wrong location | Move box to fire fighting outlet |  |
| 2nd xcut between # 2 and # 3 | Energized 480V duster in return | Move check curtain to other side of xcut |  |
| No. 2 entry face area | None observed |  | 0.0% |
| 2nd xcut between # 3 and # 4 | Check curtain down | Hung check curtain |  |
| No. 3 entry face area | None observed |  | 0.0% |
| 2nd xcut between # 4 and # 5 | No check curtain installed | Hung check curtain |  |
| No. 4 entry face area | None observed |  | 0.0% |
| No. 5 entry face area | None observed |  | 0.0% |
| * Roadways | * Travelways | * Track Haulageways/Entries | * Working Section | * Areas Equipment Installed or Removed | * Approaches to Worked out Areas |
| * Intake Seals | * +20Ft. Entries on Intake | * Unattended Diesel | * Intake High Spots | * Electrical Installations/Trolley Wires* | * Other Work/Travel Areas |

# Air Measurements

| Location | CFM | Location | CFM |
| --- | --- | --- | --- |
| LOCC | 19200 |  |  |

| Remarks: |  |
| --- | --- |

| Signed by Pre Certified Examiner |  | Date |  | Certification Number |
| --- | --- | --- | --- | --- |
| Countersigned by Mine Foreman |  | Date |  | Certification Number |