Confined Space Quiz

- A confined space is designed for human occupancy.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Which of the following are considered potential hazards in a confined space?

|  | a. An oxygen level of 18 percent. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Wearing an air supplying respirator in an oxygen deficient space. |  |  |  |
|  | c. Walls that slope inward. |  |  |  |
|  | d. Both A and C. |  |  |  |

- The atmosphere of a confined space is not acceptable if the concentration of a flammable gas, vapor or mist present is:

|  | a. Not detected in tests. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. So thick you can’t see five yards in front of you. |  |  |  |
|  | c. Greater than 10 percent of its lower flammable limit. |  |  |  |

- Which of the following are examples of safety hazards in permit required confined space?

|  | a. Falls. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Machinery that has not been locked out and tagged. |  |  |  |
|  | c. Engulfing materials such as saw dust. |  |  |  |
|  | d. All of the above. |  |  |  |

- The following information is included on an entry permit:  purpose of the entry, authorized entrants, hazards of the permit space, results of tests performed, name of the tester, and equipment required.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Placing your foot through the opening of a permit required confined space is considered an entry.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- If you need to isolate energy sources in a confined space (PRCS) before entry, that information will be on the permit system.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The entry permit authorizes entry to anyone who wishes to enter the permit required confined space.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Isolation of a permit required confined space is:

|  | a. Locking out and tagging all supply lines and sources of energy. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Blocking off the permit required confined space to all entrants not authorized. |  |  |  |
|  | c. All of the above. |  |  |  |

- The atmosphere of a confined space is unacceptable if the oxygen level is below 19.5 percent or above 23.5 percent.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- If the attendant detects a hazardous atmosphere during entry, workers must leave the space.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The attendant may leave his station outside a permit space during entry procedures as long as it is only for a few minutes.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Which of the following duties is the entry supervisor responsible for?

|  | a. Authorizing entry. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Determining if conditions are acceptable for an entry. |  |  |  |
|  | c. Terminating the entry if necessary. |  |  |  |
|  | d. All of the above. |  |  |  |

- When both the employer’s and contractor’s employees will perform work in or near a confined space, the employer and the contractor must coordinate entry operations.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Each member of an in-plant rescue team must receive training at least once every 12 months that involves simulated rescue operations in permit spaces.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- It is important to monitor the surrounding air outside a confined space to make sure it is not contaminated.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Several factors are commonly related to confined space injuries or deaths among emergency responders.  These include:

  - Lack of pre-incident planning and standard operating procedures.

  - Insufficient training on procedures for safe confined space rescues.

  - Lack of knowledge of the hazards of confined spaces.

  - Lack of air testing devices and rescue equipment

  - Any or all of the above.

# Signature: ______________________________________ Payroll #____________ Date _____________

Instructor _______________________________________