Electrical Hazards Quiz #1

Answers

- Suitable warning notices (tags) must be posted at power switches and signed by individuals doing the work.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Mobile equipment must not operate closer than ___________ feet to energized power lines rated 50kv or below.

|  | a. six |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. eight |  |  |  |
|  | c. ten |  |  |  |
|  | d. none of the above |  |  |  |

- How many keys can you have with your personal lockout padlock?

|  | a. one |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. two |  |  |  |
|  | c. three |  |  |  |
|  | d. doesn’t matter |  |  |  |

- Locking out equipment is required only if the procedure takes more than 10 minutes.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Simple steps to remember for locking out are …

  - proper planning

  - notifying all affected personnel

  - shutting down at operating controls

  - isolating all energy sources

  - locking & tagging each isolating device

  - dissipating all stored or residual energy

  - verifying isolation

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Inspection and cover plates on electrical equipment and junction boxes must be in place except when testing or making repairs.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The different types of energy besides electricity may include …

|  | a. chemical |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. hydraulic |  |  |  |
|  | c. mechanical |  |  |  |
|  | d. gravity |  |  |  |
|  | e. pneumatic |  |  |  |
|  | f. all of these |  |  |  |

- Lug terminals on an arc welder need to have insulated covers to prevent accidental contact by workers.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- All start switches must be returned to the “neutral” or “off” position after checking that all energy has been released.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- It is OK to pull on a power cord in order to remove the plug from the wall outlet.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

# Signature ___________________________________ PR# _____________ Date ___________________

Instructor ___________________________________