EXCAVATIONS QUIZ #1

- When using the thumb penetration test, if your thumb penetrates no further than the length of the thumb nail, the soil is probably –

|  | a. Type A |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Type B |  |  |  |
|  | c. Type C |  |  |  |
|  | d. Type D |  |  |  |

- All shoring should be installed from the top down and removed from the bottom up.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Temporary spoils must be placed no closer than _____ feet from the surface edge of the excavation.

|  | a. 1 |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. 2 |  |  |  |
|  | c. 3 |  |  |  |
|  | d. 4 |  |  |  |

- Boiling is evidenced by the upward water flow into the bottom of the excavation cut.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Soil from which water is freely seeping is –

|  | a. Type A |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Type B |  |  |  |
|  | c. Type C |  |  |  |
|  | d. Type D |  |  |  |

- Inspections are required to be conducted at, but not limited to, the following frequencies –

|  | a. Daily & before the start of each shift |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. After every rain storm |  |  |  |
|  | c. When there is an indication of change or movement in adjacent structures |  |  |  |
|  | d. When there is a change in size, location, or placement of spoil pile |  |  |  |
|  | e. All of the above |  |  |  |

- A trench shield should extent at least 12 inches above the surrounding area of the trench.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- A pocket penetrometer can be used to determine the unconfined compressive strength of saturated cohesive soils.  It has an error rate of –

|  | a. ± 10 – 20% |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. ± 20 – 30% |  |  |  |
|  | c. ± 20 – 40% |  |  |  |
|  | d. None of the above |  |  |  |

- There are two basic types of shoring which are –

|  | a. Timber & aluminum hydraulic |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Timber & steel mechanical |  |  |  |
|  | c. Gravational struts & wales |  |  |  |
|  | d. All of the above |  |  |  |

- Excavations and trenching soils are categorized into four types which are –

|  | a. Stable rock |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Type D |  |  |  |
|  | c. Type A |  |  |  |
|  | d. Cohesive soils |  |  |  |
|  | e. Type B |  |  |  |
|  | f. Type C |  |  |  |
|  | g. All but B and D |  |  |  |
|  | h. All but G |  |  |  |

- When trenches are at least 4 feet deep, a ladder or other egress means must be within _____ feet of anyone in the trench.

|  | a. 10 |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. 15 |  |  |  |
|  | c. 20 |  |  |  |
|  | d. 25 |  |  |  |
|  | e. 50 |  |  |  |

- The height/depth ratio for allowable slopes for Type C soil is 1½:1 or 340.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- When you mold a moist sample of soil into a ball and roll it into a thin thread (~ 1/8 inch in diameter by 2 inches long) and can hold it by its end without it breaking, it is considered cohesive soil.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The upward pressure created by the weight of adjoining soil is called bottom heaving or squeezing.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Underpinning involves stabilizing adjacent structures, foundations, etc. that may have an impact on the excavation or trench.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

# Signature ___________________________ Payroll # _____________ Date _______________________

Instructor ________________________________ Instructor ___________________________________